## Slide 1: AP Group Concept
Date: 2022-03-01
Authors:

## Slide 2: Abstract
This presentation is a discussion material for AP Group concept.

## Slide 3: Current Draft
Each EBCS traffic stream is identified by the Content ID that is shared by the APs using the same certificate.

## Slide 4: EBCS AP Group
“EBCS AP Group” is a new concept.
An EBCS AP Group consists of one or more EBCS AP(s).
EBCS APs in an EBCS AP Group may use different certificate.
Each EBCS AP Group is identified by the EBCS AP Group ID.
An EBCS AP Group ID is 2 octets (xx-yy).
An EBCS AP Group ID is NOT global unique and determined by the operator, same as SSID.
Each Content ID is unique in an EBCS AP Group
Addressing
  EBCS Info frame: 01-0F-AC-xx-yy-00 (xx: 00…7F, yy: 00…FF)
  EBCS Data frame: 01-0F-AC-xx-yy-zz (zz: 01…FF, Content ID)
Address space should be reserved for future use