## Slide 1
Sensing Security
Date: 2022-03-02
Authors:

## Slide 2: Introduction
It’s important to understand and agree on security requirements for a solution when defining a communications protocol.
Areas to consider/questions to answer:
  Do the parties involved in sensing need to know the identity of the peer they are talking to?
  Do we need to protect the communications? Is integrity protection enough? What communications need to be protected?
The next slide provides a table that describes security requirements for discussion.

## Slide 3: Security Requirements Table
Security Requirement | Discovery | Sensing with unassociated STAs | Sensing with associated STAs | Sensing Proxy
Authentication | None | Mutual/ Mandatory | Mutual/ Mandatory | Mutual / Mandatory (need to establish trust between sensing initiator and sensing responder through proxy)
Data confidentiality/ integrity/ replay detection (MAC) | None | Mandatory | Mandatory | Mandatory
Data confidentiality/ integrity/ replay detection (PHY) | None | Optional | Optional | Is it applicable in this case?
Privacy (prevent tracking of sensing STAs) | Prevent tracking for discovery operation (non-AP STA) | None | None | None
Availability (Prevent sensing devices from being captured or disabled, and prevent denial of service attacks) | None | Mandatory | Mandatory | Mandatory
Notes: doc.: IEEE 802.11-10/0503r4
May 2010
        Michael Montemurro, Research in Motion
Page 3

## Slide 4: Next Steps
Should we establish consensus on these requirements?
Should we include a table like this in the Spec Framework?