## Slide 1
Sensing Security
Date: 2022-03-30
Authors:

## Slide 2: Introduction
It’s important to understand and agree on security requirements for a solution when defining a communications protocol.
Areas to consider/questions to answer:
  Do the parties involved in sensing need to know the identity of the peer they are talking to?
  Do we need to protect the communications? Is integrity protection enough? What communications need to be protected?
The next slide provides a table that describes security requirements for discussion.

## Slide 3: Security Requirements Table
Security Requirement | Discovery | Sensing with unassociated STAs | Sensing with associated STAs | Sensing Proxy | STA Expected Behaviour
Authentication | None | Mutual/ Mandatory *some low capability devices may be excluded - Baseline authentication (e.g PASN) should be OK | Mutual/ Mandatory - Baseline authentication (e.g RSN) should be OK. | Mutual / Mandatory (need to establish trust between SBP, sensing initiator and sensing responder through proxy) | 
Data confidentiality/ integrity/ replay detection (MAC) | None | Mandatory RSN with PMF Need to address new replay counter for PASN | Mandatory - RSN with PMF | Mandatory | 
Data confidentiality/ integrity/ replay detection (PHY) (Need to understand the attack surface) | None | Optional - Need to understand the threat model. | Optional - Need to understand the threat model. | Is it applicable in this case? | 
Privacy (prevent tracking of sensing STAs) | Minimize what the STA has to expose with respect to sensing in the probe request. | Leverage features of 11bi Understand any unique use cases for sensing privacy | Leverage features of 11bi Understand any unique use cases for sensing privacy | None | 
Availability (Prevent sensing devices from being captured or disabled, and prevent denial of service attacks) | None | Mandatory - Understand use cases | Mandatory - Understand use cases | Mandatory | 
Notes: doc.: IEEE 802.11-10/0503r4
May 2010
        Michael Montemurro, Research in Motion
Page 3

## Slide 4: Next Steps
Should we establish consensus on these requirements?
Should we include a table like this in the Spec Framework?

## Slide 5: Discussion topics
Use cases – what can be solved, what cannot be solved.
Security can be different from privacy.
Are there unique privacy and security issues associated with sensing?