## Slide 1
Sensing Security
Date: 2022-04-12
Authors:

## Slide 2: Introduction
It’s important to understand and agree on security requirements for a solution when defining a communications protocol.
Areas to consider/questions to answer:
  Do the parties involved in sensing need to know the identity of the peer they are talking to?
  Do we need to protect the communications? Is integrity protection enough? What communications need to be protected?
The next slide provides a table that describes security requirements for discussion.

## Slide 3: Security Requirements Table
Security Requirement | Discovery | Sensing with unassociated STAs | Sensing with associated STAs | Sensing Proxy | STA Expected Behaviour
Authentication | None | Mutual/ Mandatory *some low capability devices may be excluded - Baseline authentication (e.g PASN) should be OK | Mutual/ Mandatory - Baseline authentication (e.g RSN) should be OK. | Mutual / Mandatory (need to establish trust between SBP, sensing initiator and sensing responder through proxy) | 
Data confidentiality/ integrity/ replay detection (MAC) | None | Mandatory RSN with PMF Need to address new replay counter for PASN | Mandatory - RSN with PMF | Mandatory | 
Data confidentiality/ integrity/ replay detection (PHY) (Need to understand the attack surface) | None | Optional Need to understand the threat model. Not to put effort on PHY security until we understand the problem | Optional Need to understand the threat model. Not to put effort on PHY security until we understand the problem. | Is it applicable in this case? | 
Privacy (prevent tracking of sensing STAs) | Minimize what the STA has to expose with respect to sensing in the probe request. | Leverage features of 11bi Understand any unique use cases for sensing privacy | Leverage features of 11bi Understand any unique use cases for sensing privacy | None | 
Availability (Prevent sensing devices from being captured or disabled, and prevent denial of service attacks) | None | Mandatory - Understand use cases | Mandatory - Understand use cases | Mandatory | 
Notes: doc.: IEEE 802.11-10/0503r4
May 2010
        Michael Montemurro, Research in Motion
Page 3

## Slide 4: Sensing Proxy Discussion
Proxy Initiator has a Security Association with the AP
  Initiator can decide whether it needs to trust the responder. Responder is trustworthy to Proxy Initiator.
Responder has a Security Association with the AP
AP can act as trusted third party
Responders should authorize proxy sensing capability
  Implies that the responder should inform the trusted AP that would allow sensing by proxy
  Initiator should be able to discover Responder STAs through the AP
Need SBP Initiator to establish an SA with Responder (optional)
  Related to the setup ID? Could establish keying material and setup ID is a hash of the key
  Pairwise key (initiator/responder)
  Could use public key
AP may authorize a SBP Initiator for proxy sensing
Does the connection between the Initiator and the Responder (for reporting) need to be protected (i.e. the AP cannot see the report)?
Need to understand the proxy sensing message flow in detail

## Slide 5: Next Steps
Should we establish consensus on these requirements?
Should we include a table like this in the Spec Framework?

## Slide 6: Discussion topics
Use cases – what can be solved, what cannot be solved.
Security can be different from privacy.
Are there unique privacy and security issues associated with sensing?