## Slide 1: Merged solutions for STA identification
Date: 2022-03-08
Authors:

## Slide 2: Abstract
Proposal to merge network-generated-id, sta-generated-id, MAAD, and Unique device ID

## Slide 3: Background
All three proposals have very similar principles
Merge them, allow for “negotiation” of style
Supports many use cases, provides flexibility for deployment model to fit the scenario
Note: Opaque device ID can also be used as method for Blobs in network-generated usage

## Slide 5: Example flow – Network generated ID
New STA:
STA provides nothing in Msg 2/4 (maybe we add an indication of intent to use network generated ID?)
Network generates a Blob
Network responds with Blob in Msg 3/4
(Maybe add an “OK” acknowledgement in Msg 4/4?)
Returning STA:
STA provides Blob in Msg 2/4, (encrypted in Key Data)
Network is configured for network ID, so expects the Blob
Network confirms it recognizes the Blob
Network responds with “OK” in Msg 3/4, or optionally provides an updated Blob

## Slide 6: Example flow – STA generated ID
New STA or returning STA (same flow for both):
STA provides ID in Msg 2/4, (encrypted in Key Data)
Network is configured for STA ID, so doesn’t expect a Blob
Network responds with “OK” in Msg 3/4

## Slide 7: Example flow – Optional MAAD
For either network-based or STA-based:
Initial connection:
STA uses random MAC address to connect
Network provides MAAD address in Msg 3/4
(Maybe add an “OK” acknowledgement in Msg 4/4?)
STA continues with random MAC address during association
Returning station:
STA uses new MAAD address (provided last time) to connect
Network provides new MAAD address in Msg 3/4
(Maybe add an “OK” acknowledgement in Msg 4/4?)
STA continues with “last time” MAAD address during association