## Slide 1: TG bh Cover ALL Use Cases
Date: 2022-02
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: 820.11bh PAR
“This amendment specifies modifications to the medium access control (MAC) mechanisms to preserve the existing services that might otherwise be restricted in environments where STAs in an Extended Service Set (ESS) use randomized or changing MAC addresses, without affecting user privacy. User privacy includes exposure of trackable information to third parties or exposure of an individual's presence or behavior.”
Issues Tracking Document lists 26 “Use Cases”, i.e., existing services, maybe 12 or so need to be ‘solved’, that is solutions that enable these applications to be simply preserved.

## Slide 3: Intro
Appeared to have consensus that Network generated ID preferred to STA generated.
We have two proposals using network generated
  Network generated device ID (NGID)
  MAC address designation (MAAD)

## Slide 4
NGID
AP allocates an ID to the STA during the 4-way HS, STA provides that ID on next association
  Any ID can be used, network controls the ID
  STA opts-in by showing Capability bit and by providing the ID when it associates.
MAAD
AP allocates a MAC address to the STA during the 4-way HS, STA provides that MAC address as TA on next association
  STA opts-in by setting Capability bit and by using the allocated MAC Address as TA.

## Slide 5: Methods are complimentary
NGID is well suited to applications where pre-association recognition not needed
MAAD is well suited to applications where pre-association recognition is required/used.
Both use a KDE in Message 3
Propose that both schemes be included :
  Application chooses which method suits best
    e.g. if pre-association recognition required or not
  STA can support one or both no problem
  Network/STA would use the scheme that best suits its needs

## Slide 6: Proposal
Simply accept both NGID and MAAD text
  they are distinct and each is suited to different applications
Draft text exists for both schemes.
Then ALL Use Cases are covered and our PAR is satisfied