## Slide 1: CC36 for CID 5032
Date: 2022-05-11
Authors:

## Slide 2: CID 5032

## Slide 3: Discussion
Although the [11-22/39r3] provides some discussions on FDMA solution , it doesn’t disclose the details implementation. This contribution is to facilitate development of the implementation.
Basic ideas:
Each EHT non-AP STA reports its peer’s information (like AID) to the AP MLD before EHT AP grants the TXOP.
AP allocates different subchannels to different TDLS peers via MU-RTS TXS frame.
 After the EHT non-AP STA transmits the CTS frame as the response to MU-RTS TXS frame, each TDLS peer( both transmitter and receiver) turns their BW to the allocated subchannel and then transmits and receive non-TB PPDUs without alignment

## Slide 4: Network topology
Note: STA1—STA4 affiliated with different non-AP MLDs
AP affiliated with an AP MLD
AP
STA1
STA4
WIFI connection
WIFI connection
TDLS connection
STA2
TDLS connection
WIFI connection
STA3
WIFI connection
P2P traffic
P2P traffic

## Slide 5: Subchannel solution (non-TB PPDU format: symbol alignment not needed for frequency sharing based on subchannel allocation)
TXOP
20Mhz
20Mhz
First
Second
SIFS
Frequency
SU PPDU(STA3->STA4)
SU PPDU(STA1->STA2)
SIFS
ACK
(4->3)
ACK
(2->1)
MU-RTS TXS TF
(RU1=STA1,Target RX: STA2-ID,
RU2=STA3, Target RX:STA4-ID)
MU-RTS TXS TF
duplicated
PPDU
PPDU
6 Guard
5 Guard
SIFS
CTS
CTS
Note: 5-6 Guard at the boundary of each subchannel can address the ACI issue.
Note: SU PPDU is an example of a non-TB PPDU.

## Slide 6: SP
Do you agree that an AP affiliated with AP MLD may assign different subchannels for TDLS peers via MU-RTS TXS frame?