## Slide 1: 802.11be enhancements for TSN time-aware scheduling and network management considerations
Date: 2022-04-19
Authors:

## Slide 2: Introduction
Growing interest in wireless for time-sensitive applications
  Factory/process automation, robotics, AR/VR/XR are a few examples
  A wide range of latency/reliability KPIs, but “determinism” is a common need
  Time-sensitive and other types of applications need to work in a converged network
  Interoperability/standards-based connectivity is needed for practical/wide scale adoption
Wi-Fi with TSN capabilities (WTSN) is a solution for time-sensitive applications in managed Enterprise/industrial networks
This presentation will discuss
  Time-sensitive application requirements
  Existing Wi-Fi capabilities including 802.11ax and TSN support
  Evolution of Wi-Fi capabilities (802.11be)
  Examples/demonstrations of Wi-Fi enabling industrial applications

## Slide 3: Application Classes
Monitoring & Analytics
Closed-loop Control Systems
Autonomous & Mobile Robots
Augmented/virtual reality
Delay-Tolerant
Time/Safety-Critical
(Hard Real-Time & Isochronous)
Delay-Intolerant
Need bounded latency & determinism
Notes: Add XR (connected worker) here – future of work – Malcolm

## Slide 4: Use cases where deterministic connectivity service with bounded latency are critical
Isochronous Industrial Control
Sensing
Actuation
Control
Extended Reality
Client
Edge
“Sensing”
“Actuation”
Motion to Photon Cycle: user tracking (“sensing”), computing (rendering) and display (“actuation”)
Control Cycle: sensing (I/O input), computing (control algorithm) and actuation (I/O output)
Rendering
HMD state
Video
Latency bound for communication
Motion to Photon Cycle

## Slide 5: Leading Use Cases and Requirements (Avnu Alliance WTSN Working Group)
 | Mobile Robots | Live Events | Closed loop Control | AR/VR
Typical area of service | Small/medium/large | Medium/large | Small/medium/large | Small/Medium
End stations per area of service | 100 | 100-500 | 50 | <5 devices/group
Traffic Profile | Cyclic and Event | Continuous stream | Cyclic and Isochronous | Cyclic (UL), video (DL)
Time Synchronization Accuracy | ~1 µsec | 1 µsec or better | 1 µsec or better | ~1 µsec
Bounded Latency | 10 – 1msec (cyclic) 100 – 10 msec (events) | 1msec | 10 – 1 ms (Cyclic) 10 – 100 ms (Events) | 3 to 10 msec
Reliability | 99.9 to 99.99% | 99.9 to 99.99% | 99.9 to 99.9999% | 99.9 to 99.99%
Security | Authentication, integrity and resilience to DOS/Interference | Authentication, privacy, resilience to DOS/Interference | Auth., integrity and resilience to DOS and time/QoS attacks | Auth., integrity and resilience to DOS.
Ref: https://avnu.org/wirelessTSN/

## Slide 6: Requirement considerations
Wide range of latency/reliability KPIs
  Many use cases in the 1 to 50 msec latency range
  Some use cases (e.g., motion control) need even lower latency 10’s to 100’s microsecs
Most mission-critical Enterprise and industrial applications that need “deterministic” service have predictable traffic flow behavior
  Devices need service at periodic intervals for a fixed amount of data (known a priori)
  Time-critical data needs to be delivered within a deadline
Practical scenarios are Managed, Enterprise & Industrial IOT networks
  Wi-Fi and WLAN networks are carefully planned and managed, including coverage tools, frequency planning, admission control policies, etc.

## Slide 7: Deterministic Wi-Fi
Wireless TSN
Time synch (.1AS)
Time-aware scheduling (.1Qbv)
Redundancy (.1CB)
Network
E2E wireless-wired integration Management & scheduling
Enablers
6 GHz Multi-radio clients/ APs
Core Capabilities
QoS management
802.11ax: OFDMA, Triggered access
802.11be MLO, 320 MHz, SCS, Restricted TWT
Deterministic Wi-Fi Enabling Tools

## Slide 8: TSN “toolbox” and 802.11 (Wi-Fi) support
Bounded Latency
Reliability
Synchronization
Resource Mgmt
TSN toolbox
Time synchronization (802.1AS-2020)
Time-aware scheduling (802.1Qbv)
Redundancy (802.1CB)
…
TSN Config (802.1Qcc, P802.1Qdj)
…
802.1AS over 802.11 TM,/FTM
802.11be Multi-link
Clear requirements mapped to 802.11ax and 802.11be features to meet the deadlines within the BSS:
Scheduling (802.11ax)
802.11be Enhancements: SCS/Flow QoS Characteristics and rTWT
Example TSN tools (not a complete list) enabled by 802.11
Time-Sensitive Networking (TSN) = deterministic data delivery with bounded latency without loss due to congestion or errors. Standards defined by the IEEE 802.1 TSN Task Group.
802.1AS + 802.1Qbv enable synchronous application cycle:
→ deterministic/periodic data with delivery deadlines

## Slide 9: Evolution of Wi-Fi determinism
Wi-Fi 5 (SU) experiences very high variability (>>100ms worst case) and effectively unbounded latency
Wi-Fi 6 (ULOFDMA) bounds max latency (<100ms)
WiFi7 (SCS QoS Characteristics w/ 20ms period) provides significant latency gain w.r.t. Wi-Fi 6 (<25ms)
11be (SCS QoS Characteristics w/ 20ms period + start-time) expected to bound latency to more stringent (<10ms) requirements
Wireless TSN (802.1Qbv) manages E2E latency to within 1ms 98%-ile for scheduled traffic
* E2E includes host-to-host including L2 switch and WLAN hops

## Slide 10: Network Configuration & Management
CUC
TSN-CS
Talker End Stations
TSN Bridges
Listener End Stations
Stream Data
Stream Data
End Station Configuration
OPC_UA (Pub/Sub)
UNI
End Station Configuration
(OPC_UP Pub/Sub)
1) End Station Configuration
End Station Configuration
Wired-TSN
CNC
Wireless Talker End Stations
2) SCS Req (Flow QoS)/
SCS Resp.
Wireless-TSN
AP
Wireless Listener End Stations
Stream Data
AP
WTSN-CS
1) Traffic flow QoS requirements and configuration between Talker and CUC/CNC
2) BSS QoS requirements and schedule aligned with TSN configuration
3) AP schedules channel access to meet QoS requirements using 802.11ax and 802.11be tools
3) Trigger +
DATA

## Slide 11: WTSN Evolution
TSN Enabling Capabilities
2019
2021
2023
Time Synchronization
Traffic shaping over
EDCA
802.11ac
802.11ax
802.11be
Traffic shaping and bounded latency with scheduled OFDMA operation
Deterministic low latency enhancements
WTSN Configuration and management
Redundancy over multi-radio
Redundancy over MLO
…
…
802.11 and TSN will continue to evolve and introduce new TSN tools

## Slide 12: TSN over WiFi 6 demo at MWC 2022
Joint demo by Cisco, Intel, Exor, and Keysight
Illustrating Realistic HMI scenario
  Heartbeat frame transmitted every 1ms
  Wireless emergency stop button generates repeated “emergency-stop” frames every 1ms when pressed
  Best Effort Traffic: ~20Mbps traffic
Demonstrated Technologies
  802.1AS synchronization via FTM
  802.1Qbv schedule with 1ms cycle time
Measurements conducted
  802.1AS synchronization performance
  Latency histograms illustrating 802.1Qbv performance

## Slide 13: Ecosystem activities in WBA and Avnu Alliance
Workgroup launched Feb. 2021 - https://wballiance.com/wi-fi-6-6e-for-industrial-iot/
Continue the IIOT work :
https://wballiance.com/resource/wi-fi-6-trial-report-industrial-manufacturing/
https://www.mettisgroup.com/wifi6/
Wireless TSN WG
https://avnu.org/wirelessTSN/
Defining use cases, market requirements and TSN capability testing specifications/Interop Events
https://avnu.org/wireless-tsn-paper/

## Slide 14: Conclusions
802.11 is already used as a connectivity solution for deterministic Enterprise applications such as Industrial IOT (IIOT) and AR/VR/XR
New capabilities (802.11be and Wireless TSN) are enabling support for these and future time-sensitive applications
  To meet isochronous communication requirements
  To more tightly bound latency and reliability
  To deliver on each application’s unique requirements
Wi-Fi and TSN trials, testing and deployments are in progress (WBA and Avnu Alliance)