## Slide 1: EDMG Multi-Static Sensing Sounding PPDU Structure
Date: 2022-04-12
Authors:
Name | Affiliation | Address | Phone | Email
Yan Xin | Huawei Technologies | Ottawa, Ontario |  | yan.xin@huawei.com
Rui Du | Huawei Technologies |  |  | ray.du@huawei.com
Stephen McCann | Huawei Technologies |  |  | stephen.mccann@huawei.com
Junghoon Suh | Huawei Technologies |  |  | Junghoon.Suh@huawei.com
Edward Au | Huawei Technologies |  |  | edward.ks.au@huawei.com
Osama Aboul-Magd | Huawei Technologies |  |  | Osama.AboulMagd@huawei.com

## Slide 2: EDMG Multi-Static Sensing
Multi-static sensing [1]: A multi-static system is one in which there are at least three STAs - for example, one receiver and two transmitters, or two receivers and one transmitter, or multiple receivers and multiple transmitters.
Multi-static sensing with one transmitter and two receivers
Procedure of multi-static sensing [2]

## Slide 3: Sounding PPDU Structure in Multi-Static Sensing
Multi-static sensing PPDU structure proposed in [3]
Sync filed in multi-static PPDU
The Sync fields for different responders use different rows from the matrix M(r, c) for the rth STA and the cth Golay sequence to construct sequences with good correlation properties.
DMG Multi-static sensing request frame proposed in [4]
including EDMG TRN-related parameters such as EDMG TRN Length, RX TRN-Units per Each TX TRN-Unit, EDMG TRN-Unit P, EDMG TRN-Unit M, EDMG TRN-Unit N and TRN Subfield Sequence Length subfields

## Slide 4: Discussion on the Proposed Sounding PPDU Structure
As proposed in [3], the Sync fields in multi-static sensing PPDU are designed with good correlations as possible for synchronization of different responders. Different Sync fields are transmitted to different responders possibly using different beams. Beam switching from one to another requires some operation time, potentially resulting in unreliable detection of Sync signals if one Sync field immediately follows another.
In general, a Data field includes padding bits in a PPDU. The proposed PPDU structure [3] adds the “Sync PAD” field which is transmitted using the same AWV as that for the “Data” field. However, in [3] the “Sync PAD” field is separated from the “Data” field increasing the number of AWV switches. To simplify the implementation, it is desirable to allocate the “Sync PAD” field to follow the “Data” field.
For ease of implementation and reduction of the impact due to a switch of AWV, it is desirable to minimize the change of AWV when transmitting a sounding PPDU in DMG multi-static sensing.

## Slide 5: EDMG Multi-Static Sensing Sounding PPDU Structure
To propose EDMG multi-static sensing sounding PPDU structure
With this proposed EDMG multi-static sensing sounding PPDU structure,
for better synchronization detection, it is proposed to separate Sync fields by P TRN subfields;
the number of AWV changes is reduced when transmitting the Sync field, padding field and TRN-Unit P field in multi-static sensing;
unlike in [3], the Padding field due to an introduction of Sync signals in multi-static sensing is transmitted by following the Data field without a need to change AWV.

## Slide 6: References
[1] IEEE 802.11-21/1890r0, DMG Sensing taxonomy.
[2] IEEE 802.11-22/0243r06, PDT DMG Sensing Procedure.
[3] IEEE 802.11-22/0464r1, PDT EDMG Multi-Static PPDU Structure.
[4] IEEE 802.11-22/0370r3, PDT DMG Multi-static Instance.

## Slide 7: SP
Do you agree to define EDMG multi-static sensing sounding PPDU structure as proposed in p.5 of 802.11-22/0636r0?
Yes:
No:
Abstain: