## Slide 1: EDMG Multi-Static Sensing Sounding PPDU Structure
Date: 2022-04-14
Authors:
Name | Affiliation | Address | Phone | Email
Yan Xin | Huawei Technologies | Ottawa, Ontario |  | yan.xin@huawei.com
Rui Du | Huawei Technologies |  |  | ray.du@huawei.com
Stephen McCann | Huawei Technologies |  |  | stephen.mccann@huawei.com
Junghoon Suh | Huawei Technologies |  |  | Junghoon.Suh@huawei.com
Edward Au | Huawei Technologies |  |  | edward.ks.au@huawei.com
Osama Aboul-Magd | Huawei Technologies |  |  | Osama.AboulMagd@huawei.com

## Slide 2: EDMG Multi-Static Sensing
Multi-static sensing [1]: A multi-static system is one in which there are at least three STAs - for example, one receiver and two transmitters, or two receivers and one transmitter, or multiple receivers and multiple transmitters.
Multi-static sensing with one transmitter and two receivers
Procedure of multi-static sensing [2]

## Slide 3: Sounding PPDU Structure in Multi-Static Sensing
Multi-static sensing PPDU structure proposed in [3]
Sync filed in multi-static PPDU is defined as
The Sync fields for different responders use different rows from the matrix M(r, c) for the rth STA and the cth Golay sequence to construct sequences with good correlation properties.
DMG Multi-static sensing request frame proposed in [4]
including EDMG TRN-related parameters such as EDMG TRN Length, RX TRN-Units per Each TX TRN-Unit, EDMG TRN-Unit P, EDMG TRN-Unit M, EDMG TRN-Unit N and TRN Subfield Sequence Length subfields

## Slide 4: Discussion on the Proposed Sounding PPDU Structure in [3]
EDMG-CEF is specified for channel estimation to detect Data field and possible
EDMG-Header-B field. In Multi-static sounding PPDU, Data field does not carry
any useful information. Transmission of the EDMG-CEF filed in a multi-static
sounding PPDU may also lead to a legacy EDMG device to continue conducting
an operation over the remaining fields of the whole PPDU. EDMG-CEF should be
removed from the multi-static sounding PPDU.
As proposed in [3], the Sync fields in multi-static sensing PPDU are designed with good correlations as possible for synchronization of different responders. Beam switching for Sync field transmissions from one to another may require more time compared to beam refinement, potentially resulting in unreliable detection of Sync signals with the format of Sync field [3];
Frequency beam switching may cause:
- additional RF signal phase changes after synchronization
- an impact on AGC accuracy at receiver
An additional field may be needed for improvement of frequency offset
estimation and phase tracking

## Slide 5: Discussion on the Proposed Sounding PPDU Structure in [3]
In general, Data field includes padding bits in a PPDU. The proposed PPDU structure [3] adds the “Sync PAD” field, which is transmitted using the same beam as that for the “Data” field, however, is separated from the “Data” field. To simplify the implementation, it is desirable to allocate the “Padding” field adjacent to the “Data” field, both of which are transmitted using the same beam.
For ease of implementation and reduction of the impacts due to beam switches , it is desirable to minimize the beam change when transmitting a sounding PPDU in EDMG multi-static sensing.

## Slide 6: EDMG Multi-Static Sensing Sounding PPDU Structure
To propose EDMG multi-static sensing sounding PPDU structure
This proposal of EDMG multi-static sensing sounding PPDU structure
minimizes the impacts on a legacy EDMG device by removing the EDMG-CEF field
minimizes the impacts of additional phase changes and AGC accuracy, and to perform better synchronization detection. It is proposed to arrange a Sync field and P TRN subfields using the same beam to be adjacent each other;
allocate Padding field to be adjacent to Data field both of which use the same beam in order to reduce the total number of beam changes when transmitting the Sync field, padding field and TRN-Unit P field before the first group of TRN subfields.

## Slide 7: References
[1] IEEE 802.11-21/1890r0, DMG Sensing taxonomy.
[2] IEEE 802.11-22/0243r06, PDT DMG Sensing Procedure.
[3] IEEE 802.11-22/0464r2, PDT EDMG Multi-Static PPDU Structure.
[4] IEEE 802.11-22/0370r3, PDT DMG Multi-static Instance.

## Slide 8: SP
Do you agree to define EDMG multi-static sensing sounding PPDU structure as proposed in p.5 of 802.11-22/0636r2?
Yes:
No:
Abstain: