## Slide 1: SP for TGbf Freq Domain CSI Feedback
Date: 2022-03-31
Authors:
Name | Affiliation | Address | Phone | Email
Junghoon Suh | Huawei |  |  | junghoon.suh@huawei.com
Yan Xin |  |  |  | Yan.Xin@huawei.com

## Slide 2: Background
The following CSI Feedback (Freq. Domain) methods have been introduced in TGbf
  11n based CSI Quantization with extension to higher bandwidth and number of RF chains [1]
  2’s power scaling method [2]
  Differential CSI Quantization [3]
  Phase and Magnitude [4]
A thorough examination of each scheme has been conducted based on the following three metrics
  Performance (Signal to Quantization Noise Ratio)
  Complexity
  Feedback Overhead

## Slide 3: Comparison of two schemes
 | Performance | Complexity | Feedback Overhead
[1] 11n based | Best. Upper Bound | Division operation in the normalization with scale factor. Not a big issue in the mass production | Scale factor can be fed-back per link (1dB loss from the per-tone scale factor feedback)
[2] Fractional scaling | 1 dB loss from [1] with 6 bit scale factor feedback | Bit shift in the normalization with scale factor. Pre-normalization may be required to obtain the maximum channel gain bounded by | Similar to [1]. Scale factor can be fed-back per link
 | Performance | Complexity | Feedback Overhead
[1] 11n based | Best. Upper Bound | Division operation in the normalization with scale factor. Not a big issue in the mass production | Scale factor can be fed-back per link (1dB loss from the per-tone scale factor feedback)
[2] Fractional scaling | 1 dB loss from [1] with 6 bit scale factor feedback |  | Similar to [1]. Scale factor can be fed-back per link

## Slide 4: Issue with 2’s power scaling method
Assuming is 1 and
is 1 and
, is 1 and
, is 1 and
……….
,where is the internally normalized
Channel parameter output in the green box
In order to obtain ,
the estimated channel gains should be normalized by inside the green box

## Slide 5: Controlling Output Data Path Size
When MH is the largest value of H, m =
When MH is another statistics value of H different from the largest value of H, then, we need to take an extra normalization of by the maximum value of in order to obtain m =
AGC
ADC
FFT
GI Removal and
Channel Estimation
U
D
H
Statistics of the amplitude of U, MU
Statistics of the amplitude of D, MD
Statistics of the amplitude of H, MH, where H is the channel parameter
NU
ND
NP

## Slide 6: Updated 802.11n CSI matrices quantization procedure
The maximums of the real and imaginary parts of each element of the matrix in the entire bandwidth are found as following
Choose the scaling factor, as following, (nowis not a function of subcarrier, but is a function of link (Antennas pair)), that is, is (1,1),…,(Tn,Rn), where Tn is the number of TX RF chains and Rn is the number of RX RF chains
=
=
, for the real part
, for the imaginary part

## Slide 7
3. The real and imaginary parts of each element in the matrix (k) are quantized to Nb bits in twos complement encoding as defined by following
k is the subcarrier index
R represents real component
I represents imaginary component
NSR indicates the half the size of
Subcarriers per symbol excluding Nulls

## Slide 8: Quantization of scaling factor ()
Let’s denote the quantized scaling factor to be
  (Quantize)
Let’s assume K bits to be the quantization size for
 Feedback to the initiator
The reconstruction of scaling factor at the initiator

## Slide 9: References
[1] 11-21-1676-01-00bf-simplified-scaling-factor-feedback-for-csi-matrices
[2] 11-22-0414-02-00bf-fractional-scaling-factor-for-sensing-measurement-report
[3] 11-22-0506-01-00bf-differential-quantization-for-csi-report
[4] 11-21-1921-00-00bf-partial-csi-feedback
[5] Christian Berger, “CSI Feedback Format”, TGbf CSI_ESTIMATE Offline Discussion Group

## Slide 10: SP 1
Do you agree to have a conditional mandatory CSI Feedback scheme according to the CSI matrices feedback as defined in IEEE Std 802.11-2020 with the additional following implementation updates?
  The bandwidth parameter is extended to support up to 160 MHz/320 MHz depending on Sensing NDP format
  The TX-RX pair parameters are extended to support up to 8 RF chains in each TX and RX
  The maximums of the real and imaginary parts across the entire subcarriers can be found per each link (TX-RX pair) for the Scale Factor
  This is for the freq domain CSI feedback
  “conditional mandatory” means that the CSI Feedback Scheme proposed in this SP is mandatorily supported, when the CSI Feedback is supported in a STA

## Slide 11: Appendix
802.11n CSI matrices quantization procedure

## Slide 12: 802.11n CSI matrices quantization procedure
The maximums of the real and imaginary parts of each element of the matrix in each subcarrier are found as following
The scaling ratio is calculated and quantized to 3 bits as following

## Slide 13: 802.11n CSI matrices quantization procedure continues …
3. Linear Scaler of step 2 is given as following
4. The real and imaginary parts of each element in the matrix (k) are quantized to Nb bits in twos complement encoding as defined by following
NSR indicates the half the size of
Subcarriers per symbol excluding Nulls
k is the subcarrier index
R represents real component
I represents imaginary component