## Slide 1: WLAN Two-Way Sensing Use Cases
Date: 2022-04-15
Authors:
–
Name | Affiliations | Address | Email
Oscar Au | Origin Wireless Inc. | 7500 Greenway Center Drive, Suite 1070, Greenbelt, MD 20770 USA | oscar.au@originwirelessai.com
Beibei Wang |  |  | beibei.wang@originwirelessai.com
K.J. Ray Liu |  |  | 
Hung-Quoc Lai |  |  | 

## Slide 2: Review of Non-TB sensing (Motion 39, 21/1433r2)
One non-AP STA is sensing initiator and one AP is sensing responder.
Non-AP STA transmits an NDPA and two consecutive NDPs: I2R and R2I NDP.
If non-AP STA is only the sensing transmitter (uplink sounding), then I2R NDP is used to generate sensing measurement while the R2I NDP does not.
If non-AP STA is only the sensing receiver (downlink sounding), then R2I NDP is used to generate sensing measurement while the I2R NDP does not.
Sensing NDPA
R2I NDP
For downlink sounding
I2R NDP
AP,
sensing responder
SIFS
Non-AP STA, sensing initiator
For uplink sounding
Sensing Measurement Report frame
For uplink sounding
SIFS

## Slide 3: Use case: Two-way sensing
One-way sensing: In a TB or non-TB sensing instance, the sensing initiator can send NDP to sensing responder to generate sensing results, and sensing responder can use sensing measurement report frames to send sensing results to sensing initiator. Alternatively, sensing responder can send NDP to generate sensing results at sensing initiator.
2-way sensing use case: There are some use cases in which both AP and non-AP need sensing results. E.g. one performs a sensing task while the other performs another sensing task. We propose that 11bf should support two-way sensing use case.
  E.g. a home router (AP) may run motion detection application for home security, while a TV (non-AP STA) may run presence detection for improved TV viewing experience and a bedroom device (non-AP STA) may run sleep monitoring for sleep well-being applications. Both AP and TV may need sensing result. Both AP and bedroom device may need sensing results.
  AP may run WLAN sensing applications from AP vendor or ISP, while non-AP STAs (consumer electronics, IoT devices, high-end, low-end, etc) may run WLAN sensing applications from consumer electronics/IoT device manufacturers. The AP applications and non-AP STAs applications tend to be different due to different goals.
  A home may have 10 to 20 IoT devices. This two-way sensing need may arise in a majority of the IoT devices.

## Slide 4: Two-way Non-TB sensing
Non-TB sensing (initiator=non-AP, responder=AP) already has both I2R and R2I NDP. We can simply use them.
Two-way sensing for non-TB sensing:
  In a non-TB sensing instance, both I2R NDP (uplink sounding) and R2I NDP (downlink sounding) can be used to generate sensing results at AP and non-AP respectively.
  There is NO NEED for AP (sensing responder) to use sensing measurement report frame to transmit its sensing measurement result to non-AP STA (sensing initiator), because the non-AP STA has its own sensing results.

## Slide 5
SME
SME
MLME
MLME
MLME-SENS NTB MSMT RQ.request
NDPA
NDP
MLME-SENS NTB REPORT.indication
Sensing initiator (non-AP STA)
Sensing responder (AP)
MLME-SENS NTB REPORT.indication
NDPA
NDP
MLME-SENS NTB REPORT RQ.request
MLME-SENS NTB REPORT RQ.confirm
Sensing Measurement Report frame
MLME-SENS NTB MSMT RQ.confirm
One-way non-TB sensing: (Uplink sounding) sensing measurement results reported from AP to Non-AP STA.
One-way non-TB sensing: (Downlink sounding) sensing measurement at Non-AP STA; No sensing measurement report frame.
Non-TB sensing

## Slide 6
SME
SME
MLME
MLME
MLME-SENS NTB MSMT RQ.request
NDPA
NDP
MLME-SENS NTB REPORT.indication
Sensing initiator (non-AP STA)
Sensing responder (AP)
MLME-SENS NTB REPORT.indication
NDPA
NDP
MLME-SENS NTB REPORT RQ.request
MLME-SENS NTB REPORT RQ.confirm
Sensing Measurement Report frame
MLME-SENS NTB MSMT RQ.confirm
One-way non-TB sensing: (Uplink sounding) sensing measurement results reported from AP to Non-AP STA.
One-way non-TB sensing: (Downlink sounding) sensing measurement at Non-AP STA; No sensing measurement report frame.
Non-TB sensing
MLME-SENSNTBREPORT.indication
NDPA
NDP
NDP
MLME-SENSNTBREPORT.indication
Two-way non-TB sensing: (uplink + downlink sounding) sensing measurement at both AP and non-AP STA; No sensing measurement report frame.

## Slide 7: Two-way TB sensing
In TB sensing (initiator=AP, responder=non-AP), AP uses either NDPA frame (downlink sounding) or Trigger Frame (uplink sounding) to signal the transmission of NDP, which is one-way sensing.
Two-way sensing for TB sensing:
  In a TB sensing instance, AP can send a “Two-way Trigger Frame” (e.g. we can re-use Trigger Frame or NDPA frame), followed by both I2R and R2I NDP such that sensing results are generated at both AP and non-AP.
  NO NEED for sensing responder (non-AP) to use sensing measurement report frame to transmit its sensing measurement result to sensing initiator (AP), because the sensing initiator has its own sensing results.

## Slide 8
SME
SME
MLME
MLME
MLME-SENS TB MSMT RQ.request
SENS Poll Frame
NDP
MLME-SENS TB REPORT.indication
Sensing initiator (AP)
Sensing responder (non-AP STA)
MLME-SENS TB REPORT.indication
SENS Trigger Frame
NDP
MLME-SENS TB REPORT RQ.request
MLME-SENS TB REPORT RQ.confirm
Sensing Measurement Report frame
MLME-SENS TB MSMT RQ.confirm
One-way TB sensing: (Downlink sounding) sensing measurement results reported from non-AP to AP using report frame.
One-way TB sensing: (Uplink sounding) sensing measurement at AP; No sensing measurement report frame.
CTS-to-self
SENS NDPA Frame
TB sensing

## Slide 9
SME
SME
MLME
MLME
MLME-SENS TB MSMT RQ.request
SENS Poll Frame
NDP
MLME-SENS TB REPORT.indication
Sensing initiator (AP)
Sensing responder (non-AP STA)
MLME-SENS TB REPORT.indication
SENS Trigger Frame
NDP
MLME-SENS TB REPORT RQ.request
MLME-SENS TB REPORT RQ.confirm
Sensing Measurement Report frame
MLME-SENS TB MSMT RQ.confirm
Two-way TB sensing: (Downlink/uplink sounding) sensing measurement at both AP/non-AP STA; no report frame.
CTS-to-self
SENS NDPA Frame
NDP
MLME-SENS TB REPORT.indication
MLME-SENS TB REPORT.indication
NDP
One-way TB sensing: (Downlink sounding) sensing measurement results reported from non-AP to AP using report frame.
One-way TB sensing: (Uplink sounding) sensing measurement at AP; no report frame.
“Two-way Trigger” Frame
TB sensing

## Slide 10: Comparison with NDPA sounding/TF sounding
One of NDPA sounding and TF sounding
Report frame optional
Overhead - one sounding
Sounding frequency controlled by AP
Non-AP STA in sleep mode - wake up once
Both of NDPA sounding and TF sounding
Report frame optional
Overhead - two soundings
Sounding frequency – can be different for AP and non-AP STA
Non-AP STA in sleep mode – wake up once/ twice, longer
Proposed two-way sensing
No report frame
Overhead - one sounding
Sounding frequency - same for AP/non-AP STA
Non-AP STA in sleep mode - wake up once

## Slide 11: Straw Poll (SP1)
Do you agree to add the following to SFD and D0.1?
“Two-way sensing within a sensing measurement instance is supported.”
Yes
No
Abstain

## Slide 12: Straw Poll (SP2)
Do you agree to add the following to the SFD (D0.1)?
“A sensing measurement instance shall optionally support transmission of both forward NDP (e.g. I2R NDP) and backward NDP (R2I NDP) in tendon to generate sensing measurement results in each of a pair of sensing transmitter and sensing receiver.”
Yes
No
Abstain

## Slide 13: Straw Poll (SP3)
Do you agree with the following?
In sensing measurement instance performing the proposed two-way sensing, sensing measurement report frames shall NOT be used to transmit sensing measurement results.
Yes
No
Abstain

## Slide 14: Straw Poll (SP4)
In two-way TB sensing use cases, which one of the following do you prefer to use as “Two-way Trigger” frame to signal the transmission of I2R and R2I NDPs?
NDPA frame
Trigger frame
Another frame
Abstain