## Slide 1: WLAN Two-Way Sensing Use Cases
Date: 2022-04-26
Authors:
–
Name | Affiliations | Address | Email
Oscar Au | Origin Wireless Inc. | 7500 Greenway Center Drive, Suite 1070, Greenbelt, MD 20770 USA | oscar.au@originwirelessai.com
Beibei Wang |  |  | beibei.wang@originwirelessai.com
K.J. Ray Liu |  |  | 
Hung-Quoc Lai |  |  | 

## Slide 2: Two-way Responder-to-Responder sensing
In sensing procedure initiated by AP, responder-to-responder sounding is optionally allowed.
Two-way Responder-to-Responder sensing:
  In sensing procedure initiated by AP, we propose to optionally allow two-way sounding between two responders, with an NDP from responder1 (R1) to responder2 (R2) and another NDP from responder2 (R2) to responder1 (R1).
  This is useful when there are N responders forming a daisy chain or a scanning order or a configuration.
  For an example of N=3, three responders R1, R2 and R3 may form a closed daisy chain or a closed loop. R2 can get CSI between R1-R2 and also between R2-R3. It can perform useful WLAN sensing computation based on the two CSIs. Optionally the CSI may be reported to AP.

## Slide 3: Example of Two-way Responder-to-Responder sensing
In this example, four sensing responders R1, R2, R3 and R4 are configured to form a network (e.g. daisy chain)
Some “links” may do two-way sensing (e.g. R1-R2, or R2-R3) s.t. each linked pair would send NDP to each other in tandem (e.g. R1-to-R2 NDP and R2-to-R1 NDP)
Some links may do one-way sensing (e.g. R3-R4, R4-R1) s.t. NDP would be sent in one direction only
R2 has two CSIs: CSI between R1-R2, and CSI between R2-R3 (more if R2 is further linked to additional responders such as R4)
Reporting of sensing measurements are optional
AP=
Sensing Initiator
Non-AP STA R1= Sensing Responder, Tx/Rx
Non-AP R2= Sensing
Responder, Tx/Rx
Non-AP R3= Sensing
Responder, Tx/Rx
Non-AP R4= Sensing
Responder, Tx/Rx
Sensing PPDU transmission
Optional CSI transmission

## Slide 4: Straw Poll (SP1)
Do you agree to add the following to SFD and D0.1?
“In the optional responder-to-responder sensing, a first sensing responder should be allowed to perform one-way sensing or two-way sensing with a second sensing responder. In the one-way sensing, an NDP is sent from the first responder to the second responder. In the two-way sensing, an NDP is sent from the first responder to the second responder followed by another NDP sent from the second responder to the first responder.”
Yes
No
Abstain