## Slide 1: Further discussion on next generation WLAN
Date: 2022-05-09
Authors:

## Slide 2: Introduction
In previous WNG SC meetings, 6 contributions [1-6] about “beyond be” were presented and it is expected that more and more contributions will pop up.
802.11 members are almost aligned to start a next generation “beyond be” activity this year (e.g., September or later).
In this contribution, we will focus on the following two areas:
  Provide preliminary answer to the questions in the last WNG SC meeting about machine learning (ML) impact on standardization
  Initiate a discussion about the primary objectives and their corresponding KPIs for a “beyond be” activity.

## Slide 3: Machine learning enabled use cases
In reference [6], we initialized a discussion on machine learning (ML) enabled use cases, as shown below
Next step: to continue the study of ML enabled use cases and identify target use cases that impact the specification.
Delay insensitive use cases | Delay sensitive use cases
Enhanced roaming/mobility | Distributed channel access
Multi-RU/channel allocation (preamble puncture, channel bonding, channel assignment) | Channel estimation
Latency/QoS optimization | Link adaptation
Traffic prediction | Beam management
Device level power consumption | MU-MIMO MAC scheduling (user selection and resource allocation)
Spatial reuse | CSI compression and feedback
 | MIMO detection

## Slide 4: An example- Machine learning framework
To identify target use cases that impact the specification, we should first have a common understanding on an ML framework. An example of a ML framework[7][8] from 3GPP is shown in the figure below:
Data Collection: a function that provides input data to the ML Model Training and ML Model Inference functions. It may involve the exchange of data between an AP and non-AP STA.
ML Model Training: a function that creates an ML model to learn features and patterns that best represent the training data automatically. It may be time-consuming.
ML Model Inference: a function that uses a pre-trained machine learning model to make a prediction and guide the decision. It is less computationally intense.
Typically, there are three types of machine learning algorithms: supervised learning, unsupervised learning and reinforcement learning.

## Slide 5: Machine learning for air interface
For a machine learning framework, the AP and non-AP STA can act as different function nodes. Based on the placement of ML model training/inference functionality, the follow two types are recommended
Type 1: the air interface has limited support of light information exchange, excluding the parameters of the ML model
AP
(ML Model Training &Inference)
Non-AP
Feedback from
non-AP
Output
ML Model Training & Inference and Data collection are implemented at the AP side, the non-AP STA can perform action according to the received output of ML Model Inference
The non-AP STA can provide feedback, such as performance metric or SINR, to the Data Collection component as a close-looped ML framework
AP
(Data collection)
Non-AP
(ML Model Training &Inference)
ML Model Training & Inference are implemented at the non-AP STA side, but the data collection is done at the AP side and the requested data is delivered to the non-AP STA over the air
The non-AP STA also provides feedback, such as performance metrics or SINR, to the AP if needed.
Feedback from
non-AP
Feedback from AP

## Slide 6: Machine learning for air interface
Type 2: the air interface is supposed to support both model deployment and parameter updates.
AP
(ML Model Training)
Non-AP
(ML Model Inference)
Feedback from
non-AP
Model deployment/ update
ML Model Training is implemented at the AP side, ML Model Inference is implemented at non-AP STA side. The non-AP performs ML Model Inference and action according to the output of ML Model Inference
The non-AP STA can provide feedback, such as performance metrics to update the trained ML Model
AP
(ML Model Training &Inference)
Non-AP
(ML Model Training &Inference)
ML Model Training & Inference are implemented at both the AP and the non-AP STA side, the general ML model is downloaded/updated from a control center-AP
The non-AP STA refines the received general ML mode using it’s own environment and performance and can provide feedback, such as performance metrics to update the general trained ML Model
Feedback from
non-AP
Model deployment/ update

## Slide 7: Possible way to continue machine leaning study
Exchange over the air interface in slide 5 and 6 could provide some insights on the specification impact. To have more deep understanding, we suggest the group consider the following work:
Collect ML background information and reach an alignment on ML terminology. Propose some high level principles, such as
  Which parts of ML should be implementation specific, e.g., the detailed ML model?
  Where should ML functionality reside within the current 802.11 architecture?
  How to ensure training data represents a realistic environment, both in terms of quality and quantity, possibly with synthetic data augmented with real data?
Study and specify a machine learning framework for 802.11
  Create a generic ML framework, including training and inference components/functionalities
  Determine the placement of ML model training and ML model inference functions
  Specify air interfaces updates to convey the required data for AI functions

## Slide 8: Possible way to continue machine leaning study
  Accuracy of a STA’s ML model can also be improved by utilizing other STAs’ ML models.
  Study and evaluate the model performance under distributed and federated ML-enabled 802.11
  Study and evaluate the standardization impacts for an ML model shared between two STAs or an ML model downloaded from an AP (or network server) to a STA
Study and specify ML target use cases that could benefit from machine learning, including
  Identify a set of limited ML target use cases with their specification impacts
  Evaluate the standardization impacts, including data collection, input/output from the Model Training and Model Inference functions
  Determine the standardization impacts on the air interface to convey the necessary information/data to support the ML functionalities
  Align evaluation methodology metrics and data model
  Evaluate the performance gain of various ML based solutions

## Slide 9: Primary objectives and KPIs for beyond be
Based on the motion text about the formation of the EHT SG, we initiate a discussion about the primary objectives and their corresponding KPIs for a new “beyond be” amendment.

## Slide 10: Primary objectives and KPIs for beyond be
The following use cases that drive “beyond be” have been discussed so far
The main/key use cases, such as metaverse, AR/VR/XR, urgently demand further improvement on throughput and latency
Categories | Use cases
High throughput | Metaverse, digital twin, Cloud AR/VR/XR/MR, wireless projection, 8K/16K Video
Low latency | Metaverse, real-time AR/VR/XR, gaming, tactile signals, Industrial PLC control, Cloud/edge computing, p2p links (distributed sharing/operation between devices)
Extended coverage | Large home/office, wireless video doorbells and wireless home security surveillance cameras
Reliability/manageability | ‘Private Cellular’ networking (e.g., for IoT industrial)
Device power consumption | combat/limit climate change, e.g., carbon-neutral
AI/ML enabled (different from other categories) | Traffic prediction, Enhanced roaming/mobility, Multi-RU/channel allocation, channel access, MU-MIMO MAC scheduling …

## Slide 11: Primary objectives for beyond be
Two primary objectives for this new “beyond be” amendment are proposed:
  Increase throughput for both AP and non-AP STA
  Improve worst-case delay bound
The KPIs of these two primary objectives are:
  100 Gbps for peak aggregated throughput [1] and 10 Gbps for non-AP STA with 2 spatial streams[3]
  Note- the above numbers are in terms of PHY data rate
  Less than or equal to 1 ms for worst-case delay bound in at least one scenario [6]
  For other objectives, such as intelligence, converge, Reliability/manageability, mobility, power consumption, we could continue to discuss them in a TIG/SG

## Slide 12: Summary
A discussion about the machine learning (ML) impact on 802.11 standardization and possible ways to continue the study of machine learning are provided in this contribution.
Two primary objectives are proposed for “beyond be”, including
  Increase throughput for both AP and non-AP STA
  Improve worst-case delay bound

## Slide 13: References
[1] 11-22-0030-01-0wng-look-ahead-to-next-generation
[2] 11-22-0032-00-0wng-next-gen-after-11be
[3] 11-22-0046-01-0wng-next-generation-after-802-11be
[4] 11-22-0059-00-0wng-beyond-be
[5] 11-22-0418-00-0wng-considerations-of-next-generation-beyond-11be
[6] 11-22-0458-01-0wng-looking-ahead-to-next-generation-follow-up
[7] https://www.3gpp.org/ftp/specs/archive/37_series/37.817/37817-h00.zip
[8] https://www.3gpp.org/ftp/TSG_RAN/TSG_RAN/TSGR_94e/Docs/RP-212708.zip