## Slide 1: TG bh MAAD MAC Outline
Date: 2022-02
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Introduction
MAAD MAC has been presented a few times, but it has been realized, based upon questions I have received, that the details are still somewhat not understood by several.
This Outline’s objective is to try to make it clear that MAAD MAC scheme is simple, secure, and an apt solution for TGbh.

## Slide 3
BASICS:
MAAD MAC Both STA and AP advertise support
AP assigns a new MAAD MAC address at every RSN association
STA uses that NEW allocated address the NEXT time it associates
  New MAC Address EVERY Association
  Cannot be followed
AP recognizes STA pre-association
  AP “knows” the MAC Address
Reassociation uses MAC address used for the association
  Has to, that’s the rule
Text is in 22/0427r5

## Slide 4: Outline
AP and STA show support for MAAD in Extended Capabilities
STA associates first time using 4 W HS
A MAAD MAC Address sent by AP in EAPOL-Key msg 3/4 (as per NG ID)
  48 bit MAC address, Locally administered (maybe SLAP?)
  AP stores the allocated MAAD MAC for that STA
  STA stores the allocated MAAD MAC for that AP
When STA comes back it uses that previously allocated MAAD MAC Address as TA
AP instantly recognizes the STA from TA in Association Request etc.
  AP can identify the STA pre-association – e.g. directed probe
STA Associates using the allocated MAAD MAC as TA
At association, AP provides new MAAD MAC address in EAPOL-Key msg ¾
  New MAC Address used for the NEXT association.
NOTES (as per network generated device ID):
For FILS new MAAD MAC address is received in Association Response frame
For FT new MAAD MAC address is received in EAPOL-Key msg 3/4, but not during the FT protocol reassociations within the same ESS

## Slide 5: ADVANTAGES
TA is identified pre-association
  STA is identified and AP can decide to let it associate, which changes the MAAD MAC Address
  Any attempt to spoof the MAC Address is doomed to failure (if STA associated, MAC address changed, if it was not allowed to associate, then MAC address is not accepted)
TA changes every time, but is identified only by the AP
  STA cannot be tracked
Existing Apps, affected by RCM, can be easily adapted (a true TGbh solution)
  Applications as per Use Cases use the MAC Address as identifier
  MAC address again used BUT ONLY THE AP KNOWS IT.
No link between a STA ID and the (changing) MAC Address.
From outside, MAC Address is Random
AP and STA store just the latest MAAD MAC allocation
No calculations!!

## Slide 6: MOTION
Do you agree that the MAAD scheme, as described in <this document> (text is in 22/0427r5), is included in the TGbh Amendment?