## Slide 1: TG bh Identifiable Random MAC Address (revised)
Date: 2022-01
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Intro
This is a presentation on “Identifiable Random MAC Address”, IRMA
Original proposal was 21/1585r12
This proposal removes the need for Robust Action frames and sends the IRMK in message 4 of the 4 w HS.
IRM is a STATION allocated scheme. STA has control over the MAC Address used.

## Slide 3: 802.11 Definitions
  Identifiable Random MAC (IRM) : a scheme where a non-AP STA uses identifiable random medium access control (MAC) addresses (IRMA) to prevent third parties from tracking the non-AP STA while still allowing trusted parties to identify the non-AP STA.
Identifiable Random MAC Address (IRMA) – a random MAC address used by a STA using IRM
Identifiable Random MAC Key (IRMK) – a Key used to resolve an IRMA

## Slide 4: Identifiable Random MAC Address - IRMA
Purpose
  Prevent third-parties from tracking the STA while still allowing trusted parties to recognize the STA.
Identifiable
  Uses a key shared with trusted AP/network – IRMK
    Updated every association
  IRMA is the random TA MAC address used by the STA
  STA generates an “IRM OKM” using IRMK and IRMA
  IRM OKM is sent in IRM element (in Association Request)
Changing fields
  The IRMA (TA), IRM OKM and IRMK change for every association
AP uses IRMK as the identification for the STA on NEXT association

## Slide 5: CAPABILITY BIT
An IRM Capability field is used in the STA and AP
The AP looks for the IRM Capability AND the IRM Hash in IRM element
AP can use the IRM Capability bit to indicate to STAs that there may be a reason to be identified, i.e., “I provide a service”

## Slide 6: Basic Steps for IRM
STA and AP indicates IRM support in Extended Capability Field
First Time Association
STA generates 48 bit IRMA
  Generates a random 46 bit number
  Appends I/G = 0, U/L = 1 (Compatible with 12.2.10)
STA sends the IRM element in Association Request
  IRM Indicator set to “Unknown”
  IRM OKM field is omitted.
During Association, STA sends an IRMK in message 4
  AP stores this IRMK

## Slide 7: STA Re-Associates
Re-Associations
STA generates 48 bit IRMA
STA calculates IRM OKM using the IRMA and the IRMK previously provided to that AP
STA sends the IRM element in Association Request
  IRM Indicator set to “Known” and IRM OKM is included
  IRM Check field may be included (Down-selects IRMK list by factor of 256)
AP uses IRMA and stored IRMKs to calculate IRM OKM and identifies the STA IRMK.
During Association STA sends a new IRMK to AP
AP and STA update their lists
It’s important to note that the IRMK is not used to reveal the STA’s MAC or “identity” address but for verification purposes only, i.e., the OKM matches

## Slide 8: IRMK and IRM OKM function
IRMK (Identifiable Random MAC Key)
STA generates the IRMK
  Random 72-bit number .
STA provides an IRMK with AP when first associated
STA provides IRM OKM in “IRM element”
The IRMK is used to resolve the identity of the STA
  verifies that the OKM included in the IRM element matches the output of the local OKM computation
  IRM OKM= HKDF-Expand (IRMK, IRMA, 9)
  This produces a 9 octet, 72 bit, output key
Since the AP has the IRMK stored locally and has access to the IRMA (the TA address) and the IRM OKM in the association packet, it can perform this computation and verify the IRMK
NOTE: Only the HKDF-Expand is used because the IRMK is already a “good” pseudorandom key. i.e. the HKDF-Extract is not required.
NOTE: 72 bit key is considered secure enough for this application. For reasons that will become clear. Only real need is to prevent duplicates.

## Slide 9: IRM element
STA can use “private” address
IRM element sent in Association Request
AP then knows if STA IRMK already known (stored) or not
See next slide
Thinking about adding indicators such as “ID”. Tells AP STA has an ID.

## Slide 10: IRMK Check field
IRMK Offset takes a value N, from 0 to 56 (Note: IRMK is 72 bits)
The Check field contains the 8 bits representing the EX-OR of the 8 bits of the IRMK, bN to bN+7 with the following 8 bits (bN+8 to bN+15)
i.e. For n = 0 to 7
Bits in Check field are bn = EX-OR (bN+n, bN+n+8) where bN is Nth bit in IRMK
Note: Could keep it simpler by just providing 8 bits of the key. Same basic integrity.
Acts as a “Hint” to the AP so AP can quickly find a stored IRMK.
Reduces the list of IRMKs by 1/256
e.g. correct key in a list of 1000 IRMKs found in just 2 calculations
As key changes every association no incentive to try to break it.
Reduces the integrity of key from 72 bits to 64 bits

## Slide 11: Pre-Association
AP can identify the STA from the Association Request
AP can decide if STA is a ‘wanted STA’ and allow association
When STA associates, the IRMK is changed
NOTE: If 3rd party copies MAC address, then it will not work if STA did associate, if STA was refused association, then copying address is moot.

## Slide 12: IRM is very Secure
Every time STA associates, the address IRMA AND IRM Hash values change.
  Impossible to know if same STA associating.
Even if Third party brute strength all keys, IRMK (72 bits, or 64 bits if using IRMK Check), to find the IRMK, as IRMK changes each association, there is no point!!!
  Actually 72 bits is probably overkill.
Spoof STA copying the IRMA and IRM OKM from an association is not recognized by AP as the IRMK changed after “real” STA associated.
IMPOSSIBLE to know the STA for third parties listening as IRMA and IRM OKM change every time (as does the IRMK)

## Slide 13: STA details and Storage
IRM enables the AP to identify the STA,
  i.e. STA “123”
AP can exchange frames or higher layer APP can then associate STA 123 with some other specific details/IDs
  Membership ID , customer ID, guest ID, family member, employee ID, etc.
  AP stores 9 octets for the IRMK for each STA.

## Slide 14: Advantages
A different Random MAC is used even when returning to same ESS – more privacy!
  Even though STA indicates “Known”, No way a 3rd party can know if same STA (unlike “same MAC address for same AP”)
  MAC address and OKM IRM field values change every time.
An IRM STA can still choose to use “private” random MAC
  If no OKM IRM Hash field, then private MAC address in use.
STA changes IRMK at every association
  Changed when associated. Hence even if brute force were practical to find IRMK, if changed, impossible to spoof or know if same STA reassociates
  AP still knows that it is STA X even though IRMK has changed
AP can store long lists
  IRMK Check down selects the list by a factor of 256 – 1000 stored IRMKs found with just 2 calculations.
  AP can request IRMK but must provide a reason
  If AP drops STA from its list, it gets a new IRMK anyhow and can perform the higher level interrogation again.
STA can be identified pre-association
  AP can check stored IRMKs as soon as Association Request received OR wait for association
Use Case problems created by RCM are simply adapted as ID is still the MAC Address
However, address is only known by AP.

## Slide 15: Motion
Do you agree that an Identifiable Random MAC scheme, along the lines as described in <this document>, is included in the TGbh Amendment?