## Slide 1: Time Requirement of Immediate Feedback
Date: 2022-6-13
Authors:
Name | Affiliation | Address | Phone | Email
Mengshi Hu | Huawei Technologies Co. Ltd | F3, Huawei Base, Shenzhen, China |  | humengshi@huawei.com
Rui Du |  |  |  | 
Gerile Naren |  |  |  | 

## Slide 2: Immediate Feedback and Delayed Feedback
Immediate feedback and delayed feedback are supported in 11bf.
  The sensing receiver which is a sensing responder shall provide a Sensing Measurement Report frame in the assigned RUs with either results obtained from the I2R NDP of the current measurement instance, when negotiated to deliver immediate feedback reporting, or results obtained from the I2R NDP of the previous measurement instance, when negotiated to deliver delayed feedback reporting. [Ref: 802.11bf D0.1]
Fig. 1 Example of immediate feedback
Fig. 2 Example of delayed feedback (one-instance delay, same measurement setup)

## Slide 3: How to Determine the Feedback Mode (1/2)
A natural idea people may have is that the STA will tell the AP its feedback mode in the Measurement Setup phase according to the measurement setup configuration.
However, to determine the feedback modes, the STA also needs to know (or at least estimate) the given time between the NDP and the Sensing Measurement Report frame it sends. Actually, the time may be very different because of the following reasons:
  The duration of the trigger frame in the reporting phase may be different.
  There may exist other frames or phases between the NDPA phase and the Reporting phase (such as the TF sounding phase, Polling phase).

## Slide 4: How to Determine the Feedback Mode (2/2)
Therefore, only having one binary indication (immediate or delayed) in the Measurement Setup phase seems to be inefficient sometimes.
  It is more reasonable for a STA to tell its time requirement of the immediate feedback in the Measurement Setup phase or in the capability exchange.
  Note: The time requirement of the immediate feedback means the immediate feedback from the STA can be done when the given time is larger than or equal to the required time.
Why is the binary indication inefficient sometimes? (Two reasons are given below)
  The STA tends to choose the delayed report because of not knowing the given time. This conservative way (The given time has to be considered to be very small by the STA, and the mode is chosen on the basis of this estimated given time) is chosen to avoid notifying immediate mode which can not actually be satisfied.
  In the case that the time requirement is a little bit larger than the given time, actually the AP can choose to give a padding to the trigger to achieve the immediate feedback.

## Slide 5: Notification of Time Requirement
To improve the efficiency, the time requirement for a STA to feed back an immediate feedback could be told to the AP in the corresponding Measurement Setup phase.
  The AP could choose whether or not to satisfy the time requirement for immediate feedback dynamically shown as below.
Fig. 1 Example for delayed feedback
  If the actual time is smaller than the time requirement for an immediate feedback, a delayed feedback is used.
Fig. 2 Example for immediate feedback
  If the actual time satisfies the time requirement for an immediate feedback, a immediate feedback can be used.

## Slide 6: Conclusion
A STA can tell the AP its time requirement for the immediate feedback for one measurement setup configuration in the Measurement Setup phase.
  Then the AP can explicitly know when the STA will have the ability to feed back the immediate feedback or delayed feedback.
  Compared with only telling the AP the immediate or delayed modes for one measurement setup configuration, a STA is more easily to be in the immediate feedback mode, which improves the efficiency.
  If only telling the AP the immediate or delayed modes, the STA may easily choose the delayed mode, especially when the feedback size is large.

## Slide 7: SP 1
Do you agree that a STA may tell the AP its time requirement of the immediate feedback for a TB measurement instance corresponding to a measurement setup configuration?
This is an optional feature.
  Y
  N
  A

## Slide 8: Updates in 22/0761r2
How to enlarge the given time between the NDP and the sensing measurement frame?
Add padding in Trigger frames
Add TF sounding phase and other frames between them
etc. (This proposal doesn’t limit the used methods (implementation dependent).)
How to add padding in Trigger frames?
AID12 subfield in a User Info field equal to 4095 (indicating the start of the Padding field, used in 11ax and 11be)
Post-EOF A-MPDU padding
Aggregating other MPDUs in the A-MPDU
etc.
Note: The above padding methods are given in 11ax and 11be. It is common to use Padding for a Trigger frame for different motivations, such as ensuring the MinTrigProcTime shown in 11ax and 11be, and satisfying the EMLSR and EMLMR delay in 11be. [Ref: Padding for a triggering frame]