## Slide 1: PPDU formats for DMG sensing
Date: 2022-05-19
Name | Affiliation | Address | Phone | Name
Rui Du | Huawei Technologies Co. Ltd | F3, Huawei Base, Shenzhen, China |  | ray.du@huawei.com
Yan Xin |  | Ottawa, Ontario |  | 
Naren |  |  |  | 
Mengshi Hu |  |  |  | 

## Slide 2: Outline
Abstract
DMG measurement setup element
PPDU format adopted in bistatic sensing
PPDU format adopted in coordinated bistatic sensing
PPDU format adopted in multistatic sensing
PPDU format adopted in passive sensing
PPDU format adopted in monostatic sensing
PPDU format may be adopted in coordinated monostatic sensing
References
SP

## Slide 3: Abstract
DMG sensing support different types of sensing, e.g. (coordinated) bistatic, multistatic, passive sensing and (coordinated) monostatic.
In this contribution, the PPDU formats (may be) adopted in different types of DMG sensing are discussed and analyzed.

## Slide 4: DMG measurement setup element[1]
The parameters could be exchanged during the measurement setup.
Tx beam information (number, beamwidth, scheduling,…)
Rx beam information (number, beamwidth, scheduling,…)
Burst parameters (intra burst, inter burst,…)
Sensing type
Report type
EDMG TRN parameters, e.g. TRN-M, TRN-P, TRN-N (if a non-EDMG device is involved, TRN-M, TRN-P are reserved and set to 0 and TRN-N indicate the number of repetitions for each receive pattern).
…

## Slide 5: PPDU format adopted in bistatic sensing
Non-EDMG/EDMG BRP PPDU are adopted in DMG bistatic sensing [1].
Both control mode and SC mode PPDU could be considered.
Key information to be exchanged in the bistatic sensing:
Tx beam information (number, beamwidth, scheduling,…)
Rx beam information (number, beamwidth, scheduling,…)
Burst parameters (intra burst, inter burst,…)
Report type
EDMG TRN parameters
…

## Slide 6: PPDU format adopted in coordinated bistatic sensing
Non-EDMG/EDMG BRP PPDU are adopted in DMG coordinated bistatic sensing[1].
Both control mode and SC mode PPDU could be considered.
The bistatic sensing instance request frame and instance response frame are TBD.
Key information to be exchanged in the coordinated bistatic sensing:
Tx beam information (number, beamwidth, scheduling,…)
Rx beam information (number, beamwidth, scheduling,…)
Burst parameters (intra burst, inter burst,…)
Report type
EDMG TRN parameters
…

## Slide 7: PPDU format in multistactic sensing
The multistatic PPDU is an EDMG PPDU that will be transmitted to multiple responders in the multistatic sensing instance[2][3]. Both control mode and SC mode PPDU could be considered.
Key information to be exchanged in the multistatic sensing:
Tx beam information (number, beamwidth, scheduling,…)
Rx beam information (number, beamwidth, scheduling,…)
Burst parameters (intra burst, inter burst,…)
EDMG TRN parameters
Report type
…

## Slide 8: PPDU formats adopted in passive sensing
Non-EDMG/EDMG Beacon are adopted in passive sensing, and there are some other potential PPDU formats that may be considered for passive sensing, e.g.
SSW/Short SSW [6].
Other PPDUs in the ATI or DTI.
Both control mode and SC mode PPDU could be considered.
Key information to be exchanged in the passive sensing:
Tx beam information (number, beamwidth, scheduling,…)
Location of transmitter
…

## Slide 9: PPDU adopted in monostatic sensing
As it is stated in Annex AB in 11ay[4]:
  The PPDU is a valid EDMG or DMG PPDU constructed according to the EDMG or DMG PHY specification, respectively; and
  The STA follows all corresponding medium access rules to transmit the PPDU; and
  The TA field and RA field of the frame in the PPDU are set to the MAC address of the transmitting STA; and
  If case of a Short SSW PPDU, the source AID field and Destination AID field of the PPDU are set to the same value.
Any PPDU could be used for monostatic sensing. So, if a non-EDMG/EDMG sensing capable device plans to perform monostatic sensing by itself, it could follow the rule stated above and send the PPDU it needs.
If monostatic sensing is performed by the device itself(sensing initiator is the device who perform monostatic sensing), there is no need to exchange any information shown in the previous slides.

## Slide 10: PPDU maybe adopted in Coordinated monostatic sensing (1)
Different with all the potential parameters that may be exchanged in the DMG measurement setup request/response, the only information may be exchanged for monostatic sensing in 11bf draft 0.1[7] is Tx/Rx beam information. And the PPDU format in coordinated monostatic sensing is not decided yet.
Theoretically, any PPDU(without TRN) could be adopted for coordinated monostatic sensing. But actually, no matter which kind of PPDU is adopted, sensing is conducted with CEF of the PPDU preamble (which has very good correlation properties). To enhance the sensing efficiency, data part is not needed in the monostatic sensing.
TRN could be adopted to enhance both sensing efficiency and performance (direction switching is performed every N TRN subfields rather than every PPDU, N repeated TRN subfields transmitted with same beam/AWV could be used to improve the SNR).

## Slide 11: PPDU maybe adopted in Coordinated monostatic sensing (2)
If TRN is not considered in coordinated monostatic sensing, it will be very hard for some of the parameters to be negotiated in measurement setup phase. For example,
Burst parameters (intra burst, inter burst,…).
This field is related to (also limited by) the Maximum Doppler field in DMG sensing capabilities field. Usually, the Doppler frequency could be measured with TRN field is greater than the entire PPDU. So, if an application needs to measure greater Doppler frequency, a PPDU with TRN may be needed.
TRN subfield sequence length (not included in the DMG measurement setup element yet, recommend to add).
This field is related to the sensing range (the ZCZ of TRN subfields are different with different length Golay sequences) which is important for different sensing applications.

## Slide 12: PPDU may be adopted in Coordinated monostatic sensing (3)
In general, it is good to adopt PPDU with TRN in the coordinated monostatic sensing, this is also supported in annex AB in 11ay[4]. This will enhance the sensing efficiency and performance.
So, PPDU with TRN is recommended to be considered in the DMG coordinated monostatic sensing. Relevant (TRN related) subfields in DMG measurement setup request/response can be used to negotiate the parameters.
But we do think that there could be a simplified monostatic sensing mode, in which the monostatic sensing is performed with some readily available PPDUs with very good transmitting properties (e.g. DMG beacon, transmitting periodically to different directions). And for this mode, there is no need to exchange some parameters during the sensing measurement setup.

## Slide 13: Summary
PPDUs (may be) adopted in different sensing modes are summarized and discussed in this contribution.
For coordinated monostatic sensing, generally it is better to utilize PPDU with TRN which could provide better sensing efficiency and performance .
A simplified monostatic sensing mode could be considered in 11bf, in which monostatic sensing is performed with some readily available PPDU(e.g. DMG beacon) and there is no need for the exchange of some parameters.

## Slide 14: References
[1] 11-22-0295-05-00bf-pdt-dmg-measurement-setup-frames.docx
[2] 11-22-0327-01-00bf-pdt-bi-static-sounding-and-bpr-frame.docx
[3] 11-21-1865-02-00bf-dmg-multi-static-ppdu-structure.pptx
[4] 11-22-0636-03-00bf-edmg-multi-static-sensing-sounding-ppdu-structure.pptx
[5] 802.11ay-2021.pdf
[6] 11-22-0241-07-00bf-pdt-dmg-passive-sensing.docx
[7] 11-22-0543-00-00bf-pdt-for-dmg-passive-sensing-based-on-a-bft.docx
[8] 802.11bf D0.1.pdf

## Slide 15: SP 1
Do you support to add the following to the 11bf SFD.
For all the DMG sensing types, both control mode and SC mode PPDU should be considered.
Yes
No
Abs

## Slide 16: SP 2
Do you support to add the following to the 11bf SFD.
PPDU with TRN should be adopted in DMG coordinated monostatic sensing, and TRN parameters could be negotiated in the coordinated monostatic sensing.
Yes
No
Abs