## Slide 1: Rule-based Random MAC-Identification proposal (RRCM)

## Slide 2: Abstract
This Document focuses on a specific solution (v3) presented in 22/818r3.
Rule-based Random and Changing MAC Address (RRCM)
  A privacy enhancement mechanism for non-AP STA and AP to generate one or more Random Mac Addresses (RMA) for use by non-AP STA to prevent non-AP STA from being tracked (by third parties) and still allow the non-AP STA to be identified by the AP in subsequent message exchanges. “Rule-based” implies that the non-AP STA and AP apply the same procedures for generating RMA or RMA(s) locally at their sides.

## Slide 3: Background-1
Conventional 802.11 standards are designed in a way that each STA uses its own fixed unencrypted MAC address.
  This causes a privacy concern such as allowing others to track STAs based on their MAC address.
To reduce this privacy risk, using MAC randomization (STAs using random MAC address) became a common technique.
Within this context, 11bh focuses on the identification issue on the STA with Random Mac Address (RMA), and several use cases are defined in 332r37:
  The STA uses a MAC address in the first-time association, and connects to AP.
  After a while, STA disassociates and wants to connect to the AP with a new MAC address (RMA).
  In this scenario, how can AP identify the STA with its new MAC address (RMA) privately?

## Slide 4: Background-2
802.11bh D0.2 provides a device ID solution, which covers use cases that the identification happening after association.
the identification based on probing (pre-association & post-association) is not addressed.
the identification on authentication/(re)association is not addressed.

## Slide 5: Motivation
We propose a “rule-based” mechanism to identify a STA with its random MAC address.
Basic Idea,
  STA and AP generate one or more RMA(s) locally at their sides using,
    Key (RMA key) – locally generated private key
    Seed – exchanged between two sides to feed into RMA generation formula
    Counter – exchanged between two sides to make sure both sides generate the same number of RMA(s)
  The STA will use the generated RMA(s) in its next association. Since AP also generates the same RMA(s), it will identify the STA.
  If STA generates a single RMA -> STA can use it in all message exchanges If STA generates multiple RMA(s) -> STA can use them in different message exchanges (e.g. RMA1 in probe request frame, RMA2 in other frames).

## Slide 6: RRCM Procedure
In current Association,
  STA and AP generate the same key (RMA Key, i.e. RMAK) locally based on KDK (RMAK is not shared).
  RMAK = KDF-Hash-256(KDK, "RMA Key", Min(ANonce, SNonce) || Max(ANonce, SNonce)
    This will output 256 bits RMAK.
  STA behavior:
    STA generates one or more RMA(s) locally –decided by STA- based on:
    RMAn = KDF-Hash-48(RMAK, "Next RMAs", seed || n),
    seed is 128- bit random string n is initialized with 1 and incremented by 1 until n is equal to Counter, which is the number of generated RMA(s). As an example, Counter = 3 -> n=1 :: RMA1, n=2 :: RMA2, n=3 :: RMA3.
    STA sends {Seed, Counter} to AP in encrypted 4-way HS Msg2 (except RRCM IE in Assoc Req for FILS)
  AP behavior:
    AP checks {Counter} to determine how many RMAs it should generate. Then it uses {Seed, Counter} to generate the same RMA(s) that STA generated.
    RMAn = KDF-Hash-48(RMAK, "Next RMAs", seed || n),

## Slide 7: RRCM Procedure
In next Association,
  STA uses the generated RMA(s) freely. As an example,
  STA re-generates {Seed, Counter} and sends them to AP in encrypted 4-way HS Msg2 (except RRCM IE in Assoc Req for FILS).
  AP and STA generates new RMA(s) for future use (next association).
Note: Normally, PTK is partitioned into KCK, KEK, TK. However, when WUR is negotiated, The PTK is partitioned into KCK, KEK, TK, and a KDK. Similarly, when RRCM is negotiated, The PTK is partitioned into KCK, KEK, TK, and a KDK. KDK is used to derive RMAK.
Implementation 1 | Implementation 2
RMA1 for Probe Req (unicast or broadcast) RMA2 for Auth/Assoc/4-way HS/Data Connection | RMA1 for Probe Req (unicast or broadcast) for 3 hours RMA2 for Probe Req (unicast or broadcast) for another 3 hours RMA3 for Auth/Assoc/4-way HS/Data Connection.

## Slide 8: RRCM Procedure
RRCM KDE in 4-way HS (scenarios other than FILS)
      Octets 16 2
RRCM IE in Association Request (for FILS)
      Octets 1 1 1 16 2
Seed | Counter
Element ID | Length | Element ID Extension | Seed | Counter

## Slide 9: RRCM Procedure
Example Diagram (two RMAs generation)
STA1
AP
Prob/Auth/Ass Req/Resp - MAC1
4-way Handshake – MAC1 ({seed, counter} sent in encrypted Msg2 from STA to AP)
PTK::RMAK
PTK::RMAK
Data Connection – MAC1
Disconnect
Prob – RMA1, Auth/Ass Req/Resp – RMA2
4-way Handshake – RMA2 ({seed, counter} sent in encrypted Msg2 from STA to AP)
Data Connection – RMA2
AP receives RMA1from probe req and identifies the STA (i.e. STA1). AP also receives RMA2 from other frames and identifies the STA (i.e. STA1)
Map RMA1, RMA2 -> STA1
RMAn = KDF-Hash-48(RMAK, "Next RMAs", seed || n) where n is the value of counter. [RMA1 = KDF-Hash-48(RMAK, "Next RMAs", seed || 1)
RMA2 = KDF-Hash-48(RMAK, "Next RMAs", seed || 2)]
RMAn = KDF-Hash-48(RMAK, "Next RMAs", seed || n) where n (counter) and seed received from STA. [RMA1 = KDF-Hash-48(RMAK, "Next RMAs", seed || 1)
RMA2 = KDF-Hash-48(RMAK, "Next RMAs", seed || 2)]

## Slide 10: Reference
[1] 802.11bh draft 0.2
[2]11-22-0296-08-00bh-tgbh-proposals.pptx
[3] 11-21-0332-37-00bh-issues-tracking.docx

## Slide 11
THANK YOU 