## Slide 1: TG bh Identifiable Random MAC Address IRMA - 3
Date: 2022-06
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Intro
This new proposal is very simple and sends a random MAAC address, IRMA, in message 4 of the 4 w HS.
STA tells AP what address it will use for the NEXT association.
IRM is a STATION allocated scheme. STA has control over the MAC Address used.
Note that
MAAD is very similar but NETWORK allocated scheme. Network allocates the MAC address to be used (changes every association)
BOTH schemes cover all the Use Cases.

## Slide 3: IRM Definitions
  Identifiable Random MAC (IRM) : a scheme where a non-AP STA uses identifiable random medium access control (MAC) addresses (IRMA) to prevent third parties from tracking the non-AP STA while still allowing trusted parties to identify the non-AP STA.
Identifiable Random MAC Address (IRMA) – a random MAC address used by a STA using IRM

## Slide 4: CAPABILITY BIT
An IRM Capability field is used in the STA and AP

## Slide 5: Outline
STA uses a random MAC address, IRMA
Every time the STA associates, the STA generates a new random address, IRMA and sends to AP
  The STA will use this new Address the NEXT time it associates
AP identifies STA by checking the stored IRMAs.

## Slide 6: Basic Steps for IRM
STA and AP indicates IRM support in Extended Capability Field
First Time Association
STA generates 48 bit random address
  Generates a random 46 bit number
  Appends I/G = 0, U/L = 1 (Compatible with 12.2.10)
STA associates using the random address
During Association,
  STA generates a new random MAC address, IRMA.
  STA sends a new IRMA in message 4
  AP stores this IRMA.

## Slide 7: STA Associates again
Subsequent Associations
STA uses the IRMA it provided at the last association
AP can identify STA pre-association
During Association STA sends a new IRMA to AP in msg 4
AP and STA update their lists.

## Slide 8: Important Points
STA uses a different MAC Address for every association
Effectively the MAC address is the “identifier” BUT only known by the AP.
  Makes adoption by existing Apps easy.
Very simple
NO computations
Works for all Use Cases
Similar to MAAD but STA allocates address

## Slide 9: STA details and Storage
IRM enables the AP to identify the STA,
  i.e. STA “123”
AP can exchange frames or higher layer APP can then associate STA 123 with some other specific details/IDs
  Membership ID , customer ID, guest ID, family member, employee ID, etc.

## Slide 10: IRM element – Optional ??
STA can use “private” address
IRM element sent in Association Request
AP then knows if STA IRMK already known (stored) or not
Not sure if this would be useful. Does inform AP to search for IRMA, or not.

## Slide 11: Straw Poll/Motion
Do you agree that an Identifiable Random MAC scheme, IRMA-3, along the lines as described in <this document>, is included in the TGbh Amendment?