## Slide 1: TG bh Multiple Schemes for TGbh
Date: 2022-06
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Intro
This presentation investigates how selection(s) may be made in the case that multiple solutions for TGbh are adopted
Three schemes considered NGID, MAAD, IRMA
  Note that NGID and MAAD are completely compatible, and AP can decide what to send, ID or MAAD MAC.
  IRMA is similar but is aimed at applications where the STA decides.

## Slide 3: Case 1 – NGID and MAAD
NGID – AP sends an ID once (in msg 3), and STA sends that ID on every association (in msg 2 or 4)
MAAD – AP sends MAC address (in msg 3) every association and STA uses that as TA in the next association
Comments:
Doubtful if both would be used at the same AP
Can we assume that the upper layer APP would decide, i.e., is pre-association desired or not?
Hence, can we assume that AP would only advertise one?
Actually, not a problem if AP advertises both and STA supports both.

## Slide 4: Case 1 – AP and STA support NGID and MAAD
AP decides to use NGID
  STA associates
  AP sends NGID KDE in msg 3
  STA logs the ID and uses it on subsequent associations
AP decides to use MAAD
  STA associates
  AP sends MAAD KDE in msg 3
  STA logs the MAAD MAC and uses it on subsequent associations
Completely compatible – no special selections required
STA should support NGID and MAAD, but AP can either support one or both.

## Slide 5: Case 2A – NGID, MAAD and IRM STA controls
Need to make decision on whether STA or AP controls. First assume that STA controls.
i.e., STA makes the decision. Leave it to the AP or use IRM.
AP and STA support NGID, MAAD and IRM
  If STA decides NGID or MAAD, i.e., leaves it up to AP
    STA associates and waits for msg 3, ID or MAAD MAC (as per case 1)
  If STA decides IRM,
    STA associates and sends IRMA in msg 2
    AP sees msg 2 and does not try to send a KDE in msg 3

## Slide 6: Case 2B – NGID, MAAD and IRM AP controls
Assume that AP controls.
AP and STA support NGID, MAAD and IRM
  If AP decides NGID or MAAD, STA associates and waits for msg 3, ID or MAAD MAC (as per case 1)
  If AP decides IRM,
    STA associates
    AP does not send KDE in msg 3
    STA does not see KDE in msg 3 so sends IRMA in msg 4
If IRMA KDE is sent in msg 2, STA controls,
if IRMA KDE is sent in msg 4, AP controls

## Slide 7: Solution 1 – fix msg for IRMA KDE
Fix whether AP or STA controls by fixing in Standard in which msg IRMA KDE is sent.
  If IRMA KDE is specified to be sent in msg 2, the STA effectively controls
  If IRMA KDE is specified to be sent in msg 4, then AP controls
The first KDE received wins
  If AP sees KDE in msg 2, it will not send a KDE in msg 3
  If STA sees KDE in msg 3, it will not send KDE in msg 4
This simple solution works for all combinations

## Slide 8: Solution 2 - leave it up to STA for IRMA
STA controls if it wants to use IRMA by sending IRMA KDE in msg 2.
If STA wants AP to decide, and no KDE in msg 3 (NGID or MAAD) then STA sends IRMA KDE in msg 4
The first KDE received wins
  If AP sees KDE in msg 2, it will not send a KDE in msg 3
  If STA sees KDE in msg 3, it will not send KDE in msg 4
This simple solution works for all combinations

## Slide 9: What should AP and STA support?
We can assume that the Network should know which solution is required from the Application or Use Case: NGID or MAAD.
  E.g., if pre-association required or not.
  Both use msg 3 and clear which is in use
    NGID KDE or MAAD KDE
If there is no interest in the STA having control, then strong case to be made for just NGID and MAAD.
Only if there is interest that the STA should be able to control, i.e., use IRMA, do we need to include the IRMA scheme.
    OR leave IRMA KDE in msg 4, then AP always controls, but would it ever use it as MAAD does the same thing, pre-association-wise

## Slide 10: Simple Proposal
We should just include NGID and MAAD.
AP can support either or both
STA should support both.
Completely compatible, AP elects the one that suits better the Use Case or APP.

## Slide 11: Straw Poll
Should TGbh allow for the non-AP STA to make decision on RCM mitigation scheme?
Y/N/A

## Slide 12: AUTOMATIC for RSNA association
There is no requirement for any selection process.
NGID and MAAD are joined at the hip and AP can decide which to use (presumably based on the upper layer APP, i.e., does it want pre-association?)
IF STA controls when to use IRM, IRMA KDE is sent in msg 2
or if we decide that AP controls:
IRMA sent in msg 4.
Hence, comes down to the text, IRMA in msg 2 or msg 4?
The three solutions are completely compatible for RSNA association.
(will look at FILS once we have decision on STA/IRM)