## Slide 1: TG bh Multiple Schemes for TGbh
Date: 2022-06
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Intro
This presentation investigates how selection(s) may be made in the case that multiple solutions for TGbh are adopted
Three schemes considered NGID, MAAD, IRM
  Note that NGID and MAAD are completely compatible, and AP decides.
  IRMA is similar but the STA decides.

## Slide 3: Case 1 – NGID and MAAD
NGID – AP first sends an ID (in msg 3), and STA sends that ID on every association (in msg 2 or 4)
MAAD – AP sends a new MAC address (in msg 3) every association and STA uses that as TA in the next association
NOTE:
Both can be used together
  Pre-association and STA provides the ID each time
OR
AP decides which to use
  assume that the upper layer APP would decide, i.e., is pre-association desired or not?

## Slide 4: Case 1 – AP and STA support NGID and MAAD
AP decides to use NGID only
  STA associates
  AP sends NGID KDE in msg 3
  STA logs the ID and sends it in msg 4 it on subsequent associations
AP decides to use MAAD only
  STA associates
  AP sends MAAD KDE in msg 3
  STA logs the MAAD MAC and uses it on subsequent associations
AP decides to use both, NGID AND MAAD
  STA associates
  AP sends NGID KDE and MAAD KDE in msg 3
  STA next associates using the MAAD MAC and sends ID in msg 2 or 4 and AP sends new MAAD MAC in msg 3.
  Completely compatible no selection mechanism required

## Slide 5: Case 2 – NGID and IRMA
NGID – AP first sends an ID once (in msg 3), and STA sends that ID on every association (in msg 2 or 4)
IRMA – STA sends a new MAC address (in msg 2 or 4) every association and STA uses that as TA in the next association
NOTE:
Both can be used together or just one.
  Pre-association with identifiable MAC and STA provides the ID each time

## Slide 6: Case 2 – AP and STA support NGID and IRM
AP decides to use NGID
  STA associates
  AP sends NGID KDE in msg 3
  STA logs the ID and sends it in msg 4 it on subsequent associations
STA decides it wants to use IRM (not NGID)
  STA associates
  AP sends KDE in msg 3
  STA sends IRMA KDE in msg 2 (or 4) and does not send NGID KDE Note that STA always has option not to send the ID
Use both, NGID AND IRM
  STA associates
  STA sends IRMA in msg 2 (or 4)
  AP sends NGID KDE in msg 3
  STA next associates using the IRMA and sends ID and IRMA KDE in msg 2 or 4
  Completely compatible no selection mechanism required

## Slide 7: Case 3A – NGID, MAAD and IRM STA controls
Obviously cannot have IRM and MAAD together
Consider that STA controls i.e., STA makes the decision.
(Some) STAs may not like being told a MAC address to use – they prefer to choose it.
AP and STA advertise support for NGID, MAAD and IRM
  STA decides NGID and IRMA
    STA associates, sends IRMA KDE in msg 2
    AP sees msg 2 IRMA KDE and does not send MAAD KDE in msg 3
    AP sends NGID in msg 3
  STA decides NGID and MAAD
    STA associates,
    AP sends MAAD KDE and NGID in msg 3
Note that STA always has choice to use NGID or not, i.e., can ignore and not send ID.

## Slide 8: Case 3B – NGID, MAAD and IRM AP controls
Assume that AP controls.
AP and STA support NGID, MAAD and IRM
  If AP decides NGID or MAAD,
    STA associates and sees MAAD MAC in msg 3, ID or (as per case 1)
    STA does not send IRMA KDE in msg 4
  If AP decides IRM,
    STA associates
    AP does not send KDE in msg 3
    STA does not see KDE in msg 3 so sends IRMA KDE in msg 4
Hence,
If IRMA KDE is sent in msg 2, STA controls,
If IRMA KDE is sent in msg 4, AP controls
We can simply make decision.

## Slide 9: Solution for MAAD or IRMA – fix msg position for IRMA KDE
Fix whether AP always or allow STA controls IRM or MAAD by fixing in Standard in which msg IRMA KDE is sent.
  If IRMA KDE is specified to be sent in msg 2, the STA effectively controls
  If IRMA KDE is specified to be sent in msg 4, then AP can controls
The first KDE received wins
  If AP sees KDE in msg 2, it will not send a KDE in msg 3
  If STA sees KDE in msg 3, it will not send KDE in msg 4
This simple solution works for all combinations

## Slide 10: What should AP and STA support?
AP only
We can assume that the Network should know which solution is required from the Application or Use Case – NGID and MAAD.
  E.g., if pre-association required or not. (i.e., MAAD or IRMA desired)
  Both use msg 3 and clear which is in use
    NGID KDE or MAAD KDE
If there is no interest in the STA having control, then strong case to be made for just NGID and MAAD.
STA allowed
However, if some STAs want to control their MAC Addresses (not happy to be allocated a MAC Address as in MAAD), then NGID, MAAD and IRMA should be supported
    IRMA KDE in msg 2, then STA decides MAAD or IRMA

## Slide 11: AP and STA Proposal
Propose we set IRMA in msg 2, the AP is still effectively in control, but STA, if it wants can choose IRM over MAAD;
AP advertises NGID only – then NGID only it is
AP advertises NGID and MAAD - does not allow IRM
AP advertises NGID and IRM – AP lets STA do IRM
AP advertises NGID, MAAD & IRM – AP OK if STA chooses IRM
STA should advertise support as follows:
NGID and MAAD – cover all use cases but OK with AP setting the MAC address
NGID and IRM – STA wants to set its MAC address
NGID, MAAD and IRM – STA can select according to the network

## Slide 12: Simple Solution
If TG agrees that STA should sometimes make decisions, then draft could include NGID, MAAD and IRMA (Case 2)
  IRMA KDE is then sent in msg 2
All combinations of schemes in AP and STA are then straightforward.
SIMPLE,
NO NEGOTIATIONS,
NO COMPUTATIONS

## Slide 13: Straw Poll 1
Given that multiple schemes can be easily be accommodated, should TGbh include more than one scheme such that pre-association use cases may be addressed?
Y/N/A

## Slide 14: Straw Poll 2
On the understanding that some STAs may not want to have their MAC Address allocated for them, but others are OK with that, should TGbh include a “pre-association” scheme where the STA can choose to allocate its MAC address?
Y/N/A
Note 1: For example, in the MAAD scheme the AP allocates the MAC address for the STA to use the next association, whereas in the IRM scheme, the STA tells the AP what MAC address the STA will use in the next association. Should TGbh cater for both these options (answer Yes) or just allow the AP to decide (answer No)?
Note 2: Even if STA is allowed to choose the scheme, it may still choose to let the AP allocate the MAC address (see slide 7)

## Slide 15: Straw Poll 3
Given that the NGID, MAAD and IRM schemes can all be supported together, with no negotiation required, do you support going forward with these schemes for the TGbh draft?
Y/N/A
Note 1: Amend or run this Straw Poll 3 accordingly based upon Straw polls 1 and 2.
Note 2: Text exists for each scheme (MAAD and IRM) and new text will be written to explain how they co-exist and how they work together, as per this presentation and the Straw Polls.