## Slide 1: TG bh Pre-association in TGbh - Probes
Date: 2022-07
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Intro
22/0908r1 considered three schemes NGID (device ID), MAAD, IRM
  All schemes can exist together with no negotiations, calculations or computations
  MAAD and IRM are schemes to meet the pre-association Use Cases.
22/0933r2 “compared” the RRCM scheme to MAAD and IRM
  RRCM can derive multiple addresses used for probes and association
  Note: So can MAAD and IRM.
Questions were made about how Probes and MAC addresses were used with these pre-association schemes
This presentation discusses how Probes are used and if different addresses are required.
By trying to cover this is detail there is a danger that it will seem that this is a complex item. It is not, but I am trying to cover all the areas and questions that inevitably will come up.

## Slide 3: MAAD IRM RRCM Outlines
MAAD – AP sends a new MAC address (in 4-way HS msg 3) every association and STA uses that as TA in the next association
IRM – STA sends a new MAC address (in 4-way HS msg 2) every association and STA uses that as TA in the next association
    IRM was proposed as some members indicated they wanted an option for the STA to choose the MAC address, rather than it being allocated for them
RRCM – STA sends a seed (16 octets in 4-way HS msg 2) in each association, then AP and STA, using PTK, independently generate one or more MAC addresses to be used in next association.
    RRCM can generate that multiple addresses from same seed.
Note – Nothing stopping MAAD or IRM from allocating more than one address.

## Slide 4: Broadcast Probes
Active Broadcast
  Looking for networks in range.
  No reason why STA should use the identifiable address, would use an RMA (random MAC address)
  STA may use broadcast probes to find a network
  BUT
  STA is ill-advised to use an identifiable address in a broadcast probe – no requirement to do so, anyhow, and why would it?

## Slide 5: Active Directed Probes
  Looking for a specific AP/network. (Maybe already found using broadcast)
    A STA probing with same TA over time and area is definitely trackable, so don’t do it
      Why use identifiable address? Why even use a fixed address? Definitely discouraged and not required.
  Is there ever any reason to use an identifiable TA in a directed Probe?
    Are there APs that will not respond if they don’t know who it is?
    Use Cases for steering?
      If STA knows it is in vicinity of the network, then probing with identifiable TA is OK.

## Slide 6: Probing in vicinity of Network
  If in the vicinity of the network*, then is it trackable?
  If STA probes with same address as it Associates with – there is no problem?
    All listener knows is that a STA probed and associated – so what?
    Listener will NEVER see that address AGAIN in that area, AND
    Listener will NEVER see that address AGAIN if monitoring a large area. (If it did, it is highly probable it is a different STA anyway).
The allocated random MAC address contains no identity to STA
Not even a need to use a second identifiable address.
*Determined by Passive or active (with RMA) scanning, or directed by network for steering purposes

## Slide 7: Is there a need for Multiple Addresses?
RRCM’s can generate a number of addresses each time. (Needs further computations, KDE ‘seed’ plus ‘counter’ 18 octets)
  e.g., RMA1 in probe request frame for 3 hours then use RMA2, then use RMA3 in other frames (Association)
  No rule defined
MAAD and IRM could simply send 2 (or 3) addresses each time - (still only 12/18 octets) no computations.
  STA could then use one address for probes and other for associations.
BUT WHY?
Is the overhead worthwhile? Let’s look at the Use Cases

## Slide 8: Use Case 4.1 – Pre-Association client steering
“Before connecting to the 802.11 network, the phone scans to discover the available APs, by sending Probe Requests.
…infrastructure monitors the signal levels …at multiple APs and bands … determines which AP and band will provide the best service, and steers the client to that AP.”
Discussion:
STA could/should use an RMA for the probes in order to find the network,
STA knows it is in vicinity so probing with identifiable TA is now not a problem.
No real need for a different TA for the probes.
  .

## Slide 9: USE Case 4.2 – During association (parental controls)
“devices to be recognized when attaching to the 802.11 network and control access to Internet content based on the user…”
“…unknown devices need to be distinguishable from one of the approved devices.”
Discussion
STA recognized by MAC Address in Association Request.
AP can decide whether to respond or not etc.
No need for multiple addresses. No specific probes required in this Use Case.

## Slide 10: Use Case 4.8 - Infrastructure
“if the client uses the stable MAC address when probing, the infrastructure can help steer the client across both APs and bands, to give the entire network better experience.
The associated AP sends a Beacon request frame to instruct the STA to send the probing on the target APs’ operating channel”
Discussion
In this case STA knows it is “in the vicinity” , as it is “instructed” to send probes,
hence
This is not a problem, as already noted, probing and associating using same address in one vicinity, is not trackable.
  If a STA is in an area of a network, then no real benefit to a third party knowing that. The STA will return with a different address, and listener has no idea who it is.

## Slide 11: Use Case 26 – Vitual BSSID
“Follow the user.
A given client device is “assigned” a generated BSSID. That BSSID moves from AP to AP within an ESS, to manage the client transitions.
The device is recognized by the APs in multiple-AP infrastructure via its MAC address in the probe request frame, so that the APs generate a unique BSSID for the device to set up wireless connection.”
Discussion
Requires identifiable address in probe and associations (I think).
No problem as this is the same “vicinity” condition.
If you really, really want 2 addresses, this particular network could simply allocate 2 addresses using MAAD (way easier than generating 2 RMAs with RRCM).
  The network knows what it wants, so MAAD would be used here.

## Slide 12: ANQP
ANQP is used by a STA to find out what services are offered and if it wants to connect.
Pre-association identification may be useful
  Offers based on knowledge of who STA is
But mainly post association ID (Device ID useful here) so could associate with any RMA. Not clear if this is a pre-association case at all.
Aside: STA has been there before, might use ANQP to see what’s on offer? But doubtful. It would simply associate.
Anyhow, do not see need for different identifiable addresses in GAS frames and association. (Same tracking argument as previous)

## Slide 13: Probe “rules”
General rule is to use passive probing
Broadcast Active probes can be used when simply looking. Hence should use RMA.
Direct probes should still as a rule use RMA.
  Probing for a network over time and area should never use same TA even if an RMA.
If STA knows it is in the vicinity of known AP/network it could use the identifiable address IF it wants the network to recognize it, steer it, BEFORE Association Request.
  STA could use directed probes with identifiable address No real problem even if same address used for association.
  Listener notes a STA is probing and associating BUT NEVER sees that address again – so nothing to track!

## Slide 14: Conclusions - 1
General rule – use RMAs in probes.
The important point is that even if a STA used the same (allocated) address in probes and association, while in vicinity of AP, still not trackable. Address changes next time STA comes back and associates OR goes anywhere else.
  Address changes every association.
Can’t see any good reason to have multiple recognizable addresses allocated.

## Slide 15: Conclusions - 2
22/0908r1 showed how Device ID, MAAD and IRM simply co-exist, complementing each other and allowing the AP to either:
  allow the STA to choose (AP Supports Device ID, MAAD and IRM)
  or not, (AP only supports Device ID and MAAD).
provides full flexibility with pre-association plus ID recognition
The MAAD MAC or IRMA work just fine and are secure and untrackable even if used with directed Probes in identified Use Cases.