## Slide 1: Reply to 11-22/0831r0
Date: 2022-07-14
Authors:

## Slide 2: Abstract
This presentation contains questions and answers related to the 802.11 working group letter ballot of TGbb. Answers to the questions are in italic letters. In case draft text is reused, it has been updated to most recent D2.1 of TGbb.

## Slide 3: LC STA
An LC STA is a STA with an OFE.
An LC STA is either an LC HT STA or an LC VHT STA or an LC HE STA. An LC HT STA consists of an LC HT PHY and an HT MAC. An LC VHT STA consists of an LC VHT PHY and a VHT MAC. An LC HE STA consists of an LC HE PHY and an HE MAC.
Simultaneous or separate communications using RF and LC PHYs is supported in multi-band capable devices (see 4.9.4 (Reference model for multi-band operation)). Simultaneous use of multiple transmit chains and multiple receive chains within the LC PHY is supported per 32.3.5 (Multiple transmit chains and multiple receive chains).

## Slide 4: LC Light Interface Example
  The HT, VHT or HE TX signal is down-converted from RF to LC IF signal and transmitted transparently over LC channel.
  The signal received from the LC channel is up-converted from LC IF to RF and detected by using the HT, VHT or HE RX.

## Slide 5: LC-STA - Observations
Is there any channelization applicable to the LC range? Is it needed?
How the proposed mapping (Clause 32.3.4) is performed?
  the concept is the same like block conversion in a satellite low noise block (LNB) RX
  a fixed radio frequency is used to up- and down-convert a block of adjacent 802.11 channels from 5 and 6 GHz band and transport it transparently by using the resulting LC IF signal
  for details which channels are used over LC, refer to 32.3.4 in TGbb D2.1

## Slide 6: LC STA MAC
31. 31.2 LC MAC specification
The MAC of an LC HT STA shall consist of an HT MAC. The MAC of an LC VHT STA shall consist of a VHT MAC. The MAC of an LC HE STA shall consist of an HE MAC.
Yes, this is true.
LC uses the HT, VHT and HE waveforms in a transparent manner over the LC channel.
I.e., the existing MAC features are fully reused.
Likewise, future features may be supported.
This is entire MAC Clause

## Slide 7: LC STA MAC - Observations
Is the Beacon frame sent by the LC STA?
  Yes
Is there an LC Capability IE?
  No.
What about the other MAC functions – Association, De-Association, probe Request/Response, Power management, Channel Switching, media access, etc.
What about other specific MAC functions – Bandwidth Signaling, Two NAV Counters, Spatial Reuse, Quiet Time, etc.
Security
  All the three above are the same as in the HT, VHT and HE MAC.

## Slide 8: LC HT PHY
In the LC HT mode, data subcarriers are modulated using binary phase-shift keying (BPSK), quaternary phase shift keying (QPSK), 16-quadrature amplitude modulation (QAM), and 64-QAM. Forward error correction (FEC) ccoding (convolutional coding) is used with a coding rate of 1/2, 2/3, 3/4, or 5/6. Low-density parity-check (LDPC) coding is included as an optional feature. The LC HT mode provides support for 20 and 40 MHz contiguous channel widths.
The LC HT mode PHY shall be the same as Clause (High-throughput (HT) PHY specification) and behavior specified for a HT STA shall apply to an LC STA using the LC HT PHY mode, except when the specifications in 32.3.2.2 (LC High Throughput (LC HT) mode) supersede corresponding text in Clause 19 (High-throughput (HT) PHY specification).
The subclause 19.3.14 (Regulatory requirements) does not apply to the LC HT PHY mode. For channel numbering, refer to 32.3.4 (Channel numbering).
(similar for VHT and HE, see D2.1)

## Slide 9: LC STA PHY - Observations
Are timing related constants (Table 19-6, Table 21-5) still applicable?
  Yes
Is there a need for TXVECTOR/RXVECTOR?
  Same as for HT, VHT and HE
RU sizes supported similar to HE?
  All the same.

## Slide 10: 802.11af (White Spaces (TVWS) OPeration)
802.11af is based on VHT PHY and MAC
  802.11af purpose is operation of 802.11 in TV white space. This means operating WLAN as secondary user in spectrum owned by a primary user (broadcasting). This implies that certain conventions (e.g. channelization) in the TV spectrum are also satisfied by 802.11af PHY. Moreover, the 802.11af MAC needs to sense the radio utilization and is allowed to transmit only in case the primary spectrum can be considered unused. Therefore, substantial changes were needed in both, 802.11af PHY and MAC.
  There is no such constraint for LC, as LC operates in unused optical spectrum. Thus, the existing channelization from 802.11 can be reused. Of course, LC IF frequencies have to be standardized. Also the 802.11 MAC can be reused. 802.11bb adds an optional LC repetition mechanism allow the existing CCA mechanism to be used within non-AP LC STAs with the assistance of the LC AP. Also the realization of MIMO over LC has been specified.
802.11bb should follow the example of 802.11af
  Indicate what HT, VHT, HE features are supported - all
  Specify any new features applicable to LC STA – none, except operating in optical spectrum
  What changes in the PHY needed to support the LC STA band – operation of 802.11 on LC IF signal

## Slide 11: Last Word
Draft D2.0 is more than an implementation agreement
  It agrees to build LC based on previously approved specifications (LC HT STA, LC VHT STA, or LC HE STA).
  It describes the new features to be agreed upon between different vendors
    Transparent operation of 802.11 over LC
    Channelization on the optical spectrum
    MIMO operation of 802.11 over LC
    LC repetition mechanism to aid CCA in 802.11 MAC

## Slide 12: References
IEEE P802.11bb™/D2.1 June 2022