## Slide 1: 802.11 standard use of 802 architecture
Date: 2022-07-11
Authors:

## Slide 2: Abstract
This presentation summarizes IEEE Std 802.11™-2020 use of the IEEE Std 802 Overview and Architecture, for discussion at the 2022-07-11 802 Technical Plenary Tutorial meeting.
Use of the LLC, MAC address formats, QOS mechanisms and MSDU formats are described.
Extracted text is from IEEE Std 802.11™-2020

## Slide 3: 802.11 MAC Services support LLC sublayer entities
LLC sublayer entities or IEEE 802.1Q bridge ports can use the 802.11 service to exchange MAC Service Data Units (MSDUs)

## Slide 4: All 802.11 MAC Services and protocols use 48-bit MAC addresses
48 bit MAC addresses are used (See 9.2.2)

## Slide 5: Quality of Service via User Priority is supported
While the reference to 802.1D is being removed, the functionality remains

## Slide 6: Several QoS management mechanisms are specified in the 802.11-2020 standard
Including:
802.11e EDCA Access Categories: Voice, Video, Best Effort, Background; widely implemented as WFA WMM
Stream Classification Service (initial specification dates to 2009)
Traffic Classification (TCLAS) based on L3 parameters (IPsec Security Parameter Index ) and MAC layer parameters
Use Multiple TCLAS elements to define SPI, IP Address, Ports
Mirrored Stream Classification Service: Client devices direct the AP QoS marking of downlink IP flows (useful when DSCP markings not present)
QoS MAP feature: L2 priority based on L3 DSCP marking in IP headers
* Many of these mechanisms have WFA interoperability certification.

## Slide 7: Both Logical Link Control (LLC) Protocol Discrimination (LDP) and Ethertype Protocol Discrimination (EPD) are supported
LDP is generally used;
EDP used in:
802.11p/bd (Vehicular)
802.11ak (General Links) for 802.1Q bridge port links

## Slide 8: Figure 5-1 shows the MAC Data Plane architecture, including use of 802 entities, including 802.1X

## Slide 9: Summary: The 802.11 standards uses several components of the 802 architecture
Use of the LLC, MAC address formats, MSDU formats: enable straightforward implementation of devices with Ethernet and IETF IP based protocols
QOS mechanisms are based on defined UPs
The 802.1X Security framework is used, enabling use of IETF EAP protocols and multiple credential types
802.11 uses the 802.1AC definitions of the MAC Service, enabling use of other 802.1-defined facilities, in addition to providing the expected and standardized MAC SAP interface

## Slide 10: References
IEEE Std 802.11™-2020, see https://ieeexplore.ieee.org/document/9363693