## Slide 1: NS-3 Working Group on WiFi: An Update on 802.11ax and .11be Models
Date: 2022-07-14
Authors:

## Slide 2: Abstract
Introducing the NS3W Group, focused on research on Wi-Fi with the aid of the ns-3 network simulator.

## Slide 3: Current usage of simulation results
Packet-level simulations are often used to evaluate proposed new 802.11 features
The code of the simulator is not publicly available
  Often, companies maintain their own customized version of ns-3
Results are not easily reproducible
Difficult to verify and validate the presented results

## Slide 4: Open source ns-3
Code is publicly available
  Existing code can be inspected by everyone
  New code is publicly reviewed
  No duplicate efforts to implement new features
Community helps testing and finding bugs
  About five 802.11ax bugs were fixed in last months after user reports
But ns-3 was running much behind the IEEE standard
  Support for a new amendment came months/years after the publication of the standard

## Slide 5: The NS3W Group
In March 2021, the NS3W group was formed to conduct research on Wi-Fi by leveraging the ns-3 network simulator
Membership from industry and academia
Founding members/new members
Intel | Univ. of Washington
Cisco | Univ. of Napoli
Apple | UPF Barcelona
MaxLinear | Univ. of Delaware
 | Georgia Tech

## Slide 6: The NS3W Group
Companies provide
  Funding
  Directions for current/future research
  Insights on specs interpretation & implementation choices
  Code review (optional)
Universities
  Propose projects
  Periodically (bi-weekly) share updates on project progress

## Slide 7: NS3W Group: achievements
Developed code eventually is merged into the open source ns-3 (at the discretion of the Group)
Many 802.11ax features were merged shortly after the publication of 802.11ax-2021
  DL OFDMA (three ack sequences)
  UL OFDMA (Basic TF, BSRP TF, Multi-STA Block Ack)
  Spatial Reuse (OBSS-PD)

## Slide 8: NS3W Group: achievements
Many other features are in development/being merged into the open source ns-3
  Per-20 MHz channel sensing and dynamic bandwidth operation
  Dual NAV
  MU-MIMO (both DL and UL), including CSI feedback protocol
  PowerSave mode
  TWT (both Individual TWT agreements and broadcast TWT schedules)

## Slide 9: NS3W Group: achievements
Work is already ongoing to support new 11be features
  Node architecture has been redesigned to support Multi-Link Operation
    First two merge requests already merged
  Multi-Link discovery
  Multi-Link setup
  EHT PPDU formats

## Slide 10: NS3W Group: achievements
Code and project updates are shared within the group
Companies are not prevented from developing their own logic for internal use
  Multi-User Scheduler to select among SU, DL MU and UL MU transmissions
  Association Manager to select the links a non-AP MLD requests to setup
  TWT AP Manager and TWT STA Manager to define the behavior of TWT requesting/responding STA and TWT scheduling AP/scheduled STA

## Slide 11: NS3W Group: achievements
Projects not necessarily have to implement standard features
  2021 project on multi-AP coordination (C-TDMA and C-OFDMA)
Universities can use the developed features to carry out research works
  Following slides illustrate sample simulation results obtained with the enhanced ns-3 simulator

## Slide 12: OFDMA impact on latency
S. Avallone, P. Imputato, G. Redieteab, C. Ghosh and S. Roy, "Will OFDMA Improve the Performance of 802.11 Wifi Networks?," in IEEE Wireless Communications, vol. 28, no. 3, pp. 100-107, June 2021, doi: 10.1109/MWC.001.2000332.
Single BSS, 40 MHz channel, 40 stations, MCS 11, non-saturated conditions (100 Mbps [left] or 125 Mbps [right])

## Slide 13: OFDMA impact on throughput
S. Avallone, P. Imputato, G. Redieteab, C. Ghosh and S. Roy, "Will OFDMA Improve the Performance of 802.11 Wifi Networks?," in IEEE Wireless Communications, vol. 28, no. 3, pp. 100-107, June 2021, doi: 10.1109/MWC.001.2000332.
Single BSS, 40 MHz channel, MCS 11, saturated conditions (data rate = PHY rate), DL only [left] or DL+UL with MU EDCA Param Set [right]

## Slide 14: MU EDCA Timer impact on throughput
D. Magrin, S. Avallone, S. Roy, and M. Zorzi, "Performance Evaluation of 802.11ax OFDMA through
Theoretical Analysis and Simulations," in IEEE Transactions on Wireless Communications, under revision.
Single BSS, equal number of HE stations and legacy stations

## Slide 15
Questions?