## Slide 1: Opt-in or opt-out from the STA ID
Date: 2022-07-11
Authors:
11-22-1084-00-00bh-STA ID-Opt-in-IEEE-4

## Slide 2: Abstract
IEEE802.11bh has completed the comment collection (CC41). Several comments have been made with regards to STA ability to opt-in to being uniquely identified by a network.
This slide-set defines signalling for a STA to opt-in to or opt-out from the STA identifier.
The proposal paves the way to comply with regulations such as GDPR.

## Slide 3: End User Consent
The end user should always provide consent to use device ID in a network
  The end user makes conscious decision to allow STA to be tracked by the network
  By default, the STA disables use of the network ID
The 802.11bh D 0.2 spec needs a mechanism to communicate the end user consent to the MAC-layer
  Currently, the draft just says that STA may opt-in without including the user consent

## Slide 4: Communicating the End User Consent within a user device
The 802.11bh D 0.2 spec needs a mechanism to communicate the end user consent to the MAC-layer
  One possibility is to use Management Information Base (MIB) Control variable dot11UserConsent
The dot11UserConsent variable carries a Boolean user consent
  True = The STA uses Device ID
  False = The STA does not use the Device ID

## Slide 5: Current Status
Identifier is created by the network and assigned upon association in M3 of 4-Way HS
The 802.11bh has no means to signal the end user consent whether it desires to be tracked by the network

## Slide 6: The user consent should be signaled to AP
Current draft has does not allow the STA to signal the user consent to the AP
This causes the following disadvantages:
  AP will provide Device ID even if not desired by the STA
  AP memory and computation power is consumed unnecessarily, even if the STA is not planning to use the Device ID
  STA can just ignore the Device ID, but no control whether it wants to receive and use the ID (OPT-IN)

## Slide 7: Proposal: Opt-in Mechanism
This proposal modifies the Device-ID element to include a field that can be used to Opt-in to Device Identification
By default, the STA should opt-out from Device Identification
  Only if the STA explicitly allows Device ID allocation for itself, then it should get the Device ID

## Slide 8: First time association to a network
When user first selects to associate with the network, the user only has a list of networks
  Only after association and authentication the user knows whether it can use the network. Example: Captive Network T&Cs
Network should explicitly provide what information it will collect or how it will profile a STA based on any assigned identifier
The user should provide explicit consent whether the user desires the STA to be remembered by the network
  Further, the user may not be ready to consent immediately as part of the first association
  User Opt-in may be communicated via Robust Management Action Frames (Slide 13)

## Slide 9: Proposal: Addition to Device Id Element
Reserved
(6 bits)
Device ID Element
Opt-in (1 bit):
  0b1 = Opt-in;
  0b0 = Opt-out of network identification
Clear Data (1bit):
  0b1= delete all STA information, 0b0 otherwise
ID Blob (variable length): Identifier assigned by network during previous association
Element ID Extension
Length
ID Blob
Opt-in Control
Element ID
Opt-in (1 bit)
Clear Data (1 bit)

## Slide 10: Proposal: Opt-in/Opt-out during Association
Device ID element encapsulated using KDE in M2 message of 4way-HS
STA Opt-in
STA Opt-out
  No Device ID Element
Element ID Extension
Length
ID Blob = Empty
Opt-in bit = 0b1
Element ID
Element ID Extension
Length
ID Blob = Empty
Opt-in bit = 0b0
Element ID

## Slide 11: Opt-in during Re-assoc
Device ID Element sent in M2 message of 4-way HS
  Includes previously assigned identifier
  AP re-uses previously assigned identifier as per protocol defined in prior proposals
Element ID Extension
Length
ID Blob
Opt-in bit = 0b1
Element ID

## Slide 12: Proposal: Opt-out on DeAuth/Disassoc
A STA should be able to signal in disassociation or de-authentication frame whether it will use the allocated STA ID at the next association
If the STA will not use the Device ID:
  The AP may erase the Identifier and related information
  The STA will not use the same ID blob in the next association
  STA can use RCM on subsequent associations
Element ID Extension
Length
ID Blob
Opt-in bit = 0b0
Element ID

## Slide 13: Opt-in Post-Association
STA may choose to opt-in to accept Device ID post-association by using Robust Management Action Frame

## Slide 14: Opt-out Post-Association
STA may choose to opt-out to accept Device ID post-association by using Robust Management Action Frame

## Slide 15: Identifier Protection
Transmission of identifier in M2 ensures that the ID blob within KDE can be encrypted
DeAuth/Disassoc can be protected using Management Frame Protection
ID Blob in Management Action Frames are protected by the use of Management Frame Protection

## Slide 16: Clear Data Bit
STA can ask network to delete data collected using the identifier at any time
To do so, STA can set the Clear Data bit (Slide 3) in the Device ID Element in any of the following frames and transmit to AP as permitted by 802.11
    M2 Message of 4-way Handshake
    DeAuth/Disassoc Message
    Robust Management Action Frame

## Slide 17: Summary
Use of Opt-in mechanism allows STA to make a clear choice about when to use an identifier
  Allows binding between STA behavior and user consent
Use of clear data bit enables methods for compliance with regulations in some regions