## Slide 1: TGme Clause 6 re-write
Date: 2022-07
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Intro
CID 1114
“What purpose is Clause 6 performing in particular 6.3? 434 pages? As big as Clause 11. I suggest that Clause 6 be investigated as to usefulness and necessity. Too much of it is purely boilerplate and never gets used.
A presentation 21/1822 was originally made in ARC prior to the comment. ARC members indicated strong support to do something hence the comment was subsequently submitted.

## Slide 3: Background:
In writing some proposed new text for a number of request / response exchanges, I realized I needed to add text to Clause 6. I then went through the “boiler plate” routine of writing descriptions for each request, plus the response, plus the indication plus the confirm. 10 pages later I started to think.
I noticed that Clause 6 consumes 434 pages
MORE THAN Clause 11 (398 pages) !!!
Boy, this must be good stuff, thinks I… then I realized that what I am adding, in fact, has no real value that I can see and was obvious from the text and frames.
Hence, I gave myself the task of looking into this Clause further.
I am informed that it all comes from ITU-T X,210 dated 11/1993, in particular Clauses 6 and 7.

## Slide 4: 6.3 MLME SAP interface
“These services are described in an abstract way…and do not imply any particular implementation….
MLME SAP primitives are of the general form
  ACTION.request primitive,
    Initiates request for a procedure
  ACTION.confirm primitive (for an exchange initiated by the SAP client)
    Reports result of request (success?)
  ACTION.indication primitive
    Result of receipt of request for procedure
  ACTION.response primitive (for an exchange initiated by the MLME)
    Initiate transmission of the requested procedure
BUT on investigation I found there are 7 different “types”
Also ‘discovered’ some normative stuff which should not be (only) in 6.3.

## Slide 5
On further investigation, in the vast majority of cases the primitives are simply boiler-plate and do not need to be spelled out in all their glory.
  Straightforward to construct the primitives based upon the descriptions and action frames.

## Slide 6: Way Forward
The following basic Way Forward was adopted
  Identify the different ‘Types’.
  Identify MLME SAP primitives that are not “obvious” or have specific content that it not covered well by text.
    Keep these in full (Clause 6.4)
  Construct a table that provides the MLME-XXX name, Type and gives references. (Clause 6.5)
  try not to correct or improve the primitives
    This is important. As each was examined in detail, the choices of the Type(s) used, and content details were found to be arbitrary.
      Hence, at this stage do not “Repair” what was 6.3
    Once this approach is accepted, changes and comments could be accepted in future ballots.

## Slide 7: New Amendments
New amendments can simply add line to the Table in 6.5
  And ensure the text references are correct
OR
They can insert the full primitives, in all their glory, in 6.4

## Slide 8: Text 22/0916r5
Estimated reduction in pages – 300
Let’s look at the proposal details.
Suggested strategy is that “experts” should look at the primitives in their area(s) and confirm that they are content that the new format works.