## Slide 1: Device ID Synchronization and Control
Date: 2022-08-11
Authors:

## Slide 2: Revisions
R0 – Initial Version
R1 – Simplification of logic and removal of Informational Element changes. No need to modify Device ID KDE. Logic reworked as well as additions for FILS.
R2 – Modify AP not recognize non-AP STA identifier.

## Slide 3: Abstract
This submission proposes methods on how the Device ID shall be synchronized between the non-AP STA and the network. It also suggests a method to determine if a non-AP STA has Activated Device ID for the network.

## Slide 4: Device ID Synchronization and Control
In the comment collection process for IEEE P802.11bh Draft 0.2 several comments addressing the passing of the ID and synchronization between the non-AP STA and the network. This submission seeks to address these comments.
If the methods suggested herein are agreed upon, a text submission will be prepared to codify these methods in the text.
Seeks to address: CR-4,CR-6, CR-10, CR-11, CR-15, CR26, CR30, CR31

## Slide 5: Device ID Implemented / Device ID Activated Truth Table
Device ID Implemented | Device ID Activated | Result
0 | Don’t Care | Indicates Device ID has not been implemented in the device. The Device ID Support bit will not be set in the RSN Extension Element. No Device ID Element sent in the Association Request frame for FILS No Device ID KDE will be passed in message 2 of the 4-Way handshake for FT or other.
1 | 0 | Indicates that the device has implemented Device ID but has chosen not to be identified. The Device ID Support bit will be set in the RSN Extension Element. No Device ID Element sent in the Association Request frame for FILS No Device ID KDE will be passed in message 2 of the 4-Way Handshake for FT or other.

## Slide 6: Device ID Implemented / Device ID Activated Truth Table
Device ID Implemented | Device ID Activated | Result
1 | 1 | Indicates that the device has implemented Device ID and is allowed to be identified within the network. The Device ID Support bit will be set in the RSN Extension Element. Device ID Element with ID Blob sent in the Association Request frame for FILS Device ID KDE with ID Blob passed in message 2 of the 4-Way Handshake for FT and others.

## Slide 7: Non-AP STA Indication of Device ID Activated
Device ID Activated | ID BLOB | Result
0 | Don’t Care | Indicates device has chosen not to be identified. Network will not assign an ID to the device. No Device ID Element sent in the Association Request frame for FILS No Device ID KDE passed in message 2 of the 4-Way Handshake for FT or other.
1 | EMPTY | Indicates the device has chosen to be identified by a network generated ID, but the ID Blob for this network has not been assigned. Device ID Element with an empty ID Blob sent in the Association Request frame for FILS Device ID KDE with an empty ID Blob sent in message 2 of the 4-Way Handshake for FT or other.

## Slide 8: STA Indication of Device ID Activated
Device ID Activated | ID BLOB | Result
1 | ID | Indicates the device has chosen to be identified with this ID. Device ID Element with ID Blob sent in the Association Request frame for FILS Device ID KDE with ID Blob sent in message 2 of the 4-Way Handshake for FT or others.

## Slide 9: AP Responses
Device ID Active? | ID BLOB | Result
No | N/A | AP should not insert Device ID Element in the Association Response frame for FILS AP should not return Device ID KDE in Message 3 of the handshake for FT or others
Yes | EMPTY | AP should insert a network generated ID Blob in the Device ID Element in the Association Response frame for FILS. The device shall store and subsequently return this ID Blob in the Association Request Device ID Element. AP shall insert a network generated ID Blob in the Device ID KDE in message 3 of the handshake for FT and others. The device shall store and subsequently return this ID Blob in the Device ID KDE in message 2 of the 4-Way handshake.

## Slide 10: AP Response
Device ID Active? | ID BLOB | Result
Yes | ID | Indicates the device has chosen to be identified with this ID.
 |  | If the ID Blob is recognized by the network: AP should not insert Device ID Element in the Association Response frame for FILS AP should not return Device ID KDE in Message 3 of the handshake for FT or others
 |  | If the ID Blob is NOT recognized by the network AP may allow this ID to be utilized to identify the device. AP should not insert Device ID Element in the Association Response frame for FILS AP should not return Device ID KDE in Message 3 of the handshake for FT or others AP may insert a network generated ID Blob in the Device ID Element in the Association Response frame for FILS. The device shall store and subsequently return this ID Blob in the Association Request Device ID Element. If so, AP shall insert a network generated ID Blob in the Device ID KDE in message 3 of the handshake for FT and others. The device shall store and subsequently return this ID Blob in the Device ID KDE in message 2 of the 4-Way Handshake.

## Slide 11: References