## Slide 1: Device ID Synchronization and Control
Date: 2022-12-13
Authors:

## Slide 2: Revisions
R0 – Initial Version
R1 – Simplification of logic and removal of Informational Element changes. No need to modify Device ID KDE. Logic reworked as well as additions for FILS.
R2 – Modify AP not recognize non-AP STA identifier.
R3 – Updates made during presentation. Modified Text for Supported/Active to move into one variable.
R4 – Further updates based on review of 8/20/2020
R5 – Updates based on text review in sessions.

## Slide 3: Abstract
This submission proposes methods on how the Device ID shall be synchronized between the non-AP STA and the network. It also suggests a method to determine if a non-AP STA has Activated Device ID for the network.

## Slide 4: Device ID Synchronization and Control
In the comment collection process for IEEE P802.11bh Draft 0.2 several comments addressing the passing of the ID and synchronization between the non-AP STA and the network. This submission seeks to address these comments.
If the methods suggested herein are agreed upon, a text submission will be prepared to codify these methods in the text.
Seeks to address: CR-4,CR-6, CR-10, CR-11, CR-15, CR26, CR30, CR31
Suggests update to 9.4.2.241 RSN Extension Element

## Slide 5: Suggested Change to 9.4.2.241
Suggest changing Notes to read as follows:
The STA sets the Device ID Support bit to 1 to indicate that it has activated the device ID. Otherwise, the STA sets the Device ID Support field to 0.

## Slide 6: Device ID Support Truth Table AP STA
Device ID Active Bit | AP STA Result for a given network
0 | Indicates Device ID has either not been implemented or it is not active for this SSID No Device ID Element is sent in the Association Response frame for FILS authentication. No Device ID KDE will be passed in message 3 of the 4-Way handshake for other exchanges
1 | Indicates that the AP STA has implemented Device ID and it is active for this SSID Device ID Element with Identity sent in the Association Request frame for FILS authentication. Device ID KDE with ID Identity passed in message 3 of the 4-Way Handshake for other exchanges.

## Slide 7: Device ID Support Truth Table non-AP STA
Device ID Active | Non-AP STA Result for a given network
0 | Indicates Device ID is not active for this SSID No Device ID Element is sent in the Association Request frame for FILS authentication. No Device ID KDE will be passed in message 2 of the 4-Way handshake for other exchanges.
1 | Indicates that the device has implemented Device ID and it is active for this SSID Device ID Element with ID Identity sent in the Association Request frame for FILS authentication Device ID KDE with Identity passed in message 2 of the 4-Way Handshake for other exchanges.

## Slide 8: Non-AP STA Indication of Device ID
Device ID Active | Identity | Result for the network
0 | Don’t Care | Indicates device has chosen not to be identified. Network will not assign an ID to the device. No Device ID Element sent in the Association Request frame for FILS No Device ID KDE passed in message 2 of the 4-Way Handshake for FT or other exchanges
1 | EMPTY or not sent | Indicates the device has chosen to be identified by a network generated ID, but the Identity for this network has not been assigned. Device ID Element with an empty Identity sent in the Association Request frame for FILS authentication Device ID KDE with an empty Identity sent in message 2 of the 4-Way Handshake for FT or other exchanges.

## Slide 9: Non-AP STA Indication of Device ID Activated
Device ID Active | Identity | Result Per Network
1 | ID | Indicates the device has chosen to be identified with this ID. Device ID Element with Identity sent in the Association Request frame for FILS Device ID KDE with Identity sent in message 2 of the 4-Way Handshake for other exchanges.

## Slide 10: AP Actions
Device ID Active | Identity | AP Actions
0 | N/A | AP should not insert Device ID Element in the Association Response frame for FILS AP should not return Device ID KDE in Message 3 of the 4 way handshake other exchanges
1 | EMPTY or not sent | AP shall insert a network generated Identity in the Device ID Element in the Association Response frame for FILS. AP shall insert a network generated Identity in the Device ID KDE in message 3 of the 4 way handshake for other exchanges The non-AP STA shall store and subsequently return this Identity for this SSID.

## Slide 11: AP Response
Device ID Active | Identity | Result
1 | ID | Indicates the non-AP STA has chosen to be identified with this ID for this SSID.
 |  | If the Identity is recognized: AP may insert the Identity in the Device ID Element in the Association Response frame for FILS AP may insert the Identity in the Device ID KDE in Message 3 of the 4-Way handshake for other exchanges
 |  | If the Identity is NOT recognized: AP may allow this ID to be utilized to identify the device. If so, the AP may return this Identity in: Device ID Element in the Association Response frame for FILS The Device ID KDE in Message 3 of the 4-Way handshake for others
 |  | AP may assign a new Identity. If so: The new ID is inserted in the Identity in the Device ID Element in the Association Response frame for FILS. The new ID is inserted in the Identity in the Device ID KDE in message 3 of the handshake for others. The non-AP STA shall store and subsequently return this Identity for this SSID.

## Slide 12: References
IEEE 802.11-22/1599
IEEE 802.11-22/1329