## Slide 1: Duplication Transmission over ML for Low Latency Traffic
Date: 2022-04-26
Authors:

## Slide 2: Background
Restricted TWT is introduced to support RTA traffic in 11be.
  rTWT will work fine for periodic RTA traffic
Interval and data volume of RTA traffic burst changes
  From AP point of view, interval of DL RTA traffic burst to an APP in a STA is changing along with the situation of the network busy status between the AP and the peer point of the APP.
  The interval and data volume of UL traffic burst of many RTAs may be changing along with the RTA APP running.
The rTWT SP needs be set long enough to cover the interval change and data volume change of RTA traffic burst to meet the low latency requirements.
  This leads to impacts to the BSS.
Notes: Duplication transmission
Take consideration on system level : this mechanism introduce more load may make worse.

## Slide 3: Background
3GPP New Radio (5G) introduces PDCP PDU duplication transmission over multiple cells for URLLC (Ultra Reliable Low Latency Communications).
  Copies of a PDCP PDU are being transmitted concurrently over multiple cells.
  The transmission is stopped as soon as one copy is transmitted successfully.
  The latency of the PDCP PDU is the latency of the copy first successfully transmitted.
Multi-link is introduced in 11be.

## Slide 4: Discussion
To have low latency, duplication transmission over ML between 2 MLDs can be utilized as a supplementary to rTWT.
  Duplication transmission over ML between 2 MLDs means copies of a MPDU are being transmitted concurrently over the Multi-Link.
MLO fits for duplication transmission over ML
  Acknowledgement across links
  Duplication detection
To keep the impacts of rTWT SP to the BSS small,
  rTWT SP can be set with a proper duration (which is no need to cover all RTA traffic data arrivals ) to afford most of the RTA traffic bursts.
  RTA data that are not transmitted during the rTWT SP because of late arrival or bigger data volume can be transmitted with duplication over ML to meet the latency requirements.

## Slide 5: Examples

## Slide 6: Considerations
Rules are needed to prevent abuse of duplication transmission over ML.
  Which data to apply duplication transmission over ML?
    Latency sensitive data arrived out of rTWT SP are transmitted with duplication over ML.
  Over which links the duplication transmission is applied?
    TID mapped links, or subset of TID mapped links
  Maximum number of copies of the duplication transmission
  The duplication transmission can be switch on/off by the AP MLD

## Slide 7: Conclusion
To keep the impacts to the BSS small, it is not good to set a long rTWT SP enough to cover the interval change and data volume change of RTA traffic burst.
3GPP’s PDCP duplication transmission provides a method to achieve low latency, which has been proved in practice.
MLO fits for duplication transmission over ML.
Rules are needed to prevent abuse of duplication transmission over ML.

## Slide 8: Proposal
Following rules for duplication transmission of latency sensitive data over ML between 2 MLDs are introduced in 11be.
  Latency sensitive data arrived out of the corresponding rTWT SP are transmitted with duplication over the links which are mapped by the TID of the data.
  Maximum number of the data copies for the duplication transmission are negotiated by both the MLDs
  The duplication transmission can be switch on/off by the AP MLD.
Notes: Clarified the proposal