## Slide 1: Hashed SSID
Date: 2022-08
Authors:

## Slide 2: Background
Requirement #15
  11bi shall define a mechanism for a BPE Client to determine which of the BPE Client’s configured networks a BPE AP belongs to (if any), while providing some mitigation against an eavesdropper easily identifying the ESS of the BPE AP.
We discuss a mechanism that can satisfy this requirement in this contribution

## Slide 3: Problem and Challenge
Problem: SSID is transmitted in the clear by both AP and STA. Trackable.
Challenge:
  Balancing complexity of valid discovery against complexity of malicious discovery
  Any solution that mitigates all attacks places unacceptable burden on AP and STA
  E.g. asymmetric crypto based solution or long-term shared key.

## Slide 4: Solution
Problem: SSID is transmitted in the clear by both AP and STA. Trackable.
An AP computes a hashed SSID value as follows and places it in the SSID field of the SSID element (carried in the Probe Response frame and optionally in the Beacon frame):
  Hashed_SSID = hash_function(SSID || BSSID), where the BSSID is the link MAC address of the AP on which the frame that carries the SSID element is transmitted or received
A STA computes a hashed SSID value based on each SSID that it has been configured with. If there is a match, that means this AP belongs to the configured SSID that the non-AP STA could connect to if it chooses to

## Slide 5: Some Properties of the Proposal
Simple – very low complexity overhead. Mitigates casual attackers - attacker must guess SSID
Does not require any frame changes and hardware changes in the AP or STA
When the BSSID changes (e.g., randomized to avoid being tracked), the hashed SSID value will change automatically and simultaneously

## Slide 6
Sample Discovery Call Flow
Client Link Access
(Affiliated STA)
AP Link Access
(Affiliated AP)
Beacon (option pSSID, OTA-TSF, Ext_PASN)[TA=OTA-BSSID1, RA=bcast]
Prob Req (Min STA Capability IEs)[TA=rand1, RA=bcast]
Probe Resp (pSSID, Min AP Capability IEs, Ext_PASN)
[TA=OTA-BSSID1, RA=rand1/bcast]
OTA-BSSID1
Client Core (NA MLD)
AP Core (AP MLD)
Private AP MAC = AP MLD MAC, TSF, SSID
Private Client MAC = NA MLD MAC, SSIDs
Note: Not all fields shown – only relevant fields shown
Client
Mobile AP
ML Prob Req (Min MLO Capability IEs)[TA=rand2, RA=OTA-BSSID1]
ML Prob Resp (Min MLO Capability IEs, no SSID included)
[TA= OTA-BSSID1, RA=rand2]
Client checks if the received pSSID corresponds to any of its configured SSIDs by computing an expected pSSID using a configured SSID and the received OTA-BSSID
pSSID=hash(SSID, OTA-BSSID1). Note pSSID changes automatically when the OTA-BSSID is changed
AP MLD info
AP MLD info
AP MLD info Req