## Slide 1: RR-TAG mmWave Spectrum Survey
Date: 2022-09-13
Authors:
Notes: September 2012

## Slide 2: Abstract
IEEE 802.11 is considering mmWave bands for the UHR project to supplement the bands currently in use. IEEE 802.18, the Radio Regulatory Technical Advisory Group has experts and experience in spectrum use. This presentation is an introduction to what the 802.18 mmWave Ad Hoc group will be doing, and what it plans to deliver to the UHR SG/TG. This information will also be useful for other IEEE wireless groups, specifically 802.15.
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 2

## Slide 3: The Bands Being Studied (and Why)
45 GHz band
  Potentially 5.5 GHz available (42.5 – 48 GHz) for license exempt sharing in China
  The experience with IEEE 802.11aj-2018 standard will aid in this effort
  Preferred in China over 60 GHz
  Europe has an SRD standard encompassing the band (EN 305 550-1)
60 GHz band
  Potentially 14 GHz available (57 – 71 GHz) for license exempt sharing in the US, EU, etc.
  IEEE 802.11 has long experience with this band
  ETSI has a standard that could be modified to support UHR (EN 303 753)
This is a representative sample only
  Both of these bands include Fixed, Satellite, Radioastronomy and other incumbents
  China’s limited license-exempt spectrum was the reason for the 45 GHz effort
  The US and the EU are typically the drivers for a lot of the global spectrum sharing rules

## Slide 4: Parallel Project For Information Only
For IEEE 802.11
  Work will be conducted independent of the UHR SG/TG
  The group will provide updates either periodically or upon request
  Once the SG/TG makes a spectrum determination, this group will shift its focus to support the UHR SG/TG as required
For IEEE 802.15
  The group will provide updates either periodically or upon request
  If IEEE 802.15 have any specific requirement, the group will consider and support

## Slide 5: The Art of Spectrum Complexity
6GHz
45GHz
60GHz

## Slide 6: Spectrum Study Plan
Review all the relevant documents and online information
  ITU-R Radio Regulations [and all the footnotes!]
  European Table of Frequency Allocations
  ECO Frequency Information System
  US FCC Table of Frequency Allocations
  All other applicable and available regulatory domain regulations
Review existing applicable standards
    E.g. ETSI EN 305 550-1, EN 303 753
Request information where clarifications are necessary

## Slide 7: What the Information Supplied Will Contain
Spectrum availability, status and regulatory requirements
  Parts or all of the proposed bands
  Incumbent protection expectations
Historic spectrum sharing successes with similar incumbents
Global expectations for success with any required regulatory changes
  e.g., historically, the resources and time involved in making changes to regulations

## Slide 8: What the Group Will Not Do
Formal requests for regulatory changes are beyond the resource capacity of this ad hoc group
  Information will be the primary work product
Advocate for a spectrum preference

## Slide 9: The IEEE 802.18 mmWave Ad Hoc Group Meetings
Edward Au is inviting you to a scheduled Webex meeting.
Occurs every Wednesday effective 8/24/2022 until 1/25/2023 from 3:00 PM to 4:00 PM, (UTC-04:00) Eastern Time (US & Canada)
Join from the meeting link
https://ieeesa.webex.com/ieeesa/j.php?MTID=ma28b1d9d051ecdddab365d1a7ea00687
Join by meeting number
Meeting number (access code): 2331 559 4743
Meeting password: mmWave-weekly
Tap to join from a mobile device (attendees only)
+1-646-992-2010,,23315594743## United States Toll (New York City)
+1-213-306-3065,,23315594743## United States Toll (Los Angeles)
All are welcome

## Slide 10: References
ITU-R Radio Regulations
  https://www.itu.int/pub/R-REG-RR
US FCC Table of Frequencies
  https://transition.fcc.gov/oet/spectrum/table/fcctable.docx
European Table of Frequency Allocations
  https://efis.cept.org/ [search by frequency, country, etc.]
  https://efis.cept.org/sitecontent.jsp?sitecontent=ecatable
European National Frequency Tables
  https://efis.cept.org/views2/national_frequency_table.jsp