## Slide 1: TGbi, Protection against Spoof AP using Probe
Date: 2022-08
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: The “Problem”
Dastardly people set up APs that spoof the “home BSS” of the target X.
  The “J Lo” paparazzi attack
If X’s mobile, STA X, comes in range, it will attempt to Associate
It does not matter what MAC Address STA X is using, the mere fact it sent an Association Request exposes that it (or someone from X’s home) is in the area.
Originally RCM stopped simple MAC tracking, but now spoof AP can be used.
TASK - Is it possible to know that the AP is the “real deal” BEFORE attempting to Associate?

## Slide 3: Why present in TGbh?
RCM did not ‘break’ this, but also it did not solve it.
This proposed solution uses an identifiable TA and hence requires the adoption of a “pre-scheme” such as MAAD.
Hence, this is presented in TGbh as a further justification that a “pre-scheme” should be adopted.

## Slide 4: How to stop the STA from sending Association Request to a spoof?
Three basic IDEAS were presented previously:
Location based – Use GPS to record location of “Home AP”
  Not an 802.11 solution
SSID Profile – Take an SSID profile of the “Home AP” and use this to verify the AP
  Could be an 802.11 solution but probably proprietary
  Very difficult to fake, (need to transmit a range of known SSIDs but mere presence of new SSIDs would defeat this)
  Needs to account for updates and an algorithm would be out-of-scope.
Identifiable Beacon – Add a Beacon protection key and include hash in beacon.
  Definitely an 802.11 solution,
  Can only be defeated by near real-time relay of the beacons
This proposal presents a fourth IDEA
Allocated MAC Address, ID and wildcard probe

## Slide 5: “Allocated Address and ID and Wildcard Probe” Basic scheme
Each time STA associates with the “home” network, it is allocated an address AND an ID
  Use MAAD for the address and the ID could use Device ID or similar
IF STA ‘sees’ the home network, (passive)
Before sending Association Request STA sends a wildcard probe using the allocated MAC Address.
The real AP identifies the STA and sends a Probe response including the correct ID.
  Real AP has a limited number of “clients” which it is remembering anyhow
STA checks the ID and will then associate and receives a NEW Address and ID.
“Spoof AP” does not know this STA address from any other and will not respond with the correct ID
  In practice, there won’t be a spoof AP because it won’t work.

## Slide 6: More Details
STA associates (User knows this is ‘Home”) and receives an allocated MAC address (e.g., using the MAAD scheme) and an ID
  NOTE: Only provided for identified users, not “guests”
  Address and ID in KDEs in msg 3
STA sees “home” AP (passive scan)
STA sends wildcard probe using the allocated MAC address
  Not a directed probe so not distinguished from other STAs.
  Allocated MAC Address is not known by the spoof. Indistinguishable from RCM.
“Real Home” AP recognizes STA and sends a Probe Response with the ID
  Home AP is remembering the clients as per Use Case 4.2 etc.
STA confirms the ID and sends Association Request
STA receives new Address and ID.

## Slide 7: Important points
No obvious worthwhile attack.
  TA appears to be same as an RCM to a listener
No computations required
  Simple address check
ID could be the “Device ID” or simply tacked on to the MAAD address. (One octet is more than enough)
  Depends if the Home APP uses a distinctive Device ID.
  Could use the opaque ID (changes every association)
Requires that a “pre-scheme” (e.g., MAAD) is adopted
IT DOES APPEAR TO SOLVE THE PROBLEM!
All TGbh need do is include a “pre-scheme” in the Draft

## Slide 8: Straw Poll
In order to allow possible adoption of a scheme (in TGbi?) that mitigates the spoof AP “paparazzi attack”, TGbh should include a “pre-scheme” method.
Y/N/A
Note: Proposed “pre-scheme” methods such as MAAD, IRM, IRMA and RCCM could be considered.