## Slide 1: TGbh, Protection against Spoof AP using Probe
Date: 2022-09
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: The “Problem”
Dastardly people set up APs that spoof the “home BSS” of the target X.
  The “J Lo” paparazzi attack
If X’s mobile, STA X, comes in range, it will attempt to Associate
It does not matter what MAC Address STA X is using, the mere fact it sent an Association Request exposes that it (or someone from X’s home) is in the area.
Originally RCM stopped simple MAC tracking, but now spoof AP can be used.
TASK - Is it possible to know that the AP is the “real deal” BEFORE attempting to Associate?

## Slide 3: Why present in TGbh?
RCM did not ‘break’ this, but also it did not solve it.
This proposed solution uses an identifiable TA and hence requires the adoption of a “pre-scheme” such as MAAD.
Hence, this is presented in TGbh as a further justification that a “pre-scheme” should be adopted.

## Slide 4: How to stop the STA from sending Association Request to a spoof?
Three basic IDEAS were presented previously:
Location based – Use GPS to record location of “Home AP”
  Not an 802.11 solution
SSID Profile – Take an SSID profile of the “Home AP” and use this to verify the AP
  Could be an 802.11 solution but probably proprietary
  Very difficult to fake, (need to transmit a range of known SSIDs but mere presence of new SSIDs would defeat this)
  Needs to account for updates and an algorithm would be out-of-scope.
Identifiable Beacon – Add a Beacon protection key and include hash in beacon.
  Definitely an 802.11 solution,
  Can only be defeated by near real-time relay of the beacons
This proposal presents a fourth IDEA
Allocated MAC Address, ID and wildcard probe

## Slide 5: “Allocated Address and ID and Broadcast Probe” Basic scheme
Each time STA associates with the “home” network, it is allocated two addresses #1 and #2 AND an ID
  E.g., Use MAAD for the addresses and the ID, any pre-scheme should work.
  Address #1 for Association, Address #2 for probes (Only when wants to be identified. Otherwise use RMA).
  could use Device ID or similar but may prefer to add 1 octet to the MAAD element

## Slide 6: Basic scheme - 2
IF STA ‘sees’ the home network, (passive or broadcast probes)
Before sending Association Request STA sends a broadcast probe using the allocated MAC Address #2.
The real AP identifies the STA and sends a Probe response including the correct ID.
STA checks the ID and will then associate using address #1 as TA
STA receives NEW Addresses and ID.
“Spoof AP” does not know this STA address from any other, or the ID, and can not respond with the correct ID
STA will not attempt to associate.
  No real problem if STA continues to broadcast probe. Nothing to distinguish it from any other STA.

## Slide 7: More Details
STA associates (User knows this is ‘Home”) and receives two allocated MAC addresses (e.g., using the MAAD scheme) and an ID
  NOTE: Only provided for identified users, not “guests”
  Addresses and ID in KDEs in msg 3
STA sees “home” AP (passive scan)
STA sends broadcast probe using the allocated MAC address
  Not a directed probe so not distinguished from other STAs.
  Allocated MAC Address is not known by the spoof. Indistinguishable from RCM.
“Real Home” AP recognizes STA and sends a Probe Response with the ID
  Home AP is remembering the clients as per Use Case 4.2 etc.
STA confirms the ID and sends Association Request using address #1
  Listener cannot link the addresses
STA receives new Addresses and ID.

## Slide 8: AP Spoof Mitigation - continued
This “broadcast probe AP identity scheme” requires that the Address is identifiable, i.e., a pre-scheme is required.
MAAD MAC allocates two addresses to mitigate copying :
  Address #1 used only for association
  Address #2 used only when probing and ‘wants to be identified’
Home AP should include a “random ID” in every Probe response, using the actual ID when address #2 is identified.
  Prevents “relay” attack (see next slide)
  Only the Home Network need do this.
  STA may have several MAAD MAC addresses, but this only required for ‘special’ identifiable networks.

## Slide 9: AAID Spoof defense
To overcome AAID:
Attacker needs to record every broadcast probe TA at target site (spoof AP),
Then relays every TA to a STA situated near the “home” and send broadcast probe to home AP using every TA.
Then note the ID returned per TA, and relay that back to target site (spoof) AP,
Then either use ID in a probe response (there is a time delay) or wait to see if same TA used again for a probe*, and if so, send the ID recorded in 3) in probe response
Wait to see if that causes a STA to try to associate.
  Note that it will use different address to associate
Still do not know who it is, but does know a member of the “home” network
Is this even a practical “attack”? Multitude of probes received, still does not know who it is.
*Easy for a STA to not send another broadcast probe if response from the spoof “home” SSID does not have the correct ID – time limit etc.
Bottom line - This means that using MAAD pre-scheme has more privacy than RMA AND provides solution for pre-association Access Control use cases
Note: RCM did not ‘break’ this “spoof’ scenario, but also it did not solve it (spoof AP)
  Justification that a “pre-scheme” should be adopted

## Slide 10: Important points
No obvious worthwhile attack.
  TAs appear to be same as an RCM to a listener
  Separate TAs used for probing and association
No computations required
  Simple address check
ID could be the “Device ID” or simply tacked on to the MAAD address. (One octet is more than enough)
  Depends if the Home APP also uses a distinctive Device ID.
  Could use the opaque ID (changes every association)
Requires that a “pre-scheme” (e.g., MAAD) is adopted
IT DOES APPEAR TO SOLVE THE PROBLEM!
All TGbh need do is include a “pre-scheme” in the Draft

## Slide 11: Straw Poll
In order to allow possible adoption of a scheme (in TGbi?) that mitigates the spoof AP “paparazzi attack”, TGbh should include a “pre-scheme” method.
Y/N/A
Note: Proposed “pre-scheme” methods such as MAAD, IRM, IRMA and RCCM could be considered.