## Slide 1: Thoughts on High Reliability Communications (for Next Gen WiFi)
Date: 2022-08-29
Authors:
Name | Affiliation | Address | Phone | Email
Aiguo Yan | Zeku | 2479 E Bayshore Rd, Palo Alto, CA 94303 |  | aiguo.yan@zeku.com
Yi-Hsiu Wang | Zeku |  |  | 
Xiaogang Chen | Zeku |  |  | 
Doc.: IEEE 802.11-22/1413r0
August 2022

## Slide 2: Agenda
Key Points from past WNG Presentation
Area 1 for Improvement
Area 2 for Improvement
Area 3 for Improvement
Summary
Straw-Polls
August 2022
Doc.: IEEE 802.11-22/1413r0

## Slide 3: Key points from previous WNG meetings
Throughput/DataRate, and Latency are two KPIs emphasized by many presenters.
Another often emphasized point is Reliability, along with similar KPIs such as QoS, Robustness, Coverage and Efficiency.
One presentation [MTK] also emphasized “practical” throughput improvements instead of theoretic throughput improvements on paper, in general popular usage scenarios instead of some rare usage scenarios.
UHR-SG is formed with emphasized on Reliability. One of requirements is performance improvement at different SNR level.
More resources (such as Higher TX power, wider channel BW, more antennas, more available spectrum … ) can always make a wireless system more reliable.
In addition to high cost with these approaches, resources may be unavailable and there are constraints to these resources (regulatory issues and physical size of a device)
Question: What could WiFi Community do to optimize existing technology for improving reliability?
August 2022
Doc.: IEEE 802.11-22/1413r0
Notes: BW, Modulation Order, Power, Coding, ……….

## Slide 4: Area 1: Existing Concerns with MIMO/TXBF
11ax-P579: It is recommended that the spatial mapping matrix applied to HE-STF and beyond be chosen such that it preserves the smoothness of the physical channel, achieved by limiting the variation of each element’s real and imaginary values in the spatial mapping matrix across successive tones within one RU
11beD1.5-P652: It is recommended that the spatial mapping matrix applied to EHT-STF and beyond is chosen such that it preserves the smoothness of the physical channel, achieved by limiting the variation of each element's real and imaginary values in the spatial mapping matrix across successive tones within one RU.
Call for actions: Could WiFi community define ways for AP/STA work together to better preserves and improve the smoothness of the BFed physical channel?
August 2022
Doc.: IEEE 802.11-22/1413r0

## Slide 5: Area 2: TXBF feedback Overhead
With more 4K subcarriers (possible more in WiFi8) and 8 TX antennas (possible more in WiFi8), and potential multi-AP schemes in WiFi8, amount of data to be fed-back is enormous
Multiple contributions emphasized importance of overhead reduction. [InterDigital]; [Samsung]; [Toshiba] and [Huawei]
Recently, CIS Feedback Overhead Reduction was proposed as the top use cases in July AIML TIG meeting
August 2022
Doc.: IEEE 802.11-22/1413r0

## Slide 6: Existing Proposals on Overhead Reduction (except Subband [Huawei]/Grassmannian[Toshiba]/DR[Samsung])
August 2022
Doc.: IEEE 802.11-22/1413r0
 | Scheme | Pros | Cons
1 | ϕ only feedback | exists in 802.11ah | single data stream only
2 | time domain channel | exists in 802.11ad/ay | may need additional signaling to identify tap positions and the extra matrix
3 | Differential Givens Rotation | Simple improvement from 802.11ax, variant in 11ay | Additional processing, Error Propagation
4 | Variable Angle Quantization | simple improvement from 802.11ax | additional processing
5 | Multi-component Feedback | Well understood, reduced feedback overhead | May need additional design
6 | Codebook based Feedback | Well understood, reduced feedback overhead | May need additional design
7 | Two way channel training | Do not need calibration, reduced feedback overhead | May need additional design
8 | Implicit Feedback | Simple improvement from 802.11n | Needs calibration
Table is from “11-19-0391-00-0eht-feedback-overhead-reduction-in-802-11be.pptx” by InterDigital

## Slide 7: Area 3: GMD based TXBF
SVD based TXBF was first introduced in 11n.
There are no much changes since then.
GMD (Geometric Mean Decomposition) based TXBF has been a hot topic in research community.
Question: could the WiFi community conduct more research in this area and standardize the GMD based TXBF scheme, providing gain is significant and complexity increase is acceptable?
August 2022
Doc.: IEEE 802.11-22/1413r0

## Slide 8: Summary
Use advanced algorithms and additional functionalities supported by standard to further unlock the potential of MIMO technologies
August 2022
Doc.: IEEE 802.11-22/1413r0

## Slide 9: SP #1 and #2
Are you willing to support enhancement of standard on SVD based TXBF if SNR gain is at least 1.0 dB?
Are you willing to support enhancement of standard on SVD based TXBF if SNR gain is around 2.5 dB?
Note:
Baseline: SVD based TXBF Performance without channel smoothing.
These SPs are for Information Collection only.
August 2022
Doc.: IEEE 802.11-22/1413r0

## Slide 10: SP #3 and #4
Are you willing to support enhancement of standard for SVD TXBF feedback overhead reduction if the amount of data to be feedbacked is reduced to ½-th, with potential performance degradation <=0.25dB?
Are you willing to support enhancement of standard for SVD TXBF feedback overhead reduction if the amount of data to be feedbacked is reduced to 1/4-th, with potential performance degradation <=0.25dB?
Note:
Baseline: 11be feedback scheme
These SPs are for Information Collection only.
August 2022
Doc.: IEEE 802.11-22/1413r0

## Slide 11: SP #5 and #6
Are you willing to support enhancement of standard for GMD based TXBF if SNR gain is at least 1.0 dB?
Are you willing to support enhancement of standard for GMD based TXBF if SNR gain is around 2.5 dB?
Note:
Baseline: SVD based TXBF Performance.
These SPs are for Information Collection only.
August 2022
Doc.: IEEE 802.11-22/1413r0

## Slide 12: Selected References
WNG Presentations
Please see all WNG presentations until July 2022. (inclusive)
Overhead Reduction Presentations
Key reference: 11-19-0391-00-0eht-feedback-overhead-reduction-in-802-11be.pptx
11-22-0950-02-aiml-discussion-on-interaction-between-ai-ml-wireless-lan.pptx
IEEE Journal/Conference Papers on Smoother Channels and GMD
C. Shen and M. P. Fitz, "MIMO-OFDM Beamforming for Improved Channel Estimation," in IEEE Journal on Selected Areas in Communications, vol. 26, no. 6, pp. 948-959, August 2008, doi: 10.1109/JSAC.2008.080811.
W. Hu, F. Li and Y. Jiang, "Phase Rotations of SVD-Based Precoders in MIMO-OFDM for Improved Channel Estimation," in IEEE Wireless Communications Letters, vol. 10, no. 8, pp. 1805-1809, Aug. 2021, doi: 10.1109/LWC.2021.3081583.
E. Jeon, M. Ahn, S. Kim, W. B. Lee and J. Kim, "Joint Beamformer and Beamformee Design for Channel Smoothing in WLAN Systems," 2020 IEEE 92nd Vehicular Technology Conference (VTC2020-Fall), 2020, pp. 1-6, doi: 10.1109/VTC2020-Fall49728.2020.9348441.
F. Jiang, Q. Li and X. Chen, "Channel Smoothing for 802.11ax Beamformed MIMO-OFDM," in IEEE Communications Letters, vol. 25, no. 10, pp. 3413-3417, Oct. 2021, doi: 10.1109/LCOMM.2021.3099167.
Yi Jiang, J. Li and W. W. Hager, "Joint transceiver design for MIMO communications using geometric mean decomposition," in IEEE Transactions on Signal Processing, vol. 53, no. 10, pp. 3791-3803, Oct. 2005, doi: 10.1109/TSP.2005.855398.
August 2022
Doc.: IEEE 802.11-22/1413r0