## Slide 1: EHT NDP Support Using Ranging NDPA
Date: 2022-08-25
Authors:
Name | Affiliation | Address | Phone | Email
Junghoon Suh | Huawei |  |  | junghoon.suh@huawei.com
Yan Xin |  |  |  | Yan.Xin@huawei.com
Osama AboulMagd |  |  |  | Osama.AboulMagd@huawei.com

## Slide 2: Sensing NDP and NDPA
Both the Ranging NDP PPDU and the EHT NDP PPDU may be used for the Sensing NDP PPDU
  Ranging NDP PPDU for BW<= 160 MHz and EHT NDP PPDU for BW = 320 MHz [1]
  The Ranging NDP PPDU is basically the HE NDP PPDU but with no preamble puncturing allowed and with no Partial BW Feedback allowed
    Furthermore, the Ranging NDP introduces the I2R NDP which can be sent from the non-AP STA to the AP
    The Ranging NDP can support the LTF repetition
  The EHT NDP PPDU supports the BW up to 320 MHz, whereas the Ranging NDP PPDU can support up to 160 MHz
    The EHT NDP PPDU of course supports the Preamble Puncturing and the Partial BW Feedback
    The EHT NDP may implicitly support the LTF repetition once, using the Number of LTFs parameter in the Common field of EHT-SIG field, that is, for the number of Spatial Stream 4, the number of LTFs can be set to 8
However, the Sensing NDPA format may most likely use the Ranging NDPA format

## Slide 3: Reuse of Ranging NDPA for Sensing NDPA [2]
B26 and/or B31 indicates the Sensing NDPA
LTF Offset is not necessary and can be repurposed in Sensing
B0
(Ranging)
Bits
:
1 1 6
Sounding Dialog
Token Number
B2
B7
STA Info # 1
STA Info # n
FCS
AID:
2045
MAC
Header
Sounding
Dialog
Token
Octets
:
1 Special STA Info Field (4) 4
4 4
Measure-ment
Set-up ID
Disambi-
guation
Ranging NDPA based Sensing NDPA
B1
(HE)
Measurement Instance ID
I2R NDP
TX Power
R2I NDP
Target RSSI
Sensing
Sensing
(Reserved)
B0
B11
B31
1 0
B10
B18
B19
B26
B27
B28

## Slide 4: Possible issues when the EHT NDP PPDU is used for the Sensing NDP
How do we indicate the CSI Measurement in the Sensing NDPA for the Preamble Punctured EHT NDP PPDU?
How do we indicate the Partial BW Feedback in the Sensing NDPA when the Operation BW of each responder is smaller than the BW of EHT NDP PPDU?
Do we need to indicate the BW of the NDPA frame?
  The SERVICE field in non-HT PPDU is used to indicate the BW and the Static Puncturing Patterns of NDPA
  Do we need an explicit BW subfield in a Special STA Info field?
How do we support any integer multiple of LTF repetitions in the EHT NDP PPDU?

## Slide 5: How do we indicate the CSI Measurement in the Sensing NDPA for the Preamble Punctured EHT NDP PPDU?
The indication of Preamble Puncturing can be done in two different ways, depending on whether the Partial BW Feedback is allowed or not
  If we agree to allow the Partial BW FB, then, at least 8 bits are necessary to indicate the Preamble Puncturing, 20 MHz is the FB resolution for the BW of NDPA/NDP, 160 MHz and below, and 40 MHz is the FB resolution for the NDPA/NDP BW, 320 MHz
    The same Table in the TGbe D2.0, Table 9-42c can be applied except for the first bit implying the FB resolution
  If we agree to disallow the Partial BW FB, then, 5 bits are good enough to indicate the Preamble Puncturing Patterns
    Preamble puncturing patterns in the Sensing NDPA should be aligned with the Preamble Puncturing Patterns in the EHT NDP PPDU, which are also aligned with the Static Puncturing Patterns exchanged during the association
    The Table 36-30 of TGbe D2.0, the Preamble Puncturing Patterns (Punctured Channel Information field) for the non-OFDMA scenario can be used
    The Dynamic Puncturing Patterns can be disallowed in the Sensing Sounding

## Slide 6: How do we indicate the Partial BW Feedback in the Sensing NDPA when the Operation BW of each responder is smaller than the BW of EHT NDP PPDU?
The Partial BW Feedback is a STA Specific parameter which is supposed to be indicated in the STA Info field of Sensing NDPA, however, it requires at least 8 bits to indicate the same Partial BW Feedback as the Partial BW Feedback in the EHT NDPA
  Resolution of Partial BW FB for the NDPA/NDP BW 160 MHz and below: 20 MHz
  Resolution of Partial BW FB for the NDPA/NDP BW 320 MHz : 40 MHz
If the Ranging based NDPA is the baseline NDPA for the Sensing, then, there are not enough space to indicate the Partial BW FB in a STA Info field
  The BW of NDPA/NDP should be aligned with the minimum operation BW of those STAs listed in the STA Info fields  It effectively disallows the Partial BW FB
  Each responder is supposed to report the measurements for the entire BW of NDPA/NDP excluding the punctured channels if the preamble puncturing is allowed

## Slide 7: Where do we indicate this Preamble Puncturing Patterns in Sensing NDPA?
The Preamble Puncturing Patterns may be common to all the STAs listed in the STA Info fields of Sensing NDPA frame, that is, this puncturing patterns can be indicated in a Special STA Info field (We can call it a Common field) or in each STA Info field
  Case for using a Special STA Info field: We can introduce a new Special AID for the second Special STA Info field in addition to the existing Special STA Info field (AID 2045)
    New Special AID can be anything available in TGbe D2.0 Table 9-42b, any AID without being occupied for some other purpose, that is, any Reserved AID such as 2008 to 2042
    The length of the new Special STA Info field would be 4 bytes as well
  Case for using a subfield in a STA Info field: The B11-B16 of each STA Info field in the Ranging NDPA was originally used for the LTF Offset which is an LTF Security relevant parameter, and the LTF Security is not needed in the Sensing. This LTF Offset subfield can be re-purposed for the Preamble Puncturing Patterns Indication. In case we only need bits less than 6 bits for the Puncturing Patterns, then, the remaining bits can be set to Reserved in the STA Info field
  When the non-HT PPDU is used for the Sensing NDPA, the Preamble Puncturing patterns are indicated in the Service field ahead of PSDU

## Slide 8: Do we need to indicate the BW of the NDPA frame?
When the non-HT PPDU is used for the Sensing NDPA, the BW of the NDPA is indicated in the Service field and/or, the responder implicitly detects the BW of Sensing NDPA until the responder receives the NDP
We propose to introduce the BW subfield (BW of the Sensing NDPA and supposed to be aligned with the BW of NDP) in a Special STA Info field (We need to set a new AID for this new additional Special STA Info field) or in a STA Info field
  Special STA Info field can be called a Common field

## Slide 9: How do we set the SIG field in the EHT NDP PPDU for any number of LTF repetition?
In the current EHT Common field of EHT-SIG field, there are 3 bits assigned to indicate the Number of EHT-LTFs
  It is only allowed to use twice as many LTFs as the number of TX Spatial Streams (SS), that is, for 1, 2, and 4 SS, it is only allowed to use 2, 4, and 8 LTFs
We propose to allow as many LTFs as the integer multiples of TX SS with 8 LTFs as being the maximum
  E.g. for 1 TX SS, we can allow 1, 2, 4, 6 and 8 LTFs
  For 2 TX SS, we can allow 2, 4, 6 and 8 LTFs
We need to indicate in the NDPA whether the following NDP is EHT-based or Ranging NDP-based
  B31 in the STA Info field is the good place to indicate the PPDU format of the following NDP

## Slide 10: How to indicate the type of the following NDP PPDU
The Ranging NDP PPDU is used for the Sensing Sounding of BW less than or equal to 160 MHz and the EHT NDP PPDU is used for the Sensing Sounding of BW equal to 320 MHz [1]
  BW indication in the NDPA implies the following NDP type
B31 in the STA Info field is the good place to indicate the PPDU format of the following NDP if we use the existing available subfield space in the NDPA and want to explicitly indicate
  The same information repeats in the STA Info fields

## Slide 11: Conclusions
Solution for the indication of Preamble Puncturing patterns in the Sensing NDPA
We propose to disallow the Partial BW Feedback in the Sensing NDPA, that is, the Operation BW of each responder should be aligned with the BW of EHT NDP PPDU
We proposed to indicate the BW of Sensing NDPA in the Special STA Info field or in a STA Info field
We proposed to repeat the LTFs as many as possible with the maximum number of LTFs limited by 8
Indication of following NDP type, the Ranging NDP PPDU or the EHT NDP PPDU

## Slide 12: References
[1] Yan Xin, et. al., “NDP formats for 802.11bf”, 802.11 TGbf 22/1380r0
[2] Junghoon Suh, et. al., “Harmonization for TGbf NDPA”, 802.11 TGbf 22/663r2

## Slide 13: SP 1
Do you agree to disallow the Partial BW Feedback in the Sensing NDPA?
  The Operation BW of each responder should be aligned with the BW of EHT NDP PPDU
  Yes
  No
  Abs

## Slide 14: SP 2
Do you agree with 5 bits to indicate the Punctured Channel Information in the Sensing NDPA?
  It is TBD to support the Preamble Puncturing for the BW of NDP/NDPA <= 160 MHz
  Yes
  No
  Abs

## Slide 15: SP 3
Do you agree to indicate the BW of the Sensing NDPA in a subfield of a Special STA Info field?
  Yes
  No
  Abs

## Slide 16: SP 4
Do you agree to use the B31 in a STA Info field of the Sensing NDPA to indicate the following NDP PPDU ?
  The following NDP PPDU can be either the Ranging NDP PPDU or the EHT NDP PPDU
  Yes
  No
  Abs