## Slide 1: Wireless for ML - Over-the-Air Computation
Date: 2022-09-13
Authors:

## Slide 2: Abstract
In this talk, we provide a brief discussion on how over-the-air computation (OAC) can address the latency and spectral congestion in a wireless network when a neural network is aimed to be trained in a distributed manner and discuss its impact on the PHY design

## Slide 3: ML for Wireless vs. Wireless for ML
Two different paths for the merge of communications and ML:
Wireless for ML
Approach: Use communications as a
method to improve ML [2]
Goal: Better ML performance
Info: Model parameters, gradients, ...
ML for Wireless
Approach: Use ML as a method to
improve communication blocks [1]
Goal: Better communications
Info: Images, video, audio, ...

## Slide 4: ML for Wireless vs. Wireless for ML
Two different paths for the merge of communications and ML:
Wireless for ML
Approach: Use communications as a
method to improve ML [2]
Goal: Better ML performance
Info: Model parameters, gradients, ...
ML for Wireless
Approach: Use ML as a method to
improve communication blocks [1]
Goal: Better communications
Info: Images, video, audio, ...
This talk

## Slide 5: Distributed Learning over A wireless Network
Part – I

## Slide 6: Centralized Learning over a Wireless Network
Assume that a deep neural network (DNN) is desired to be trained based on the local datasets at STAs
STA
Local dataset
STA 2
STA
AP
Local dataset
Local dataset
…
…
Procedure:
Step 1: All STAs transmit their local datasets
Step 2: Obtain the trained model parameters with an algorithm

## Slide 7: Centralized Learning over a Wireless Network
Assume that a deep neural network (DNN) is desired to be trained based on the local datasets at STAs
Procedure:
Step 1: All STAs transmit their local datasets
Step 2: Obtain the trained model parameters with an algorithm
STA
Local dataset
STA 2
STA
AP
Local dataset
Local dataset
…
…

## Slide 8: Centralized Learning over a Wireless Network
Assume that a deep neural network (DNN) is desired to be trained based on the local datasets at STAs
…
STA
Local dataset
STA 2
STA
AP
Local dataset
Local dataset
…
…
Procedure:
Step 1: All STAs transmit their local datasets
Step 2: Obtain the trained model parameters with an algorithm

## Slide 9: Centralized Learning over a Wireless Network
STA
Local dataset
STA 2
STA
AP
Local dataset
Local dataset
…
…
Assume that a deep neural network (DNN) is desired to be trained based on the local datasets at STAs
Procedure:
Step 1: All STAs transmit their local datasets
Step 2: Obtain the trained model parameters with an algorithm
Potential issues: Data/user privacy, spectral congestion, energy consumption
(as large datasets move one node to another node [3])
…

## Slide 10: Merit of Distributed Learning
Philosophy: Data samples are generated at edge devices and should always stay the edge devices [3]
  More privacy-preserving
  Better latency
  Better battery life
There are various distributed learning paradigms, e.g.,
  Federated learning (FL) [4]
  Split learning [5]

## Slide 11: How Does FL Work over a Wireless Network?
Consider the previous scenario:
STA
STA 2
STA
AP
…
…
Local dataset
Local dataset
Local dataset
An example procedure [4]:
Step 1: AP broadcasts the model
Step 2: Each STA calculates the gradients
Step 3: Each STA transmits the gradients
Step 4: AP averages the received gradients and updates the model (and goes back Step 1)

## Slide 12: How Does FL Work over a Wireless Network?
Consider the previous scenario:
STA
STA 2
STA
AP
…
…
Local dataset
Local dataset
Local dataset
An example procedure [4]:
Step 1: AP broadcasts the model
Step 2: Each STA calculates the gradients
Step 3: Each STA transmits the gradients
Step 4: AP averages the received gradients and updates the model (and goes back Step 1)

## Slide 13: How Does FL Work over a Wireless Network?
Consider the previous scenario:
STA
STA 2
STA
AP
…
…
Calculate gradients
An example procedure [4]:
Step 1: AP broadcasts the model
Step 2: Each STA calculates the gradients
Step 3: Each STA transmits the gradients
Step 4: AP averages the received gradients and updates the model (and goes back Step 1)

## Slide 14: How Does FL Work over a Wireless Network?
Consider the previous scenario:
STA
STA 2
STA
AP
…
…
Local dataset
Local dataset
Local dataset
An example procedure [4]:
Step 1: AP broadcasts the model
Step 2: Each STA calculates the gradients
Step 3: Each STA transmits the gradients
Step 4: AP averages the received gradients and updates the model (and goes back Step 1)

## Slide 15: How Does FL Work over a Wireless Network?
Consider the previous scenario:
STA
STA 2
STA
AP
…
…
Local dataset
Local dataset
Local dataset
…
Gradient averaging
& model update
An example procedure [4]:
Step 1: AP broadcasts the model
Step 2: Each STA calculates the gradients
Step 3: Each STA transmits the gradients
Step 4: AP averages the received gradients and updates the model (and goes back Step 1)

## Slide 16: Why Does [Plain] FL Work?
A typical training obtains the model parameters by solving an optimization problem
: Training dataset
A label (e.g., chair)
A data sample (e.g., image)
Detected label:
weights:

## Slide 17: Why Does [Plain] FL Work?
An iterative solution: Stochastic gradient descend (SGD) with a learning rate η

## Slide 18: Why Does [Plain] FL Work?
Assume that global data is divided into smaller datasets
We can then re-express the global gradient as a weighted summation of the local gradients
…
for
global gradient
th local gradient

## Slide 19: Why Does [Plain] FL Work?
Let’s rewrite the update rule as follows:
STA
STA 2
STA
…
…
AP
…
Gradient averaging
& model update
Uplink (UL) data: Gradient

## Slide 20: Why Does [Plain] FL Work?
Let’s rewrite the update rule as follows:
STA
STA 2
STA
…
…
AP
…
Model averaging
Uplink (UL) data: Model parameters

## Slide 21: Potential Issues for FL over a Wireless Network
Spectral efficiency & latency: A large number of parameters (e.g., ) may need to be transmitted in the UL and downlink (DL) many times and there can be many devices in the network
Wireless channel: Due to the fading, the gradients/model parameters can be lost
Data heterogeneity: The data at edge devices may not have identical distributions, which can cause bias in the learning
Device heterogeneity: Devices may have different hardware capabilities

## Slide 22: Potential Issues for FL over a Wireless Network
Spectral efficiency & latency: A large number of parameters (e.g., ) may need to be transmitted in the UL and downlink (DL) many times and there can be many devices in the network
Over-the-air computation (OAC) addresses the spectral efficiency &
latency challenge [2,6]

## Slide 23: Over-the-air Computation
Part – II

## Slide 24: Over-the-Air Computation
OAC exploits the superposition property of wireless multiple access channels to perform numerical calculations over the air [7]
…
Ideal multiple-access channel
Several “air-computable” functions: Mean,
weighted sum, polynomials, norm

## Slide 25: Over-the-Air Computation
OAC exploits the superposition property of wireless multiple access channels to perform numerical calculations over the air [7]
…
Ideal multiple-access channel

## Slide 26: Why Does It Matters? - Case: FL “without” OAC
STA
STA 2
STA
AP
…
…
Bandwidth
Time
Frequency
Occupied time
(STA 1’s gradients))

## Slide 27: Why Does It Matters? - Case: FL “without” OAC
STA
STA 2
STA
AP
…
…
Bandwidth
Time
Frequency
Occupied time
(STA 2’s gradients))

## Slide 28: Why Does It Matters? - Case: FL “without” OAC
STA
STA 2
STA
AP
…
…
…
Bandwidth
Time
Frequency
Occupied time
(STA ’s gradients))

## Slide 29: Why Does It Matters? - Case: FL “without” OAC
STA
STA 2
STA
AP
…
…
…
Bandwidth
Time
Frequency
Occupied time
…
Gradient averaging

## Slide 30: Why Does It Matters? - Case: FL “without” OAC
STA
STA 2
STA
AP
…
…
…
Bandwidth
Time
Frequency
Occupied time
…
Gradient averaging
Problem: Latency increases linearly with the number of STAs (due to orthogonal user multiplexing)

## Slide 31: Why Does It Matters? - Case: FL “with” OAC
STA
STA 2
STA
AP
…
…
Bandwidth
Time
Frequency

## Slide 32: Why Does It Matters? - Case: FL “with” OAC
STA
STA 2
STA
AP
…
…
Bandwidth
Time
Frequency
Occupied time
“One-shot” aggregation in the channel
All STAs transmit simultaneously & gradient aggregation occurs through signal superposition in the channel
…
Result: Latency does not scale with the number of STAs if OAC is employed

## Slide 33: OAC under Multi-path Channel & Noise
Wireless channel does not allow coherent addition as in an ideal channel
A typical equalization cannot be used as the superposition occurs after the impact of channels on the transmitted signals
Multi-path channel & noise?
…

## Slide 34: State-of-the Art Solutions: Precoding
Use a precoding that reverses the impact of channel and modulate OFDM subcarriers with model parameters/gradients [8]
STA
Calculate Gradients
Dataset
IDFT
CP+
Precoding
(e.g., if )
STA
DFT
CP-
aggregation
over-the-air
CP: Cyclic prefix
Shortcomings:
Channel state information (CSI) should be available at the STAs
Information related to the gradients or model parameters can be lost if the channel fades
It can be sensitive to the phase synchronization errors
STA
Model

## Slide 35: State-of-the Art Solutions: Precoding + Majority Vote
Use the sign of gradients to modulate OFDM subcarriers and determine the gradient direction at the AP with majority vote [9,10]
Advantages:
More compatible with today’s digital modulation schemes
Shortcomings:
CSI should be available at the STAs
Truncation still occurs if the channel fades
It can be sensitive to the phase synchronization errors
STA
DFT
CP-
Majority vote:
Gradient aggregation
over-the-air
STA
STA
IDFT
CP+
Precoding
(e.g., if )
Calculate Gradients
…
…
e.g.,
e.g.,
Model

## Slide 36: State-of-the Art Solutions: Non-coherent Transmission + Majority Vote
Use non-coherent transmission/detector along with the majority vote [11-14]
Advantages:
No precoding at the STAs
No CSI overhead
A low-complexity scheme
Robust against the time-synchronization errors
Shortcomings:
Probabilistic behavior due the randomness in the channel
Doubling the utilized resources
Energy detector
STA
DFT
CP-
Aggregation
over-the-air
STA
STA
Calculate Gradients
Local dataset
CP+
…
IDFT
-1
0
…
…
Energy
detector
…
-1
0
Majority vote:
Model
Majority vote:
Frequency-shift keying
Model update:

## Slide 37: State-of-the Art Solutions: Beamforming
Use heavy beamforming to mitigate the impact channel on aggregation [15]
Advantages:
No precoding at the STAs
Only an aggregate CSI (e.g., ) at AP is needed for beamforming
Robust against the time-synchronization errors
Shortcomings:
Ideally requires an infinite number of antennas
AP cost
DFT
CP-
…
STA
Calculate Gradients
Dataset
IDFT
CP+
STA
aggregation
over-the-air
STA
Model

## Slide 38: A Demonstration of OAC for FL
Part – III

## Slide 39: A Demonstration of OAC for Federated Learning
Task: Handwritten-digit recognition
  5 STAs, 1 AP, 500 images/digit (based on MNIST database)
  OAC scheme: FSK over OFDM + majority vote [14]
  Sample rate: 20 Msps, IDFT size: 256, # of active subcarriers: 192
  A neural network with 29034 parameters (~300 OFDM symbols)
  In-door environment (low mobility)
Energy detector
STA
DFT
CP-
STA
STA
Calculate Gradients
Local dataset
CP+
…
-1
0
…
…
Energy
detector
…
-1
0
Model
Frequency-shift keying
IDFT
Majority vote:
Majority vote:
Model update:

## Slide 40: A Demonstration of OAC for Federated Learning
STA1
STA 2
STA 5
STA 3
STA 4
AP
1st round:
AP transmits a trigger signal
Trigger
Majority votes
AP:
STA 1:
STA 2:
STA 3:
STA 4:
STA 5:
Sign of local gradients
Sign of local gradients
Sign of local gradients
Sign of local gradients
Sign of local gradients

## Slide 41: A Demonstration of OAC for Federated Learning
STA1
STA 2
STA 5
STA 3
STA 4
AP
1st round:
Simultaneous transmissions of
signs of local gradients
with FSK over OFDM
Trigger
Sign of local gradients
Sign of local gradients
Sign of local gradients
Sign of local gradients
Sign of local gradients
AP:
STA 1:
STA 2:
STA 3:
STA 4:
STA 5:
Signal superposition (Encoding for each STA: FSK over OFDM)
Majority votes

## Slide 42: A Demonstration of OAC for Federated Learning
STA1
STA 2
STA 5
STA 3
STA 4
AP
1st round:
Simultaneous transmissions of
signs of local gradients
with FSK over OFDM
Uplink channels

## Slide 43: A Demonstration of OAC for Federated Learning
STA1
STA 2
STA 5
STA 3
STA 4
AP
1st round:
AP calculates
and broadcast
the majority votes
Trigger
Majority votes
AP:
STA 1:
STA 2:
STA 3:
STA 4:
STA 5:
Sign of local gradients
Sign of local gradients
Sign of local gradients
Sign of local gradients
Sign of local gradients

## Slide 44: A Demonstration of OAC for Federated Learning
STA1
STA 2
STA 5
STA 3
STA 4
AP
1st round:
AP broadcasts
the majority votes
Subcarriers
Subcarriers
Subcarriers
e.g,
Subcarriers
Superposed
symbols at the AP:
Majority vote:
STA :
STA :
STA :
-1
0
FSK

## Slide 45: A Demonstration of OAC for Federated Learning
STA1
STA 2
STA 5
STA 3
STA 4
AP
1st round:
STAs update their models
Trigger
Majority votes
AP:
STA 1:
STA 2:
STA 3:
STA 4:
STA 5:
Sign of local gradients
Sign of local gradients
Sign of local gradients
Sign of local gradients
Sign of local gradients

## Slide 46: A Demonstration of OAC for Federated Learning
For this scenario, the test accuracy reaches to 97% while the training loss gradually decreases without sharing the local datasets

## Slide 47: Takeaways
Wireless for ML and ML for wireless are the two fundamental paths for combining ML and communications
  Distributed learning is a use case that can affect the design of a wireless network for AI/ML
OAC is a promising way to address the latency challenge of implementation of distributed learning over wireless networks
  Signal superposition in multiple access channels turns out to be a useful phenomenon to compute some functions
  Power control, time-frequency synchronization, CSI acquisition, retransmissions, and compression are several other major aspects for achieving reliable OAC

## Slide 48: References
[1] T. O’Shea and J. Hoydis, “An introduction to deep learning for the physical layer,” IEEE Transactions on Cognitive Communications and Networking, vol. 3, no. 4, pp. 563–575, Dec. 2017.
[2] H. Hellstrom, J. M. B. da Silva Jr, M. Chen, V. Fodor, V. Poor, and C. Fischione, “Wireless for Machine Learning: a Survey,” Foundations and Trends® in Signal Processing, vol. 15, no, 4, pp. 290-399, 2022
[3] P. K. et. al., “Advances and open problems in federated learning,” Foundations and Trends® in Machine Learning, vol. 14, no. 1–2, pp. 1–210, 2021.
[4] H. B. McMahan, E. Moore, D. Ramage, S. Hampson, and B. A. y Arcas, “Communication-efficient learning of deep networks from decentralized data,” 2017.
[5] A. Singh, P. Vepakomma, O. Gupta, and R. Raskar, “Detailed comparison of communication efficiency of split learning and federated learning,” ArXiv, vol. abs/1909.09145, 2019.
[6] M. Chen, D. Gunduz, K. Huang, W. Saad, M. Bennis, A. V. Feljan, and H. V. Poor, "Distributed Learning in Wireless Networks: Recent Progress and Future Challenges," in IEEE Journal on Selected Areas in Communications, vol. 39, no. 12, pp. 3579-3605, Dec. 2021
[7] M. Goldenbaum, H. Boche, and S. Stanczak, “Harnessing interference for analog function computation in wireless sensor networks,” IEEE Trans. Signal Process., vol. 61, no. 20, pp. 4893–4906, Oct. 2013.
[8] G. Zhu, Y. Wang, and K. Huang, “Broadband analog aggregation for low-latency federated edge learning,” IEEE Trans. Wireless Commun., vol. 19, no. 1, pp. 491–506, Jan. 2020.
[9] G. Zhu, Y. Du, D. Gunduz, and K. Huang, “One-bit over-the-air aggregation for communication-efficient federated edge learning: Design and convergence analysis,” IEEE Trans. Wireless Commun., vol. 20, no. 3, pp. 2120–2135, Nov. 2021.
[10] J. Bernstein, Y.-X. Wang, K. Azizzadenesheli, and A. Anandkumar, “signSGD: Compressed optimisation for non-convex problems,” in Proc. in International Conference on Machine Learning, vol. 80. Proceedings of Machine Learning Research, 10–15 Jul 2018, pp. 560–569.
[11] S. Hoque, M. H. Adeli, A. Sahin, "Chirp-Based Over-The-Air Computation for Long-Range Federated Edge Learning," IEEE International Symposium on Personal, Indoor and Mobile Radio Communications (PIMRC), 2022
[12] M. H. Adeli, A. Sahin, "Multi-cell Non-coherent Over-the-Air Computation for Federated Edge Learning," IEEE International Conference on Communications (ICC), 2022
[13 ]A. Sahin, B. Everette, S. Hoque, "Over-the-Air Computation with DFT-spread OFDM for Federated Edge Learning," IEEE Wireless Communications and Networking Conference (WCNC), 2022
[14] A. Sahin, B. Everette, S. Hoque, "Distributed Learning over a Wireless Network with FSK-Based Majority Vote," IEEE International Conference on Advanced Communication Technologies and Networking (CommNet), 2021
[15] M. M. Amiria, T. M. Duman, D. Gunduz, S. R. Kulkarni, and H. Vincent Poor, “Collaborative machine learning at the wireless edge with blind transmitters,” IEEE Trans. Wireless Commun., pp. 1–1, Mar 2021.