## Slide 1: Considerations on Multi-AP Coordination
Date: 2022-09-14
Authors:
Name | Company | Address | Phone | Email
Yusuke Tanaka | Sony Group Corporation |  |  | Yusuke.YT.Tanaka@sony.com
Kosuke Aio |  |  |  | Kosuke.Aio@sony.com
William Carney |  |  |  | William.Carney@sony.com

## Slide 2: Introduction
Multiple AP environment and AP coordination technology were discussed in the recent WNG sessions and previously EHT SG/TGbe as worthwhile topics for the next generation WLAN.
This contribution reviews discussions related to AP coordination during the WNG sessions and EHT SG/TGbe. Based on the observation, this contribution proposes some way forwards for the future discussion.

## Slide 3: Review of WNG discussion (1/2)
Various envisioned use cases were proposed during WNG, and diverse requirements to realize them were shown.
In consideration of those proposals, the motion to form UHR SG with the following multiple objectives was approved.
  Improve reliability of WLAN connectivity
  Reduce latencies
  Increase manageability
  Increase throughput at different SNR levels
  Reduce device level power consumption
To meet these objectives, it is effective to give priority to features that are able to address several objectives with one feature.
  It is possible to reduce the amount of amendment and standardization work, and to allocate standardization resources to other complementary features.

## Slide 4: Review of WNG discussion (2/2)
AP coordination are able to address the several objectives by its coordination subtypes.
  Coordinated OFDMA: Multiple APs coordinate RUs and perform OFDMA.
  Coordinated Spatial Reuse: Multiple APs coordinate or instruct transmission parameters (e.g., transmission power) and perform spatial reuse.
  Coordinated Beamforming: Multiple APs form beam/null so as not to interfere with each BSSs.
  Joint Transmission: Multiple APs transmit to the same single or multiple STAs simultaneously as if these are a single AP.
  All subtypes enable parallel transmission without waiting and achieve low latency.
  All subtypes enable collision avoidance between APs and achieve high reliability.
  All subtypes are able to improve throughput. Principles differs for each subtype (better spectrum utilization, interference reduction etc.), and the amount of improvement is generally large in the order of 4. (largest) > 3. > 2. > 1. > no coordination.

## Slide 5: Observation and way forwards
Many contributions[1-6] also expect that AP coordination is a mean to achieve the objectives and realize the use cases.
Considering these points, AP coordination is a potential feature and should be prioritized in UHR discussion.
Proposed way forwards based on the review of WNG discussion:
  AP Coordination should be prioritized in UHR SG, and discussion about coordination subtypes, network structure, and performance evaluation should be proceeded.
  Multi-AP environment and/or AP coordination should be captured in the PAR to be constructed, but it is a future discussion.

## Slide 6: Review of EHT SG/TGbe discussion (1/3)
The following items had been profoundly discussed, and the useful fruits are provided as contributions and are available for reuse.
Terminology [7], [8]
  “Coordinated” techniques and “Joint” techniques
  “Sharing AP” & “Shared AP”
Coordination type [7], [9]
  Joint processing (transmission/reception)
  Coordinated OFDMA, Coordinated Spatial Reuse
  Coordinated Beamforming, Coordinated Nulling
Scenario [10]
  “Home Mesh AP Scenario” and detailed parameters

## Slide 7: Review of EHT SG/TGbe discussion (2/3)
Spec Framework Document [11]
  The TGbe SFD included a subclause about Multi-AP, “9. Multi-AP operation,” based on a bunch of approved motions. Below is a summary of what each subclause contains.
9.1 General
9.2 Setup
  Definition of “sharing AP” and “shared AP”
  Primary 20MHz setting in sharing AP and shared AP
9.3 Channel sounding
  Joint NDP sounding scheme
  Sequential 11ax-like sounding sequence to collect CSI from in-BSS/OBSS STAs
  NDPA frame and BFRP Trigger frame design (OBSS STA’s ID) and behavior of STA received the frames from OBSS AP

## Slide 8: Review of EHT SG/TGbe discussion (3/3)
  9.4 Coordinated transmission
  AP candidate set (APs that can initiate or participate in multi-AP coordination)
  A procedure for an AP to share its frequency/time resources
  Optional feedback from APs from the AP candidate set to learn the resource needs
  Coordinated OFDMA
  Coordinated UL MU-MIMO
  9.5 Other Multi-AP coordination schemes
  Coordinated spatial reuse
  Joint transmission for single- and multi-user
  Coordinated BF

## Slide 9: Observation and way forwards
The SFD well covers basic definitions and procedures, as well as descriptions of support of high-level coordination subtypes.
Proposed Way Forwards based on review of EHT SG/TGbe discussion
  Related agreements for Multi-AP and previously approved as motions in the TGbe SFD, should carry over to UHR to allow faster progress on completing the PAR and spec development.
    Minor changes like subclause structure or Notes could be considered.
    Modification based on changes since then (e.g. Multi-Link feature) should be reexamined.

## Slide 10: Summary
This contribution reviewed the discussions about AP coordination during the WNG sessions and EHT SG/TGbe.
This contribution offered following way forwards based on the observation from the review.
  AP Coordination should be prioritized in UHR SG, and discussion about coordination subtypes, network structure, and performance evaluation should be proceeded.
  Related agreements for Multi-AP and previously approved as motions in the TGbe SFD, should carry over to UHR to allow faster progress on completing the PAR and spec development.

## Slide 11: Reference
    [1] 22/734 “Next Gen After 11be: Main Directions Proposal”
    [2] 22/729 “802.11 GEN8 Study Group”
    [3] 22/932 “Thoughts on Beyond 802.11be”
    [4] 22/965 “View on Beyond BE”
    [5] 22/694 “Thoughts on Next Gen WLAN”
    [6] 22/697 “Next-generation WLAN technology inspired by XR”
    [7] 18/1926 “Terminology for AP Coordination”
    [8] 19/1895 “Setup for Multi-AP coordination”
    [9] 18/1509 “Discussions on Multi-AP Coordination”
    [10] 20/0032 “Consideration on Multi-AP Home Mesh AP Scenario”
    [11] 19/1262 “Specification framework for TGbe”