## Slide 1: P2P Communication with EMLSR Peer in Triggered TXOP Sharing
Date: 2022-09-15
Authors:
Name | Affiliation | Address | Phone | Email
Sunghyun Hwang | ETRI |  |  | shwnag@etri.re.kr
Kyumin Kang | ETRI |  |  | kmkang@etri.re.kr
Juseong Moon | KNUT |  |  | jsmoon0211@ut.ac.kr
Ronny Yongho Kim | KNUT |  |  | ronnykim@ut.ac.kr

## Slide 2: Abstract
P2P communications with EMLSR operating non-AP STA MLD peer is not defined
Since EMLSR operating non-AP STA MLD can not receive PPDU without Initial Control Frame, a non-AP STA can not initiate P2P communication.
In this submission, P2P communication with EMLSR operating non-AP STA MLD is discussed.

## Slide 3: Related CID in LB266
12422 | Yongho Kim | Yes | 35.2.1.2.2 | 402 | 55 | When EMLSR STA MLD (or STA affiliated with EMLSR STA MLD) is recipient of P2P, EMLSR operating STA can not receive PPDU from non-AP STA without initial control frame. | Please define a procedure to communication with EMLSR operating STA in triggered TXOP sharing mode 2.

## Slide 4: P2P with EMLSR operating non-AP STA MLD - Issue
EMLSR-operating non-AP STA MLD can not receive a PPDU without the reception of the initial control frame
If P2P recipient peer is an EMLSR-operating STA, how P2P transmitter change the EMLSR-operating P2P recipient STA status from listening operation to EMLSR operation?
In this contribution, in TXOP triggered TXOP sharing, several options for a STA to initiate P2P communication with EMLSR operating peer STA are discussed.

## Slide 5: EMLSR Compatible Triggered TXOP Sharing
Option 1. AP-Assisted EMLSR Mode Change
  On behalf of a STA, AP transmits an Initial Control Frame to the EMLSR operating STA
  AP’s ICF transmission can be requested by P2P peer STA to which time is allocated.
Option 2. New TXS Mode
  Make new TXS mode (e.g., mode 3)
  If EMLSR STA receives MU-RTS TXS frame with new mode, it should participate P2P communication
Option 3. Allowing P2P sender to transmit ICF
  P2P sender STA transmits ICF to EMLSR operating STA
  P2P sender can transmit P2P data to EMLSR operating STA without AP’s assistance

## Slide 6: Option 1. AP-Assisted Mode Change
When EMLSR operating STA is the recipient of P2P, AP transmits an ICF to the EMLSR operating STA
  P2P sender STA should transmit information about recipient STA to AP

## Slide 7: Option 2. New TXS Mode
MU-RTS with new TXOP Sharing mode (e.g., TXS mode 3)
  P2P sender STA should transmit information about recipient STA to AP
  EMLSR-operating STA(s), that has set up P2P, should participate TXS if received MU-RTS TXS frame with new TXS mode

## Slide 8: Option 3. Allow P2P sender to transmit ICF
Allow P2P sender STA to transmit initial control frame
  AP’s assistance or information change with AP is not required

## Slide 9: Conclusion
P2P communication with EMLSR operating STA was discussed
  Option 1: AP-Assisted EMLSR Mode Change
  Option 2: New TXS Mode
  Option 3: Allowing P2P sender to transmit ICF

## Slide 10: Straw Polls
Straw Poll #1
  Do you support the Option 1, AP-Assisted EMLSR Mode Change, for P2P operation of EMLSR P2P Peer STA in 11be?
  Y / N / A
Straw Poll #2
  Do you support the Option 2, New TXS mode, for P2P operation of EMLSR P2P Peer STA in 11be?
  Y / N / A
Straw Poll #3
  Do you support the Option 3, Allowing P2P sender to transmit ICF, for P2P operation of EMLSR P2P Peer STA in 11be?
  Y / N / A
Straw Poll #4
  Do you not support all these options for P2P operation of EMLSR P2P Peer STA in 11be?
  Y / N / A