## Slide 1: EDCAF Selection Issue on Start Time Sync Access
Date: 2022-09-12
Authors:
Name | Affiliation | Address | Phone | Email
Juseong Moon | KNUT |  |  | jsmoon0211@ut.ac.kr
Ronny Yongho Kim | KNUT |  |  | ronnykim@ut.ac.kr
Hyojin Jung | Hyundai Motor Company |  |  | hyojin@hyundai.com

## Slide 2: Abstract
With start time sync PPDUs access defined in 802.11be Draft 2.1.1, a STA can select only one EDCAF among multiple EDCAFs with backoff counter 0 for a link
It’s needed to clarify the case of a STA with multiple EDCAFs whose backoff counter are 0 in start time sync access
In the case of transmitting from the selected one EDCAFs among EDCAFs with backoff counter 0, there are two possible cases for the not selected EDCAFs: 1. keeping backoff counter 0 and 2. invoke new backoff counter
In this contribution, start time sync PPDUs access for unselected EDCAFs is discussed

## Slide 3: Start time sync PPDUs access - Issue
12414 | Juseong Moon | Yes | 35.3.16.6 | 458.14 | When there are multiple EDCAF backoff counters that already reached zero and one EDCAF is chosen with implementation specific method, it is not clear what the expected behavior for the rest of EDCAFs with zero backoff counter. Do they re-invoke the backoff procedure with doubled CW value assuming an internal collision? Clear description on the post procedure of implementation specific one EDCAF selection is required.

## Slide 4: Start time sync PPDUs access - Issue
In 802.11be draft 2.1.1, subclause 35.3.16.6, page 473
  A STA that chooses not to transmit after the backoff counter reached zero on a link of NSTR link pair may have one or more EDCAF backoff counters with value zero on that link. The STA that initiates transmission on that link following condition a) or b), and has one or more EDCAF backoff counters that already reached zero shall choose only one implementation specific EDCAF for the transmission.
There are no following actions for not-chosen EDCAFs
  keeping backoff counter 0
  invoke new backoff counter

## Slide 5: Start time sync PPDUs access – Keeping backoff counter 0
A paragraph on line 17 may be applied.
  A STA with backoff counter that has already reached zero on a link and has a frame available for transmission shall follow channel access procedures described in 10.23.2.4 (Obtaining an EDCA TXOP) after it detect medium transition from busy to idle.
"A STA with backoff counter that has already reached zero" may have more than two EDCAFs with backoff counter 0.
Then, a STA needs to choose one EDCAF.
A description on how to select one EDCAF if there are multiple EDCAFs with backoff counter 0 is required.

## Slide 6: Start time sync PPDUs access – invoke new backoff counter
For Not-chosen AC(s) and EDCAFs
  Do they invoke backoff with previous CW[AC] and QSRC[AC]?
  Do they invoke backoff with increased CW[AC] and QSRC[AC]?

## Slide 7: Start time sync PPDUs access – invoke new backoff counter
EDCAFs that has not been chosen can invoke new backoff, and there are some cases
  Case 1: CW[AC] and QSRC[AC] are left unchanged
  Case 2: CW[AC] is doubled, and QSRC[AC] is increased
If Case 2 is selected, backoff period for not-chosen EDCAFs will increased
Since channel access operation for NSTR operation doesn’t have priority than STR or single-link channel access, Case 2 should not be selected, but Case 1 should be selected

## Slide 8: Start time sync PPDUs access – invoke new backoff counter
Case 1
  CW[AC] and QSRC[AC] are left unchanged

## Slide 9: Start time sync PPDUs access – invoke new backoff counter
Case 2
  CW[AC] and QSRC[AC] are increased
  Decreased performance for NSTR non-AP MLD

## Slide 10: Conclusion
Not-chosen ACs in start time sync PPDUs access was discussed
It is preferred to keep CW[AC] and QSRC parameters of not-chosen ACs unchanged in start time sync PPDUs access
  If CW[AC] is doubled, it may degrade the performance of EDCAFs that are not chosen in NSTR link pair