## Slide 1: A Timing Problem of Sequential Coordinated Monostatic DMG Sensing
Date: 2022-09-09
Authors:
Name | Affiliation | Address | Phone | Email
Ning Gao | OPPO |  |  | gaoning1@oppo.com
Chaoming Luo |  |  |  | luochaoming@oppo.com
Pei Zhou |  |  |  | zhoupei1@oppo.com

## Slide 2: Abstract
The Coordinated Monostatic DMG Sensing instance has two types: sequential and parallel.
In this contribution, a timing problem of sequential Coordinated Monostatic DMG Sensing instance is shown and three possible solutions for this timing problem are proposed and compared.

## Slide 3: Timing Problem in Sequential Coordinated DMG Monostatic Sensing Instance
The STA B may not get the accurate timing when to send the Monostatic PPDU.
  The Ack frame is directionally sent from the initiator to the STA A so the STA B may not receive it.
  The length/duration of the Monostatic PPDU and the DMG Sensing Measurement Report frame of STA A are unknown to STA B.
As a result, the STA B may fail to send the Monostatic PPDU and the DMG Sensing Measurement Report frame or cause interference between STAs in this instance.

## Slide 4: Should we set scheduling for each STA?
It is not a good approach.
  It is complicated for the initiator to set scheduling information for multiple responder STAs in each DMG Sensing Request frame.
    The length/duration of the Monostatic PPDU(Not defined)and the DMG Sensing Measurement Report frame(Different MCSs) of different STAs can be different.
    So, each responder STA needs to inform the initiator of the above information in the Measurement Setup phase.
    Then, in every instance, the initiator shall schedule each STA except the first to send a Monostatic PPDU no later than SIFS time after the Ack frame of the previous STA.
    Note that the number and the order of responder STAs in each instance may be different.
Use a poll frame to poll each STA is a better way.

## Slide 5: Option 1-A
In every instance, the initiator poll each responder sequentially with a new poll frame (format is TBD) before each responder STA sending a Monostatic PPDU.

## Slide 6: Option 1-B
In every instance, the initiator poll each responder except the first responder sequentially with a new poll frame(format is TBD) before each responder STA sending a Monostatic PPDU.
No new poll frame

## Slide 7: Option 2
Each responder STA sends the Monostatic PPDU no later than SIFS time after the DMG Sensing Response frame.
The initiation, sounding and reporting phases are repeated per responder STA in each instance.

## Slide 8: Comparison
Option | Pros. | Cons.
Opt.1-A | Same procedure for all STAs | Need to define a new frame More overhead (poll frame for each STA)
Opt.1-B | Little overhead (no poll frame for the first STA) | Need to define a new frame Different procedure for the first STA
Opt.2 | No need to define a new frame Same procedure for all STAs | Much more changes to the current procedure

## Slide 9: SP 1
Which option do you support to solve the timing problem of the sequential Coordinated Monostatic DMG Sensing instance as shown in slide 3?
  Option 1-A: use a new poll frame to poll each responder STA, as shown in slide 5
  Option 1-B: use a new poll frame to poll each responder STA except the first, as shown in slide 6
  Option 2: use the DMG Sensing Request frame to poll each responder STA, as shown in slide 7
  Neither
  Abstain