## Slide 1: Views on UHR
Date: 9/9/2022
Authors:

## Slide 2: Introduction
802.11 WG agreed the formation of an Ultra High Reliability Study Group (UHR SG)
SG will develop PAR an CSD to further define scope and features
In this presentation, we offer some thoughts and comments on various aspects of this activity
  Content
  Working approach

## Slide 3: Need for new PHY and MAC clauses
Previous similar amendments (“generational” amendments) have produced new PHY and MAC clauses (11ac, 11ax, 11be)
The set of features envisioned for UHR does not appear to call for such an approach
  In fact, many features used to part of “11be R2”
  11be preamble was designed with forward compatibility in mind
    Able to accommodate new PHY versions
    Able to add features to 11be through use of Reserved bits (Validate/Disregard) without need to change the preamble
  Previous generations reluctant to use reserved bits
    Purpose of these bits for 11be has been made very clear and should be exploited
Our preference is to maintain the 11be PHY version and primarily rely on use of (currently) reserved bits to extend the feature set

## Slide 4: Organization of the work
11be attempted a multi-release approach to achieve a “two-year cadence”
  Approach appears not to have worked
802.11 process does not naturally accommodate such an approach
  Comment resolution should not be used for continued design
If a shorter timeframe is desired, the amendment should be scoped accordingly
  Fit content to the time window, agree an a priori split of content
  Consider multiple projects if a split is feasible
Multiple phases = multiple amendments

## Slide 5: Questions on Use of additional spectrum above 45 GHz
This item needs further clarification
  Is this only in the context of MLO?
    E.g., Generic MAC interface for MLO?
    If so, is required specification limited to MAC definition, using existing PHY clauses (e.g., 11be & 11ay)?
  Or: is it the intention to unify PHY across < 7 GHz and > 45 GHz bands?
    No need for a new PHY below 7 GHz
    Unlikely that 11be PHY can simply be ported to above 45 GHz, given the specifics of the channel
    802.11ay-2021 just defined an updated PHY above 45 GHz
Novel use of spectrum above 45 GHz may be more appropriate as a separate activity
  Separate topics that are largely orthogonal into separate amendments

## Slide 6: Thoughts on PAR
Have a list of clearly defined features in PAR
  Flexibility is needed, but don’t leave scope too open-ended
  Keep focus
    no all-purpose amendment
    consider multiple activities/amendments if appropriate
      for comparison: see 11bh/11bi – two TGs resulting from RCM TIG/SG
Address some of the questions raised in previous slides within the PAR to establish a baseline understanding on these topics

## Slide 7: What next for 11be R2?
It appears UHR is largely incorporating features once envisioned for 11be R2
11be work should be re-scoped accordingly
Outside of scope of UHR, but 802.11 as a group needs to organize both activities to avoid overlap/duplication
Abandon 11beR2
  finalize outstanding comments instead?
  No major new features

## Slide 8: View on proposed features
Topic | Thoughts | Include?
Wider BW | Part of natural evolution. Fits in well with next-gen activity | Y
Additional SS |  | 
Coordinated Multi-AP | Discussed for 11be. Make sense to address this as part of new activity | Y
Joint Multi-AP | Discussed for 11be. May need further discussion of specific modes to be included | TBD
Latency-sensitive enhancements | Clear market need | Y
Spectrum above 45 GHz | Need to address open questions (see slide 5). DMG has its own track of amendments. | TBD
Miscellaneous | Incremental enhancements are natural for a new-generation project. Decide case-by-case to maintain coherent scope. | TBD
Full Duplex | We have had a SG before | N