## Slide 1: C-OFDMA throughput analysis in various mesh backhaul scenarios
Date: 9/9/2022
Authors:

## Slide 2: Abstract
We consider C-OFDMA added to (in-home) “mesh” network
We consider several backhaul scenarios
We evaluate possible throughput enhancement

## Slide 3: Introduction
Many residential deployments already use “mesh” topology
  One “Main” AP connected to internet
  Secondary AP(s) serve subset of STAs and forward traffic from the main AP
  Goal of mesh topology is to extend range of data delivery
We consider addition of C-OFDMA to this scenario as a possible incremental improvement to overall throughput
  “natural” evolution of mesh deployments
  SR, nulling, … more appropriate for OBSS scenarios instead
We evaluate aggregate throughput of C-OFDMA vs. SU-only transmissions

## Slide 4: Definitions
C-OFDMA
  Form of Multi-AP coordination
  One AP (“Sharing AP”) initiates channel access and inquires about requested resources from other APs (“Shared APs”)
  Based on feedbacks from Shared APs, the Sharing AP allocates final resources among all participating APs
    Allocations are in the frequency domain
  All participating APs send concurrently occupying their allocated resources
Backhaul
  Traffic from Sharing AP to Shared APs intended for connected STA(s)
Fronthaul
  Traffic between an AP and its connected STA(s)

## Slide 5: Why evaluate C-OFDMA throughput improvement?
OFDMA is not typically associated with throughput improvements in high-traffic scenarios
  Resources are shared between multiple users, no new resources created
  Only when MAC overhead dominates data (e.g., preponderance of short packets), some performance benefit is seen
  Latency improvements may be of more interest
C-OFDMA has some inherent benefits relative to OFDMA that make throughput evaluation worthwhile:
  Airtime benefit: Less contention/collisions compared to SU with hops
    Single AP effectively controls all network access
  Power benefit: Several APs can transmit simultaneously at full power
    Higher MCS possible when using part of the band (i.e. when doing OFDMA)

## Slide 6: Simulation Scenarios
Single AP serves whole network
    Two remote devices
  Mesh topology - SU only
    Two secondary mesh APs
    SU for backhaul and AP-STA links
    All transmissions on the same channel
  Mesh topology with C-OFDMA
    Higher MCS due to power gain
    SU for Backhaul
    Whenever possible, C-OFDMA for fronthaul links
    AP1 initiates C-OFDMA
    All transmissions on the same channel

## Slide 7: Evaluation Methodology
Target: Maximize aggregate network throughput
  Which configuration provides highest aggregate throughput?
    As measured between traffic endpoints, i.e., excluding any backhaul traffic
Typical Methodology:
  Full buffer scenario: pump high data rate to each of the STAs
  Excess packets are dropped from Tx buffer
  Aggregate performance determined by network conditions
This methodology does not work for C-OFDMA
  Excess packets are delivered over the backhaul from the Sharing AP to the Shared APs and are only dropped from the Tx buffer of the Sharing AP
    Airtime is spent transmitting backhaul packets that will not be sent from Sharing AP to its STA
  This creates Backhaul inefficiency

## Slide 8: Backhaul inefficiency in C-OFDMA illustrated
Non-full buffer scenario: all traffic delivered. No throughput difference between SU and C-OFDMA
Backhaul delivers amount of traffic that matches AP-STA link capacity
Backhaul delivers more traffic than can be handled by the Sharing AP-STA link. “Wasted” airtime reduces overall network performance.
Backhaul airtime usage maxes out. Further increases in data rate do not cause further reduction in airtime availability.
SU operation independent of traffic rates

## Slide 9: Backhaul inefficiency in C-OFDMA
Happens when Fronthaul and Backhaul share the same channel
  Allows for simpler devices
  Will evaluate alternative scenarios later
Hard to match backhaul transmissions to AP-STA link capacities without inefficiency
  Either backhaul too high, leading to backhaul transmission of packets that will ultimately be dropped at the Sharing AP
  Or backhaul traffic may be too low to fully utilize capacity of the Shared AP-STA link
Not just a testing/simulation issue:
  If Shared AP-STA link is oversubscribed, it will impact overall network capacity because of excess airtime used by the backhaul
    “excess” = backhaul delivers more data than final link can support

## Slide 10: Simulation assumptions
To avoid the backhaul inefficiency in C-OFDMA, traffic rates for C-OFDMA scenario are gradually increased to find the optimum
Backhaul runs independently: no synchronization with C-OFDMA, always uses SU
Padding in C-OFDMA frames is minimized
Basic C-OFDMA protocol elements are accounted for

## Slide 11: Simulation Results (3 AP scenario)
Minor performance improvement from C-OFDMA
  Requires fine tuning of backhaul
C-OFDMA gains from:
  Collision avoidance
  Higher MCS
C-OFDMA overhead:
  Additional protocol
  Possible backhaul inefficiency

## Slide 12: Alternative backhaul scenarios
Key issue in previous simulations is the Wireless Backhaul sharing the same medium as fronthaul data, which leads to inefficiencies
Alternatives include:
  Off-channel wireless backhaul
    “hides” the backhaul inefficiency issue
    Increase in needed wireless resources
  Wired backhaul
    Especially in in-home deployment scenarios, a wired alternative may be available
    Does not impact wireless spectrum availability
Packet forwarding can be done at higher layers

## Slide 13: Simulation Results (3 AP scenario)
Throughput significantly higher for both SU and C-OFDMA
  In-channel Wireless backhaul represents significant part of overall airtime consumption
  Inefficiency avoided
    Or rather, “hidden” off-channel
Some gain between SU and C-OFDMA

## Slide 14: Conclusions
We have evaluated possible performance improvement of C-OFDMA over SU in an in-home scenario
Use of wireless backhaul in C-OFDMA on the same channel leads to several inefficiencies
  Less airtime available to data
  Inefficiency in matching backhaul to actual data requirement when using C-OFDMA
Wired backhaul or off-channel wireless backhaul eliminates both types of inefficiency in-channel
  Extra resources are used off-channel
  Backhaul inefficiency (backhaul/fronthaul mismatch) may still exist off-channel

## Slide 15: Conclusions
C-OFMDA does provide some (minor) throughput gain over SU-only
  Most gain from moving the backhaul off-channel
  Latency remains to be evaluated
Backhaul and fronthaul need to be matched to avoid resource inefficiency
Multi-AP specification should be compatible with both wireless and wired backhaul scenarios
  Coordinated operation can accommodate this easily
  Joint operation may require explicit format definition

## Slide 16: Back-up slides

## Slide 17
Airtime Usage Multi-AP without C-OFDMA
Airtime Usage Multi-AP with C-OFDMA (optimal backhaul)

## Slide 18
Airtime Usage Multi-AP with C-OFDMA (inefficient backhaul)
Airtime Usage Multi-AP with C-OFDMA (optimal backhaul)
Backhaul
Backhaul