## Slide 1: Some questions to answer for UHR PAR
Date: 2022-08-25
Authors:
Name | Affiliation | Address | Phone | Email
Laurent Cariou | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-712-5560 | laurent.cariou@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com
Carlos Cordeiro |  |  |  | carlos.cordeiro@intel.com
September 2022

## Slide 2: Main technical questions that the SG must answer
Motion text for SG formation:
Approve formation of Ultra High Reliability SG (UHR SG) to develop a Project Authorization Request (PAR) and a Criteria for Standards Development (CSD) for a new 802.11 MAC/PHY amendment. The Study Group will investigate technology which may improve reliability of WLAN connectivity, reduce latencies, increase manageability, increase throughput including at different SNR levels and reduce device level power consumption.
With a target start of the task group in May 2023
Questions to answer in the SG:
We need to ensure that there are realistic and beneficial features for different main market segments (home, enterprise, …) and for both APs and clients in the scope of UHR
We need to determine what are the operating bands that are targeted by UHR
We need to refine the objectives and see if we need to quantify them
  Will be dealt with in other contributions
September 2022

## Slide 3: Main features identified so far
Multi-AP set of features in sub-7 GHz (seems well accepted)
  different flavors of cooperation between APs. (C-TDMA, C-OFDMA, C-SR, C-BF, MU-MIMO JP). Targets multiple objectives: throughput, latency, range, area throughput, reliability, …
  Deployment scenario of interest: Home, Enterprise
60 GHz and other spectrum (many undecided)
  include a 60GHz interface to mainstream Wi-Fi, reusing as much as possible low band baseband and design to reach an acceptable cost and ease integration
  reach 6G latency objectives with more guarantees, deliver huge capacity increase with large frequency reuse, peak throughput increase and controlled interference
Low latency/QoS features (seems well accepted)
  More scheduling, more protection for prioritized traffic…
September 2022

## Slide 4: Features for client devices
Paramount to have clear lighthouse features for clients in UHR, and features that will have performance impact
  No relevant/realistic lighthouse client features in lower bands identified so far
    Bandwidth higher than 320MHz at 6 GHz will not be usable in real deployments as discussed in previous contributions
    Some good features/ideas but that are more secondary features
      A-PPDU, link adaptation, secondary channel access/puncturing, …
We believe mmWave operation is the most relevant feature that rises to the level of a lighthouse feature, that can be advertised by clients, and that matches the UHR objectives
  See 22/1093r1 22/729r1 22/030r1 22/046r1
September 2022

## Slide 5: Operating band for UHR
Why including mmWave in next gen Wi-Fi?
  Opens new long term Wi-Fi roadmap, including > 10 Gbps TPT and new usages/features
  Opens path to develop integrated comms and sensing solutions
  Wi-Fi industry will have competitive mmWave offering to cellular
  STD development timeline will likely extend - lots of new features
    Right time to scale the technology, and this will be the starting point for a long list of features/enhancements
  A strong lighthouse client feature
Plurality of mmWave benefits for all UHR use cases and KPIs
  Throughput:
    If we don’t do it, single user throughput will not have meaningful improvement at least until Wi-Fi 9 (2031!), No practical line of sight for > 10 Gbps Wi-Fi
  Capacity/low latency:
    natural reduced latency of every transmission
    14 GHz of spectrum allows for huge increase in frequency reuse, especially with 320MHz channels (43 non overlapping channels), leading to each link (AP-STA) using a part of the spectrum on its own without any interference
      guaranteed QoS (latency, throughput, QoS, …) even in very dense environments
September 2022

## Slide 6: Limit the scope for mmWave in UHR
We believe it’s important to define clearly the scope of what will be defined for mmWave in this UHR generation
Benefits from simply operating in mmWave band is already so significant that we don’t need to define more features to further optimize operation.
  Optimizations can be brought in future generations
  This will significantly help meet the target timeline
For example, we believe we simply need Single User transmissions
  No need to define multi-user operation (MU-MIMO, OFDMA, …)
The only components that would then be essential and in scope for mmWave operation in UHR would be:
  PHY design for OFDM operation for different bandwidth (between 160MHz to 1280MHz for instance)
    Reusing as much as possible lower band design by using upclocking
  Simple Beamforming training sequence
  Minor adaptations to Multi-link operation
September 2022

## Slide 7: PHY Design for mmWave interface by reusing lower band design
The proposal is not to use 11ad/ay
The proposal is to reuse existing lower band Wi-Fi solution (Modem/PHY, MAC and SW) and upclock it to operate on mmWave band
  Minimize complexity, ease integration
  Reuse as much as possible of legacy .11 algo/architecture  save algo/design/validation efforts
Operating bandwidth in mmWave in the range between around 160 MHz and 1280 MHz (160/320/640/1280…)
  Allow modes for 10Gbps (1280), allow modes with huge number of non-overlapping channels (160/320)
This direction is a game-changer as, compared to 11ad/ay, it brings complexity to levels that we believe are realistic for high-end Wi-Fi devices, while matching UHR objectives
September 2022

## Slide 8: mmWave operation with MLO
We consider that all devices operating in mmWave shall be MLO-capable and shall have at least one affiliated STA/AP in the lower band in addition to the one in the mmWave band
  Basically: No mmWave-only devices
Benefits from MLO:
  Discovery/association in lower band
  Scheduling from lower band: TWT schedules negotiated in lower band
    Use of TWT SPs on mmWave band will significantly help power consumption as almost no contention is needed: wake up for TWT SP only
  Broadcast exchanges in lower band
  Beamforming training with sector sweep done at 60 GHz, but sequence can be triggered or scheduled from lower band and feedback can be provided in lower band as well
  Seamless and fast fall back to lower band in case 60 GHz link breaks (and BF-training would need to be re-done)
    Make it resilient to blockage in mmWave band
In other words, all broadcasted exchanges, as well as all exchanges done prior to an established and successful beamforming training in the mmWave band, can be done in the lower band
September 2022

## Slide 9: How mmWave support would be different and simpler: comparing with 11ad/ay
 | IEEE Std-802.11ad/ay | mmWave as part of 11bX/UHR (this proposal)
Modem (PHY/MAC) | Requires development of a dedicated modem Control PHY SC PHY as primary modulation | Fully reuses lower band modem No need for a control PHY OFDM PHY (e.g., 11ac) as primary modulation
Management and control | Full control and management in mmWave Support for mmWave only devices | Build on MLO framework Exploit lower band for control and management No support for mmWave-only devices
Channelization | Base (smallest) channel bandwidth: 2.16 GHz Channel bonding up to 8.64 GHz | Build on lower band channelization Base (smallest) channel bandwidth could be 80/160/320 MHz
September 2022
Laurent Cariou, Intel

## Slide 10: Regulatory observations
The 60 GHz band is largely harmonized across the world
  802.18 has established an ad hoc group to look into regulatory challenges and opportunities in mmWave bands (45 and 60 GHz)
However, in addition to communication systems, there is a growing number of radar/sensing applications targeting the 60 GHz band [see here]
  On July 2021, the FCC issued an NPRM that aims to define regulatory rules for operation of radar systems in the 60 GHz band (see here)
  The same debate is taking place in many other countries around the world
The technologies being used for these sensing/radar systems are causing significant concerns in terms of coexistence with communication systems (see [1], [2]), because they don’t use LBT based protocols and can occupy the entire 60 GHz band
  These concerns were also discussed in the 802.11 Coex SC (see here)
It is essential that 802.11 takes a position in favor of mmWave support now in the mainstream program so that proper coex in the 60 GHz can be ensured
September 2022

## Slide 11: Conclusions
We see strong potential in including mmWave operation in UHR
Thanks to a mmWave PHY design reusing lower band design,
  we are simplifying the standard and implementation work and bringing complexity to levels that we believe are realistic for high-end Wi-Fi devices
Thanks to MLO framework,
  we can further reduce standard and implementation work, by avoiding the definition of a control PHY mode
  We provide important tools to help with power consumption and blockage issue in mmWave band
We want to get agreement early on regarding the scope of work in mmWave bands to define only what is necessary to enable basic operation
  Next slide provides thoughts about how to capture that in the PAR document
September 2022

## Slide 12: Impact on PAR and 5C documents
The following red text is an illustration of how to capture this in the PAR document
In 5.2.b. Scope of the project:
  This amendment defines standardized modifications to both the IEEE Std. 802.11 physical layers (PHY) and Medium Access Control Layer (MAC) that enables at least one mode of operation capable of improving throughput and worst-case latency and jitter with carrier frequency operation between 1 and 7.250 GHz and between 45 GHz and 71 GHz while ensuring backward compatibility and coexistence with legacy IEEE Std. 802.11 compliant devices operating in the 2.4 GHz, 5 GHz, and 6 GHz bands.
  This amendment defines at least one mode of operation capable of improved worst case latency and jitter.
In 8.1 Additional Explanatory Notes (Item Number and Explanation)
  Explanatory note for 5.2.b
  For mmWave bands, the focus of this amendment is on:
    Enabling single user OFDM modulation, with as little changes as possible from the modulation defined for 2.4/5/6 GHz bands, and for STAs that are affiliated with an MLD with at least one other STA operating in the 2.4/5/6 GHz band.
    Defining a simple analog beamforming training procedure
September 2022