## Slide 1: Sounding Rate Ceiling for WLAN Sensing
Date: 2022-09-14
Authors:
–
Name | Affiliations | Address | Email
Oscar Au | Origin Wireless Inc. | 7500 Greenway Center Drive, Suite 1070, Greenbelt, MD 20770 USA | oscar.au@originwirelessai.com
Beibei Wang |  |  | beibei.wang@originwirelessai.com
K.J. Ray Liu |  |  | 
Hung-Quoc Lai |  |  | 

## Slide 2: Current sounding frequency ceiling ~ 100Hz
In P.9 of 0977r8 entitled “CR for SBP Reporting”,
Figure 9-788edb—ISTA Availability Information field format
  The Count subfield in the ISTA Availability Information field indicates the size in bits of the Availability Bitmap subfield. The value of this subfield is denoted as “count”. …
  When used in sensing (see 11.21.18 (WLAN sensing procedure) and 11.21.19 (SBP procedure)), each Availability Bit in the Availability Bitmap subfield indicates the transmitting STA’s availability for SBP reporting and/or TB sensing measurement instance with the recipient STA. The value indicated by each bit in the Availability Bitmap is in units of 10 TUs.
  As 1 TU is 1024 micro-seconds, the maximum sounding frequency is ~100Hz (97.7Hz).
But there are many useful applications that need sounding frequency higher than 100Hz!

## Slide 3: Needs of sounding frequency > 100Hz
  Here are some publications [1-6] reporting that sounding frequency of 500Hz, 1000Hz, 1500Hz and 2000Hz are useful for some applications such as hand-writing recognition, fall detection, gait monitoring, and speed estimation.
  In [1], hand-writing recognition, sounding frequency = 500 Hz.
  In [2], fall detection, sound frequency =1500 Hz.
  In [3], gait monitoring, sounding frequency = 1500 Hz.
  In [4], speed estimation, sounding frequency = 1500 Hz.
  In [5], sounding frequency = 2000 Hz.
  In [6], sounding frequency =1500 Hz.

## Slide 4: Challenges of sounding frequency > 100Hz
  If sounding frequency is too high, it may take too much data bandwidth to report the CSI over the air to the sensing initiator and/or SBP initiator.
    This is not an issue if CSI is (optionally) not reported.
  The “Availability Bitmap” may take too many bits to transmit.
    Size of Availability Bitmap is controlled by the “count”.

## Slide 5: Discussion: some >100Hz possibilities
Step (A): Use a reserved bit in B9-15 to indicate two possible time units. E.g. “1” = 10 TU (current value) and “0” = alternate time unit (TBD).
  Perhaps 0.1 TU (for 10000Hz sounding) or 1 TU (for 1000Hz) for alternate time unit.
Some >100Hz options:
Do (A) only when CSI is not reported. No alternate time unit when CSI is reported.
Do (A) whether CSI is reported or not, with same alternate time unit.
Do (A) with two alternate time units: a first alternate time unit (e.g. 1 TU) when CSI is reported, and a second alternate time unit (e.g. 0.1 TU) when CSI is not report.

## Slide 6: Straw Poll 1
Do you agree that 11bf should support sounding frequency higher than 100Hz?
Yes
No
Abstain

## Slide 7: Straw Poll 2
To achieve >100Hz sounding frequency, do you prefer
Option 1 (do (A) only when CSI not reported, one alternate time unit)
Option 2 (do (A) whether CSI reported or not, one alternate time unit)
Option 3 (do (A) whether CSI reported or not, two alternate time units)
Abstain

## Slide 8: References
J. Zhang, Y. Li, et.al., “HandGest: Hierarchical Sensing for Robust in-the-air Handwriting Recognition with Commodity WiFi Devices”, to appear in IEEE Internet of Things Journal.
Y. Hu, F. Zhang, et.al., “DeFall: Environment-Independent Passive Fall Detection using WiFi”, IEEE Internet of Things Journal, Vol. 9, No. 11, pp. 8515-8530, Jun 2022.
C. Wu, F. Zhang, et.al., “Gaitway: Monitoring and Recognizing Gait Speed Through the Walls”, IEEE Trans. On Mobile Computing, Vol. 20, No. 6, pp. 2186-2199, Jun 2021.
F. Zhang, C. Chen, et.al., “WiSpeed: A Statistical Electromagnetic Approach for Device-Free Indoor Speed Estimation”, IEEE Internet of Things Journal, Vol.5, No.3, pp. 2163-2177, Jun 2018.
Y. Li, Dan Wu, et.al., “DiverSense: Maximizing Wi-Fi Sensing Range Leveraging Signal Diversity”, Proc. ACM Interact. Mob. Wearable Ubiquitous Tech., Vol. 6, No. 2, pp. 94.1-94.28, Jun 2022.
X. Wang, K. Niu, et.al., “Placement Matters: Understanding the Effects of Device Placement for WiFi Sensing”, Proc. ACM Interact. Mob. Wearable Ubiquitous Tech., Vol. 6, No. 1, pp. 32.1-32.25, Mar 2022.