## Slide 1: non-AP STA Device ID Implementation
Date: 2022-09-15
Authors:

## Slide 2: Abstract
This presentation is an attempt to discuss the aspect of how a non-AP STA and an AP will determine and signal Device ID Activation and usage.
We need to find a way to move forward on specifying how this works, and stop discussing higher layer issues.

## Slide 3: Versions
Rev 0 – Initial
Rev 1 – Text Updates and Straw Poll Results

## Slide 4: Option 1 – non-AP STA Always Indicates Device ID Activated (dot11DeviceIDEnabled = 1)
Non-AP STA doesn’t want to utilize Device ID for an ESS
  Non-AP STA never provides an identifier
  Non-AP STA drops any identifier provide by the AP
  AP will provide an Identifier to the non-AP STA
Pros
  Easy for the non-AP STA – is the default action to not support per SSID
  Non-AP STA can decide at upper layers what to do
Cons
  Forces AP to generate ID when it won’t be used.
  Additional useless packet exchanges

## Slide 5: Option 1 – non-AP STA Always Indicates Device ID Activated (dot11DeviceIDEnabled = 1)
Non-AP STA wants to utilize Device ID for an ESS
  Non-AP STA provides an identifier if it has one
  Non-AP STA utilizes latest identifier provided by the AP
  AP will provide an Identifier to the non-AP STA as needed
Pros
  Easy for the non-AP STA
  Non-AP STA can decide at upper layers what to do
Cons
  Requires per SSID configuration by the user to use Identifier

## Slide 6: Option 2 – non-AP STA Indicates Device ID Activated per AP per ESS
Non-AP STA wants to utilize Device ID for an ESS
  dot11DeviceIDActivated changes based on the SSID
  Non-AP STA optionally provides an identifier if it has one
  Non-AP STA utilizes latest identifier provided by the
  AP will provide an Identifier to the non-AP STA as needed
Pros
  No extraneous Packets are exchanged if no desire for Device ID
  Default action if not configured for use.
Cons
  Requires per SSID Configuration by the user to enable.

## Slide 7: Option 3 – non-AP STA Never Indicates Device D Activated
Non-AP STA May ask for an ID
  Non-AP STA provides a NULL identifier if it wants an AP generated identifier
  AP provides an identifier ONLY if it receives a NULL identifier from the non-AP STA or wants to update the identifier
  Non-AP STA will update its identifier if a new one is provided by the AP
  STA will optionally provide an identifier if it has one
Pros
  Contents of Identifier from non-AP STA controls exchanges per SSID
  No extraneous Packets are exchanged if no desire for Device ID
Cons
  Requires per SSID Configuration by the user.

## Slide 8: Straw Poll
I support the following Option to control Device ID
Option1 – non-AP STA always indicates Device ID is active and controls at the higher layers whether to store and utilize the ID
Option 2 – non AP indicates Device ID is active on a per ESS basis
Option 3 – Non-AP STA never indicates Device ID is active and utilizes the passing of an identifier to indicate support.
Chicago Style, Option 1 – 5, Option 2 --17, Option 3 –14, NA 6
Final is Option 2 --19, Option 3 --9

## Slide 9: References