## Slide 1: MIMO interference suppression for enhanced reliability
Date: 2022-09-20
Authors:

## Slide 2: Introduction (1/2)
A key objective for features proposed in UHR SG is to improve the STA’s quality of service (QoS) which requires an increase the uplink (UL) reliability [1-4]
Increasing the number of spatial streams (SS) has been considered as a side feature in UHR SG [1,2]. However APs with large number of antennas can increase the UL reliability, as it is shown in this presentation

## Slide 3: Introduction (2/2)
WLAN spectrum is subject to unpredictable interference
  Non-cooperative OBSS
  Other technologies (UWB, Bluetooth, NR-U)
MIMO equalization can supress interference to increase reliability
  Need covariance matrix of interference channel
  Highly beneficial in the context of 16 SS
    Support of more SS can be used to increase reliability not just throughput
802.11be agreed to increase maximum number of LTFs beyond NSS [5,6]
  More LTFs are already available and can be used for extended training signals
  Extended training signals can enable
    Interference covariance matrix estimation
    Continuous observation of the channel

## Slide 4: MIMO equalization to suppress interference
Spatial directions spanned by desired channels are different from those spanned by interference
  Receiver can use estimates of interference covariance matrix to suppress interference
Spatial directions of channel estimates
Spatial directions of interference channel
Best ideal case
(orthogonal spaces)
Worst case
(parallel spaces)
practical case
(different spaces)
e.g., Many RX antennas and rich scattering
e.g., several RX antennas and some scattering
e.g., Few RX antennas, no scattering, and highly correlated channels

## Slide 5: MIMO equalization (1/2)
Received signal at one given subcarrier of one OFDM symbol
  Assumptions for unpredictable interference
    Unsynchronized to received PPDU
      is asynchronous to and considered to be random and unknown
    Covariance matrix of does not change within PPDU
Intended TX channel
Unpredictable Interference
Intended TX signal
Noise
NR-U dev.
RX
AP
Intended TX
STA
Accurate estimate from LTFs
Rough interference covariance matrix estimate
NR-U dev.

## Slide 6: MIMO equalization (2/2)
MIMO equalization to suppress interference
  is MMSE receiver with additional term based on estimated interference covariance matrix ()
  can be estimated, e.g., from unused rows of P matrix
Regularization terms
Intended TX channel estimates
Estimated interference covariance matrix
Recovered signal after MIMO equalization
NR-U dev.
RX
AP
Intended TX
STA
Accurate estimate from LTFs
Rough interference covariance matrix estimate
: Hermitian transpose
NR-U dev.

## Slide 7: Simulation results (1/2) Need more LTFs and RX antennas than spatial streams
Intended transmitter STA
  TB-PPDU with MCS 4
  Number of Spatial streams = 2
  NLTF = 2
  NLTF = 4
    IntSup: Interference Suppression
Interfering STA: legacy (unsynchronized)
  SNR = 3dB
Receiver AP with Nr. RX antennas = 4
IntSup gain over MMSE having same NLTF: ~2dB
IntSup gain over MMSE: ~3.5dB
IntSup having NLTF = 2 NSS
MMSE having NLTF = NSS

## Slide 8: Simulation results (2/2) Need more LTFs and RX antennas than spatial streams
Intended transmitter STA
  TB-PPDU with MCS 4
  Number of Spatial streams = 2
  NLTF = 2
  NLTF = 6
    IntSup: Interference Suppression
Interfering STA: legacy (unsynchronized)
  SNR = 3dB
Receiver AP with Nr. RX antennas = 6
IntSup gain over MMSE having same NLTF: ~3.5dB
IntSup gain over MMSE: ~5.5dB
IntSup having NLTF = 3 NSS
MMSE having NLTF = NSS

## Slide 9: What changes are needed in the specification
Support of more SS
  More SS can be used to increase uplink reliability
  More SS requires more LTFs
    Unused rows of P matrix can be used to suppress uncontrollable interference
  May need to modify LTFs to avoid high overhead
Support of extended training signals
  Requires LTFs to at least match number of Rx antennas for effective interference suppression
  Select NLTF independently from NSS for all PPDU types
  Define additional P matrices with larger sizes
  Define training fields that can track time-varying interference within a PPDU

## Slide 10: Conclusion
MIMO equalization with extended training signals can supress unpredictable interference at the receiver AP to increase UL reliability
  Extended training signals are supported by more LTFs
  Extended training signals can be further developed to enable continuous channel observation
  More benefits can be expected in context of 16 SS
    16 SS can not only boost throughput but also increase reliability against interference such as
      OBSS
      Non-WLAN interference ,i.e., NR-U, UWB…

## Slide 11: SP
Do you agree that interference suppression via MIMO is a promising technology for UHR?
  Yes, while keeping a maximum of 8 SS
  Yes, while adding more SS
  No
  Abstain

## Slide 12: References
[1] 11-22-1566-00-0uhr-views-on-uhr
[2] 11-22-1580-01-0uhr-aperspectiveonproposeduhrfeaturesforenterpriseusecases
[3] 11-22-1392-00-0uhr-beamforming-improvement-for-uhr
[4] 11-22-1530-00-0uhr-multi-ap-coordination-for-next-generation-wi-fi
[5] 11-20-1375-03-00be-eht-nltf-design
[6] 11-21-1579-05-00be-cc36-cr-on-clause-9-4-2-295c