## Slide 1: TG bh Discussion Contribution on MAAD and all that goes with it
Date: 2022-09
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Statement
Why do I feel that I need to go through all this again? Nothing in this presentation is new, it has all been presented before.
BUT
Presenting in Telecons has proved to be ineffective and frustrating as when making a presentation at Interim or Plenary, back come the original negative comments that have been covered in detail in presentations made in the Telecons.
I realize that this has become controversial subject, but I feel that if the pre-schemes are understood and looked at fully, there is no reasonable reason not to allow at least one of them to be used.
This presentation is meant to be presented at face-to-face, acting as a tutorial, and if presented in telecon, I reserve right to present again in Plenary/Interim before going to the Motions as proposed in 22/1584.

## Slide 3: Purpose of this presentation
Describe MAAD
  Still not sure that it is understood by all.
Co-existence with “Device ID”
How “pre-schemes” use Probes
Privacy
Spoof AP mitigation
Pre-association Use Cases
IRMA
Conclusions
  Understand all above so as to be able to look at 22/1584

## Slide 4: Introduction – 1
MAAD is very simple, requires no computations or calculations
MAAD satisfies all Use Cases as it uses the MAC address as the identifier, but this is only known by the AP.
This Outline’s objective is to try to make it clear that MAAD MAC scheme is simple, secure, and an apt solution for TGbh.
It supports privacy equal to RCM
MAAD supports a suggested scheme to overcome spoof AP

## Slide 5
BASICS:
MAAD MAC Both STA and AP advertise support
AP assigns a new MAAD MAC address at every RSN association
  AP can assign one, two, or more addresses
STA uses that NEW allocated address the NEXT time it associates
  New MAC Address EVERY Association
  Can use same or alternative addresses for probes, if it wants to be identified
  Cannot be followed, address is renewed
AP recognizes STA pre-association
  AP “knows” the MAC Address
Reassociation uses MAC address used for the association
  Must, that’s the rule
STA can use ANQP and pre-association “as usual”
  the MAC address is known/recognized by the AP.

## Slide 6: Outline
AP and STA show support for MAAD in Extended Capabilities
STA associates first time using 4 W HS
A MAAD MAC Address(es) sent by AP in EAPOL-Key msg 3/4
  AP and STA store the allocated MAAD MAC for that STA/AP
When STA comes back it uses that previously allocated MAAD MAC Address as TA
AP instantly recognizes the STA from TA in Association Request etc.
  AP can identify the STA pre-association – ANQP and directed probes
STA Associates using an allocated MAAD MAC as TA
At association, AP provides new MAAD MAC address(es) in EAPOL-Key msg 3/4
  New MAC Address used for the NEXT association.
NOTES
For FILS new MAAD MAC address(es) received in Association Response frame

## Slide 7: Co-existence with Device ID (see 22/0908r1)
AP and STA advertise support for Device ID and MAAD
AP decides to use NGID only
  STA associates
  AP sends NGID KDE in msg 3
  STA logs the ID and sends it in msg 4 on subsequent associations
AP decides to use MAAD only
  STA associates
  AP sends MAAD KDE in msg 3
  STA logs the MAAD MAC and uses it on subsequent associations
AP decides to use both, NGID AND MAAD
  STA associates
  AP sends NGID KDE and MAAD KDE in msg 3
  STA next associates using the MAAD MAC and sends ID in msg 2 or 4 and AP sends new MAAD MAC in msg 3.
  Completely compatible no selection mechanism required

## Slide 8: Probes - Active Broadcast (see 22/0955r0)
Active Broadcast
  Looking for networks in range.
  No reason why STA should use the identifiable address, would use an RMA (random MAC address)
  STA may use broadcast probes to find a network
    STA is ill-advised to use an identifiable address in a broadcast probe – no requirement to do so, anyhow, and why would it?

## Slide 9: Active Directed Probes
  Directed probes are discouraged
    Trackable irrespective of the MAC Address used
      Even if using RCM , Device ID, MAAD etc.
  Looking for a specific AP/network? Use broadcast probe (see previous slide)
  Is there ever any reason to use an identifiable TA in a broadcast Probe?
    Yes, if STA knows it is in vicinity of the network, then probing with identifiable TA is OK, i.e., Probes used for steering (next slide)
  See later “Spoof AP”

## Slide 10: Probing in vicinity of Network
  If in the vicinity of the network*, then is it trackable?
    Determined by Passive or active (with RMA) scanning, or directed by network for steering purposes
  If STA probes with same address as it Associates with – there is no problem?
    All listener knows is that a STA probed and associated – so what?
    Listener will NEVER see that address AGAIN in that area, AND
    Listener will NEVER see that address AGAIN if monitoring a large area. (If it did, it is highly probable it is a different STA anyway).
The allocated random MAC address contains no identity to STA
For non-steering purposes, could use a second identifiable address
  Allocate 2 MAAD MACs, use one for associating and other for probes
*

## Slide 11: Privacy (see 22/1230r0)
RCM prevents passive monitoring of probes.
Same if MAAD is used.
MAAD or other pre-schemes do not decrease privacy
  As explained in previous slides, with all “pre-schemes”, probes use random MAC address (RMA) unless need to be identified (e.g., steering).
  Using ‘allocated address’ while in range of wanted AP/BSS is not a problem (address is a “one-time address”).
    Must use same TA across ESS.
Note: Association to same AP/BSS always with same address (one interpretation of 11aq) is sort of ‘trackable’ in that it is known that STA has been there before.
“Pre-schemes” all use one-time addresses, so this scenario is solved. Listener cannot know it is the same STA returning.

## Slide 12: Privacy - Spoofing
Scenario - Dastardly organization sets up APs spoofing a target’s “home” network.
STA comes in range and automatically attempts to associate (fails).
Even using RCM, the mere fact the STA tried to associate ‘identifies’ it as a member of that home network. And can still be tracked simply by attempting to associate.
With MAAD, using two or more addresses may help but still same problem as RCM.
MAAD or any pre-scheme does not decrease privacy

## Slide 13: How to stop the STA from sending Association Request to a spoof? (See 22/1411r0)
Location based – Use GPS to record location of “Home AP”
  Not an 802.11 solution
SSID Profile – Take an SSID profile of the “Home AP” and use this to verify the AP
  Could be an 802.11 solution but probably proprietary
  Very difficult to fake, (need to transmit a range of known SSIDs but mere presence of new SSIDs would defeat this)
  Needs to account for updates and an algorithm would be out-of-scope.
Identifiable Beacon – Add a Beacon protection key and include hash in beacon.
  Definitely an 802.11 solution,
  Can only be defeated by near real-time relay of the beacons
Allocated MAC Address, ID and wildcard probe
  Definitely an 802.11 solution using Identifiable MAC address
Take away? Spoof AP can be countered, not a reason to state that pre-schemes lessen privacy

## Slide 14: “Allocated Address and ID and Broadcast Probe” Basic scheme
Each time STA associates with the “home” network, it is allocated an address AND an ID
  MAAD element includes MAAD MAC address(es) and an ID.
  Could use Device ID (but probably not)
IF STA ‘sees’ the home network, (passive)
Before sending Association Request STA sends a broadcast probe using an allocated MAC Address.
The real AP identifies the STA and sends a Probe response including the correct ID.
STA checks the ID and will then associate and then receives a NEW Address and ID.
“Spoof AP” does not know this STA address from any other and will not respond with the correct ID
  In practice, there won’t be a spoof AP because it won’t work.

## Slide 15: AP Spoof Mitigation
The broadcast probe AP identity scheme requires that the Address is identifiable.
Allocating two MAAD MAC addresses might be beneficial in that the STA uses the second one for the broadcast probe and the first for Association.

## Slide 16: Clone Address
Scenario: Attacker notes the MAC address and uses it to gain access.
Assumption: “Home” network is using access control based on MAC Address.
Discussion:
When does the attacker hear the Address and know who it is?
  STA does not use the address unless in the vicinity of the ‘home’ network. Probes do not use it (if they did, how does attacker know who it is? Address is changed every association.
  Attacker hears STA associating (and somehow makes it fail?)
  Using spoof AP may provide the address (see previous)
How does attacker use it?
  Address is used as first line of defense; attacker needs the key to actually associate.
  What is the gain? DOS? (easier ways to do that).
Pre-association Access Control not possible with RMA or Device ID.

## Slide 17: Spoof and Clone
Are these really privacy concerns made worse if a pre-scheme is used?
NO
  Access Control uses address as the first line, second line is the security.
  If pre-scheme not used, then the Access Control or pre-association steering not covered

## Slide 18: Pre-Association Use Cases (see 22/1230r0)
4.1 Pre-Association Steering
“The user brings a phone within range of a multiple-AP infrastructure. Before connecting to the 802.11 network, the phone scans to discover the available APs, by sending Probe Requests.”
  STA recognizes SSID (ESS), sends probe(s)
  Probe Responses only from APs ‘interested’.
4.2 Home Control
AP simply has a list of known MAC Addresses
AP can also have a list of known “blocked” MAC Addresses.
Obviously does not work if RCM
MAAD works pre-detection
  Stored MAC address in the new one issued at the prior association
4.9&4.10 Steering – Allowed/disallowed, Managed buildings
ability to identify STA from the Association Request can be used for steering, allowance, speed etc.

## Slide 19: Summary
Details in this presentation may also be used to support IRM and RRCM
  MAAD and IRM are very simple, no computations required
    Can allocate 1, 2 or more address allocations plus an ID
  RRCM has minimal computations
    Ability to allocate numerous addresses
Address ALL Use Cases including those requiring identification before Association
Can be used to mitigate spoof AP

## Slide 20: But Wait – there’s more – IRMA (see 21/1626r0)
IRMA
(STA or) AP sends IRM Key in each association (in 4-way HS msg (2 or) 3
In next association, or probes (if STA wants to be identified) STA uses a random TA plus a hash (in Association Request).
AP matches TA (IRMA) and hash to key to identify the STA.
  New key IRMK is allocated every association
  IRM Hash = function {IRMA, IRMK, “time”}
  An IRMK Check can be used to reduce the list of keys that AP checks by a factor of 256.

## Slide 21: IRM element
STA indicates “private”, “unknown” or “known” in IRM element sent in Association Request
AP then what to do, i.e., look up key or not.
  IRM Hash = function {IRMA, IRMK, “time”}
To prevent copying and re-using address and IRM hash, need a time-based variable known to both STA and AP.
This is not easy, both AP and STA need to know it.
  If AP advertises a time changing element ,e.g., BPPN incremented every X beacons
  Then real time relay of the beacon will defeat it.
  If STA advertises the “nonce” then again simple cloning.
  If using real time, need to be synchronized.
Best defense is to have a mechanism to stop STA form sending Association Requests to a spoof AP
AND if we have this then the simpler MAAD scheme is fine.
REMEMBER Cloning the address does not give network access.

## Slide 22: Conclusions
Using a ‘simple” pre-scheme does not decrease privacy AND covers all Use Cases.
There is no reason why a pre-scheme should not be included in TGbh
They make TGbh more complete and providing choices
They comply with Use Cases not met by Device ID
  Access Control and pre-association steering
They do not decrease privacy
  Spoof and clone do not allow access
May be used to prevent Association Request to a Spoof.
All schemes can co-exist and be described clearly in the Amendment
HAVING UNDERSTOOD THIS PRESENTATION, THEN WE CAN (AGAIN) GO TO 22/1584r1