## Slide 1: TG bh Discussion Contribution on MAAD and all that goes with it
Date: 2022-09
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Statement
Why do I feel that I need to go through all this again? Nothing in this presentation is new, it has all been presented before.
BUT
Presenting in Telecons has proved to be ineffective and frustrating as when making a presentation at Interim or Plenary, back come the original negative comments that have been covered in detail in presentations made in the Telecons, which maybe the objector has not seen or understood.
I realize that this has become controversial subject, but I feel that if the pre-schemes are understood and looked at fully, there is no reasonable reason not to allow at least one of them to be included.
I have covered every reasonable objection and comment made against using a pre-scheme.
This presentation is meant to be presented at face-to-face, acting as a tutorial, and if presented in telecon, I reserve right to present again in Plenary/Interim before going to the Motions as proposed in 22/1584.

## Slide 3: Outline of this presentation
Describe MAAD (one of the “pre-schemes”)
  Still not sure that it is understood by all.
Co-existence with “Device ID”
How “pre-schemes” use Probes
Privacy
Spoof AP mitigation
Clone address
Pre-association Use Cases
IRMA
Conclusions
  Understand all above so as to be able to return to 22/1584

## Slide 4: Introduction
This MAAD outline’s objective is to try to make it clear that MAAD MAC scheme is simple, secure, and an apt solution for TGbh.
It supports privacy equal to RCM but adds support for pre-association use cases
MAAD also supports a scheme to overcome spoof AP
MAAD Text (for D0.2) is in 22/0427r7

## Slide 5
MAAD (MAC Address Designation)) BASICS:
Both STA and AP advertise support
AP assigns new MAAD MAC addresses at every RSN association
    #1 is for association only, #2 is for any probes (when STA wants to be identified)
STA uses that NEW allocated address #1 the NEXT time it associates
Use address #2 for steering, directed, broadcast probes, if it wants to be identified
AP recognizes STA pre-association
  AP “knows” the MAC Addresses
Reassociation uses MAC address #1 used for the association
  Must, that’s the rule
STA can use ANQP and pre-association “as usual”
  the MAC address is known/recognized by the AP.

## Slide 6: MAAD Details Outline
AP and STA show support for MAAD in Extended Capabilities
STA associates first time using 4 W HS
MAAD MAC Addresses sent by AP in EAPOL-Key msg 3/4
  AP and STA store the allocated MAAD MAC for that STA/AP
When STA comes back it uses last allocated MAAD MAC Address as TA
AP instantly recognizes the STA from TA (Address #1) in Association Request etc.
  AP can identify the STA pre-association – ANQP and directed probes
STA Associates using an allocated MAAD MAC #1 as TA
At association, AP provides new MAAD MAC addresses in EAPOL-Key msg 3/4
  New MAC Address used for the NEXT association.
NOTES
For FILS new MAAD MAC addresses received in Association Response frame
New Addresses constantly allocated.

## Slide 7: Co-existence with Device ID (see 22/0908r1)
AP and STA advertise support for Device ID and MAAD
AP decides to use Device ID only
  STA associates
  AP sends NGID KDE in msg 3
  STA logs the ID and sends it in msg 4 on subsequent associations
AP decides to use MAAD only
  STA associates
  AP sends MAAD KDE in msg 3
  STA logs the MAAD MAC and uses it on subsequent associations
AP decides to use both, NGID AND MAAD
  STA associates
  AP sends NGID KDE and MAAD KDE in msg 3
  STA next associates using the MAAD MAC and sends ID in msg 2 or 4 and AP sends new MAAD MAC in msg 3.
  Completely compatible no selection mechanism required

## Slide 8: Probes - Active Broadcast (see 22/0955r0)
Active Broadcast Probes
  Looking for networks in range.
  In general STA should use an RMA (random MAC address)
  STA may use broadcast probes to find a network
    May use address #2 if it wants to be identified i.e., knows it is in vicinity of the wanted SSID (discussed later)

## Slide 9: Active Directed Probes
  Directed probes are discouraged
    Indicates ‘interest’ in that AP irrespective of the MAC Address used
      Even if using RCM , Device ID, MAAD etc.
  Looking for a specific AP/network? Use broadcast probe (see previous slide)
    Use Address #2
  Is there ever any reason to use an identifiable TA in a broadcast Probe?
    Yes, if STA knows it is in vicinity of the network, then probing with identifiable TA is OK, e.g., Probes used for steering (next slide)
  Use address #2 to avoid detection. See later “Spoof AP”

## Slide 10: Probing in vicinity of Network
  If in the vicinity of the network, then no problem?
    Determined by Passive or active (with RMA) scanning, or directed by network for steering purposes
      Use Address #2 for probes, Address #1 for association
  If STA probes with different address as it Associates with – there is no problem?
    All listener knows is that one STA probed, and ‘another’ associated – so what?
    Listener will NEVER see those addresses AGAIN in that area, AND
    Listener will NEVER see those addresses AGAIN if monitoring a large area. (If it did, it is highly probable it is a different STA anyway).
The allocated random MAC addresses contains no identity to STA

## Slide 11: Privacy (see 22/1230r0)
RCM prevents passive monitoring of probes across areas
MAAD also uses RMA for probes.
MAAD or other pre-schemes do not decrease privacy
  As explained in previous slides, with all “pre-schemes”, probes use random MAC address (RMA) unless need to be identified (e.g., steering), but then will use address #2.
    Allows the steering use case
    Must use same TA across ESS.
Note: Association to same AP/BSS always with same address (one interpretation of 11aq) is sort of ‘trackable’ in that it is known that STA has been there before. MAAD is a big improvement on that.
“Pre-schemes” all use one-time addresses, so this scenario is solved. Listener cannot know it is the same STA returning.

## Slide 12: Privacy - Spoofing
Scenario - Dastardly organization sets up APs spoofing a target’s “home” network.
STA comes in range and automatically attempts to associate (fails).
Even using RCM, the mere fact the STA tried to associate ‘identifies’ it as a member of that home network. And can still be tracked simply by attempting to associate or sending directed probe.
Not solved by RCM
ONLY protection is that a STA determines that the AP is the ‘real deal’ before attempting to associate.

## Slide 13: How to stop the STA from sending Association Request to a spoof? (See 22/1411)
Location based – Use GPS to record location of “Home AP”
  Not an 802.11 solution
SSID Profile – Take an SSID profile of the “Home AP” and use this to verify the AP
  Could be an 802.11 solution but probably proprietary
  Very difficult to fake, (need to transmit a range of known SSIDs but mere presence of new SSIDs would defeat this)
  Needs to account for updates and an algorithm would be out-of-scope - not as easy as it seems
Identifiable Beacon – Add a Beacon protection key and include hash in beacon.
  Definitely an 802.11 solution,
  Can defeated by near real-time relay and replay of the beacons
Allocated MAC Address, ID and wildcard probe (new)
  Definitely an 802.11 solution using Identifiable MAC address

## Slide 14: “Allocated Address and ID and Broadcast Probe” Basic scheme
Each time STA associates with the “home” network, it is allocated two addresses AND an ID
  Address #1 for Association ONLY, Address #2 for probes (if wants to be identified) or anything else.
  Note: ID could be Device ID (but probably not). 1 or 2 octets
IF STA ‘sees’ the home network SSID (passive or broadcast probes):
Before sending Association Request
STA sends a broadcast probe using allocated MAC Address #2.
The real AP identifies the STA and sends a Probe response including the correct ID.
STA checks the ID and will then associate using address #1 and then receives NEW Addresses and ID.
“Spoof AP” does not know this STA address from any other and can not respond with the correct ID or know who it is

## Slide 15: AP Spoof Mitigation
The broadcast probe AP identity scheme requires that the Address is identifiable.
MAAD MAC allocates two addresses to mitigate copying :
  Address #1 used only for association
  Address #2 used only when probing and ‘wants to be identified’
Home AP should include a “random ID” in every Probe response, using the actual ID when address #2 is identified.
  Prevents “relay” attack (see next slide)

## Slide 16: AAID Spoof defense
To overcome AAID:
Attacker needs to record every broadcast probe TA at target site,
Then relays every TA to an AP situated near the “home” and send broadcast probe to home AP using every TA.
Then note the ID returned per TA, and relay that back to target site AP,
Then either use ID in a probe response (there is a time delay) or wait to see if same TA used again for a probe*, and if so, send the ID recorded in 3) in probe response
Wait to see if that causes a STA to try to associate.
It will use different address to associate
Still do not know who it is.
Is this even a practical “attack”? Multitude of probes received, still does not know who it is.
*Easy for a STA to not send another broadcast probe if response from the spoof “home” SSID does not have the correct ID – time limit etc.
Bottom line - This means that using MAAD pre-scheme has more privacy than RMA AND does provide solution for pre-association Access Control use cases
Note: RCM did not ‘break’ this “spoof’ scenario, but also it did not solve it (spoof AP)
  Justification that a “pre-scheme” should be adopted

## Slide 17: Clone Address
Scenario: Attacker notes the MAC address (#1) and uses it to gain access.
Assumption: “Home” network is using access control based on MAC Address
Discussion:
When does the attacker hear the Address and know who it is?
  Using spoof AP can be defeated (see previous)
  Probes use address #2 if in vicinity,(attacker does not know who it is? Address is changed every association)
  Attacker hears STA trying to associate to actual ‘home’ SSID and somehow makes it fail?
How does attacker use it?
  Attacker hears the Association Request, blocks the response, then quickly tries itself, BUT why?
  Address is used as first line of defense; attacker still needs the key to actually associate.
  What is the gain? DOS? (easier ways to do that).
  Steering and access control cases still does not allow association, also they use Address #2
Remember - Pre-association Access Control not possible with RMA or Device ID.

## Slide 18: Spoof and Clone
Are these really privacy concerns made worse if a pre-scheme is used?
NO
Also, Spoof AP can be mitigated by using a pre-scheme with 2 addresses.

## Slide 19: (some) Pre-Association Use Cases (see 22/1230r0)
4.1 Pre-Association Steering
“The user brings a phone within range of a multiple-AP infrastructure. Before connecting to the 802.11 network, the phone scans to discover the available APs, by sending Probe Requests.”
  STA recognizes SSID (ESS), sends probe(s)
  Probe Responses only from APs ‘interested’.
4.2 Home Control
AP simply has a list of known MAC Addresses
AP can also have a list of known “blocked” MAC Addresses.
Obviously does not work if RCM
MAAD works pre-detection
  Stored MAC address in the new one issued at the prior association
4.9&4.10 Steering – Allowed/disallowed, Managed buildings
ability to identify STA from the Association Request can be used for steering, allowance, speed etc.
Bottom line – they do exist

## Slide 20: Summary
Details in this presentation may also be used to support IRM and RRCM
  MAAD and IRM are very simple, no computations required
    Can allocate 1, 2 or more address allocations plus an ID
  RRCM has minimal computations
    Ability to allocate numerous addresses
Pre-schemes address ALL Use Cases including those requiring identification before Association
Pre-schemes can be used to mitigate spoof AP
  Allocating two addresses can prevent spoofing.

## Slide 21: But Wait – there’s more – IRMA (see 21/1626r0)
It has been commented that an address scheme using a nonce should be used. A similar scheme proposed was
IRMA
(STA or) AP sends IRM Key in each association (in 4-way HS msg (2 or) 3
In next association, or probes (if STA wants to be identified) STA uses a random TA plus a hash (in Association Request).
AP matches TA (IRMA) and hash to key to identify the STA.
  New key IRMK is allocated every association
  IRM Hash = function {IRMA, IRMK, “time”}
  An IRMK Check can be used to reduce the list of keys that AP checks by a factor of 256.

## Slide 22: IRM element
STA indicates “private”, “unknown” or “known” in IRM element sent in Association Request
AP then what to do, i.e., look up key or not.
  IRM Hash = function {IRMA, IRMK, “time”}
To prevent copying and re-using address and IRM hash, needs a time-based variable known to both STA and AP.
This is not easy, both AP and STA need to know it.
  If AP advertises a time changing element ,e.g., BPPN incremented every X beacons
  then real-time relay of the beacon will defeat it.
  If STA advertises a “nonce” in addition to IRMA, then again simple cloning.
  If using a nonce based on “real time”, need to be synchronized.
Best defense is to have a mechanism to stop STA from sending Association Requests to a spoof AP
AND if we have this, then the simpler MAAD scheme is fine.
REMEMBER Cloning the address (even if possible) does not give network access

## Slide 23: Conclusions
Using a ‘simple” pre-scheme such as MAAD does not decrease privacy AND covers all Use Cases. Not a clear case that a more involved scheme such as IRMA is required.
This presentation has described how and why.
There is no reasonable reason why at least one pre-scheme should not be included in TGbh
Complies with Use Cases not met by Device ID
  Access Control and pre-association steering
Makes TGbh more complete and provide choices
Does not decrease privacy, in fact can improve it
  May be used to prevent Association Request to a Spoof?
  E.g., Broadcast probe with address #2
All schemes can co-exist and be described clearly in the Amendment
HAVING UNDERSTOOD THIS PRESENTATION, THEN WE CAN RETURN TO 22/1584r1